## Slide 1: Preamble Puncture Discussion in EHT PPDU
Date: 2020-07-27
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Recap
802.11be supports that U-SIG in each 80 MHz shall carry puncturing channel info for at least the specific 80 MHz where it is transmitted.
  Note: Within each 80 MHz segment, U-SIG is duplicated in every non-punctured 20 MHz.
  Whether BW/Puncturing info can be different for different 80 MHz is TBD.
  Whether BW and puncturing info in U-SIG are carried as a combined or a separate field is TBD.
  [Motion 111, #SP0611-10, [9] and [45]]
802.11be signaling in U-SIG for BW/puncturing information in every non-punctured 20 MHz of an 80 MHz segment shall allow even an OBSS or unassociated device to decode the puncturing pattern of at least the specific 80 MHz that contains the 20 MHz.
  [Motion 113, [9] and [46]]
802.11be supports BW field which does not include puncturing information.
  [Motion 112, #SP29, [9] and [46]]

## Slide 3: Preamble puncture discussion for OFDMA mode
For OFDMA mode (non-compressed mode), the STAs only need the preamble puncture info of the corresponding 80MHz in order to decode EHT-SIG.
Then in EHT-SIG, there exists the RU allocation subfields, which indicate the assigned RU/empty RUs across the whole bandwidth .
  It doesn’t matter if one 20MHz subchannel (non-EHT-modulated field) is punctured or not at this stage
Flexibility of preamble puncture in OFDMA mode needs detailed discussion.
  For non-OFDMA mode, there exists up to one hole across the whole bandwidth.

## Slide 4
For non-OFDMA mode (compressed mode), the STAs need the preamble puncture info across the whole bandwidth in order to decode the data part. Prefer to include preamble puncture info A field in U-SIG, and indicates the puncture info of the corresponding 80Mhz only.
  For consistency with OFDMA mode
Then in EHT-SIG, there exists preamble puncture info B subfield if needed, and indicates the puncture info across the whole bandwidth.
  When preamble puncture info B subfield exists and how to indicate need detailed discussion.
Preamble puncture discussion for non-OFDMA mode

## Slide 5: Preamble puncture indication in U-SIG
The following entries are included in preamble puncture indication in U-SIG:
Preamble puncture indication A field | Description in the corresponding 80MHz | Notes
0 | 1111, no puncture in the corresponding 80MHz, with puncturing in other 80MHz | Applied only when BW>80MHz, additional puncture info is needed
1 | X111 | No additional preamble puncture info needed even for non-OFDMA case
2 | 1X11 | 
3 | 11X1 | 
4 | 111X | 
5 | XX11 | 
6 | 11XX | 
7 | No puncture across the whole bandwidth | Applied to all BW No additional preamble puncture info needed even for non-OFDMA case

## Slide 6: Preamble puncture indication in U-SIG (OFDMA case)
The following entries are included in preamble puncture indication in U-SIG:
Preamble puncture indication A field | Description in the corresponding 80MHz | Notes
0 | 1212 | Follow style in 20-1259r0, “1”,”2” means two CCs
1 | X212 | 
2 | 1X12 | 
3 | 12X2 | 
4 | 121X | 
5 | XX12 | 
6 | 12XX | 
7 | 1XX2 | Proposed in 20-1259r0
8-16 | Reserved | TBD
Propose to have a table for OFDMA case too instead of a bitmap, no need to restrict which case is supported and which case is not. May use the same entry as part/all of the entries for non-OFDMA case.

## Slide 7: Preamble puncture indication in EHT-SIG
For non-OFDMA, when does preamble puncture indication B subfield exist and how to indicate have several options:
Options | When does preamble puncture indication B subfield exist | how to indicate in preamble puncture indication B subfield | Pro | Con
Opt1 | Exist except the case when preamble puncture indication A field in U-SIG indicates 7 (No puncture across the whole bandwidth) | Indicate preamble puncture info in the other one or three 80MHz segments except the corresponding 80MHz | Save overhead for some scenarios | Different puncture info/existence of puncture info in different 80MHz segments
Opt2 (preferred) | Exist except the case when preamble puncture indication A field in U-SIG indicates 7 (No puncture across the whole bandwidth) | Indicate preamble puncture info across the whole bandwidth | Same puncture info in different 80MHz segments | Overhead of preamble puncture info exists for most of the cases

## Slide 8: Preamble puncture indication in EHT-SIG
Following Opt2, for non-OFDMA, and when preamble puncture indication A field in U-SIG doesn’t indicate 7, there exist preamble puncture indication B subfield in EHT-SIG common. The contents of preamble puncture indication B subfield include:
Bandwidth (MHz) | Preamble puncture indication B | Description in the corresponding 80MHz | Aggregated Bandwidth
160 | 0 | X111 1111 | 996+(484+242), 140 MHz (8 options)
 | 1 | 1X11 1111 | 
 | 2 | 11X1 1111 | 
 | 3 | 111X 1111 | 
 | 4 | 1111 X111 | 
 | 5 | 1111 1X11 | 
 | 6 | 1111 11X1 | 
 | 7 | 1111 111X | 

## Slide 9: Preamble puncture indication in EHT-SIG
Following Opt2, for non-OFDMA, and when preamble puncture indication A field in U-SIG doesn’t indicate 7, there exist preamble puncture indication B subfield in EHT-SIG common. The contents of preamble puncture indication B subfield include:
Bandwidth (MHz) | Preamble puncture indication B | Description in the corresponding 80MHz | Aggregated Bandwidth
320 | 0 | XX11 1111 1111 1111 | 3*996+484, 280MHz (8 options)
 | 1 | 11XX 1111 1111 1111 | 
 | 2 | 1111 XX11 1111 1111 | 
 | 3 | 1111 11XX 1111 1111 | 
 | 4 | 1111 1111 XX11 1111 | 
 | 5 | 1111 1111 11XX 1111 | 
 | 6 | 1111 1111 1111 XX11 | 
 | 7 | 1111 1111 1111 11XX | 

## Slide 10: Preamble puncture indication in EHT-SIG
Following Opt2, for non-OFDMA, and when preamble puncture indication A field in U-SIG doesn’t indicate 7, there exist preamble puncture indication B subfield in EHT-SIG common. The contents of preamble puncture indication B subfield include:
Bandwidth (MHz) | Preamble puncture indication B | Description in the corresponding 80MHz | Aggregated Bandwidth
320 | 8 | XXXX 1111 1111 1111 | 3*996, 240MHz (4 options)
 | 9 | 1111 XXXX 1111 1111 | 
 | 10 | 1111 1111 XXXX 1111 | 
 | 11 | 1111 1111 1111 XXXX | 

## Slide 11: Preamble puncture indication in EHT-SIG
Following Opt2, for non-OFDMA, and when preamble puncture indication A field in U-SIG doesn’t indicate 7, there exist preamble puncture indication B subfield in EHT-SIG common. The contents of preamble puncture indication B subfield include:
Bandwidth (MHz) | Preamble puncture indication B | Description in the corresponding 80MHz | Aggregated Bandwidth (MHz)
320 | 12 | XXXX XX11 1111 1111 | 2*996+484, 200MHz 12 options
 | 13 | XXXX 11XX 1111 1111 | 
 | 14 | XXXX 1111 XX11 1111 | 
 | 15 | XXXX 1111 11XX 1111 | 
 | 16 | XXXX 1111 1111 XX11 | 
 | 17 | 1111 1111 11XX XXXX | 
 | 18 | XX11 1111 1111 XXXX | 
 | 19 | 11XX 1111 1111 XXXX | 
 | 20 | 1111 XX11 1111 XXXX | 
 | 21 | 1111 11XX 1111 XXXX | 
 | 22 | 1111 1111 XX11 XXXX | 
 | 23 | 1111 1111 11XX XXXX | 

## Slide 12: Preamble puncture discussion summary for non-OFDMA
A summary of non-OFDMA case, no preamble puncture indication part B subfield in EHT-SIG is needed for BW<=80MHz;
Following Opt2, no preamble puncture indication B subfield is needed when preamble puncture indication A field in U-SIG indicates 7 (No puncture across the whole bandwidth).
Following Opt2, 8 entries are needed for BW=160MHz; 24 entries are needed for BW=320MHz. In total, 32 entries are needed for all supported bandwidth.
So 5~6 bit is needed with a different table per BW; 5~6 bit is needed if a unified table regardless of 160/320Mhz BW.

## Slide 13: Preamble puncture flexibility for OFDMA
The next topic is about preamble puncture flexibility discussion. There are different options regarding flexibility for OFDMA transmission:
  Opt1: only one hole across the whole bandwidth, same as non-OFDMA case
  Opt2: supports up to one hole per 80MHz segments, if punctured, the puncture pattern of each segment shall be one of the following:X111
    X111
    1X11
    11X1
    111X
    XX11
    11XX
    1XX1 (newly added in r2)
Opt 2 is preferred, doesn’t add additional complexity to the STA side.

## Slide 14: Straw Poll #1
Do you agree to add the following text in the TGbe SFD:
  In U-SIG field of an EHT PPDU that is not an EHT TB PPDU, there exists a preamble puncture indication A field, which indicates the preamble puncture information of the corresponding 80MHz.

## Slide 15: Straw Poll #2
Do you agree to add the following text in the TGbe SFD:
  The preamble puncture indication A field includes the following indications:
Preamble puncture indication A | Description in the corresponding 80MHz
0 | 1111, no puncture in the corresponding 80MHz, with puncturing in other 80MHz
1 | X111
2 | 1X11
3 | 11X1
4 | 111X
5 | XX11
6 | 11XX
7 | No puncture across the whole bandwidth

## Slide 16: Straw Poll #2a
Do you agree to add the following text in the TGbe SFD:
  The preamble puncture indication field in U-SIG of an OFDMA transmission in an EHT MU PPDU includes the following indications:
Preamble puncture indication A field | Description in the corresponding 80MHz | Notes
0 | 1212 | Follow style in 20-1259r0, “1”,”2” means two CCs
1 | X212 | 
2 | 1X12 | 
3 | 12X2 | 
4 | 121X | 
5 | XX12 | 
6 | 12XX | 
7 | 1XX2 | Proposed in 20-1259r0
8-16 | Reserved | TBD

## Slide 17: Straw Poll #3
Do you agree to add the following text in the TGbe SFD:
  There exists no explicit preamble puncture indication subfield in EHT-SIG for an OFDMA transmission.
    Note: RU allocation subfields exist in the common field of EHT-SIG

## Slide 18: Straw Poll #4
Do you agree to add the following text in the TGbe SFD:
  There exists a preamble puncture indication B subfield in EHT-SIG for a non-OFDMA transmission except when preamble puncture indication A field in U-SIG indicates 7 (No puncture across the whole bandwidth).
  There exists no preamble puncture indication B subfield in EHT-SIG for a non-OFDMA transmission when preamble puncture indication A field in U-SIG indicates 7 (No puncture across the whole bandwidth).

## Slide 19: Straw Poll #5
Do you agree to add the following text in the TGbe SFD:
  Regarding preamble puncture flexibility for OFDMA, supports up to one hole per 80MHz segments. If punctured, the puncture pattern of each segment shall be one of the following:X111
    X212
    1X12
    12X1
    121X
    XX12
    12XX
    1XX2

## Slide 20: Straw Poll #6
Do you agree to add the following text in the TGbe SFD:
  The preamble puncture indication B subfield includes the indications as listed in slide 7 to 10.
    Note: different table for 160Mhz and 320MHz bandwidth

## Slide 21
https://mentor.ieee.org/802.11/dcn/20/11-20-0566-46-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx, Edward Au, Huawei
https://mentor.ieee.org/802.11/dcn/20/11-20-0285-05-00be-su-ppdu-sig-contents-considerations.pptx, Wook Bong Lee, Samsung
References