## Slide 1: Contention Window Value Management for STR MLD
Date: 2020-07-30
Authors:
Name | Affiliations | Address | Phone | email
Sanghyun Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0524 | shawn.kim@wilusgroup.com
Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 2: Introduction
802.11be supports the following cases in R1:
  STR AP MLD with STR non-AP MLD
  STR AP MLD with non-STR non-AP MLD
  Note: All the other cases are TBD.
To support the non-STR MLD, several sync operations of the STR MLD have been proposed
  Ending time alignments of PPDUs [1-4], synchronous channel access [5-8], sync RTS using MU-RTS [9]/padded RTS [10], slot boundary alignments of links, etc.
It is also important to ensure that the operation of the STR MLD does not suffer from the limited capability of the non-STR MLD
We propose collision-aware CW (Contention Window) value management for a STR MLD that utilizes collision-detection capability
  Note: The collision-detection capability of a STR MLD is ability to detect an intra-MLD collision within its peer non-STR MLD
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 3: Intra-MLD collision
Intra-MLD collision
  Decoding failure due to in-device interference of the non-STR MLD
    Example
      Receiving procedure of the STA1 of non-STR MLD may fail due to in-device interference caused by a transmission of the STA2 of the same non-STR MLD
      The AP1 of AP MLD started PPDU1 transmission before recognizing that the STA1 cannot receive (detect or decode) it from the intra-MLD collision
BUSY
Intra-MLD collision
Tx PPDU1 (to STA1)
Tx PPDU2 (to AP2)
Rx PPDU2
2
1
0
5
4
3
In-device interference
AP2
(6 GHz)
STA1
(5 GHz)
STA2
(6 GHz)
AP1
(5 GHz)
Tx
ACK
Rx
ACK
No ACK received (due to intra-MLD collision on the non-AP MLD)
SIFS
SIFS
SIFS
2
1
0
STR
AP
MLD
non-STR non-AP MLD
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 4: Problem statement
If a STA of a STR MLD should increase its CW value after transmission failure due to the intra-MLD collision of its receiving STA of a non-STR MLD, it is disadvantageous to the STA of the STR MLD compared to the neighbor single-link STAs
  Intra-MLD collision is unique problem of the MLD
There can be more scenarios where a transmission from a STA of a STR MLD fails due to the limited receiving capability of its intended receiver
  e.g., A STA of a multi-link single radio MLD cannot receive a frame when another STA of the same MLD starts transmission
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 5: CW value management
Proposal
  A STA of STR MLD does not increase its CW value when it recognizes that its transmission is failed due to intra-MLD collision of the receiving STA
  NOTE: In the baseline spec (10.3.1)
  “The CSMA/CA protocol is designed to reduce the collision probability between multiple STAs accessing a medium, at the point where collisions would most likely occur.”
July 2020
Sanghyun Kim (WILUS), et al.
Failed Tx due to intra-MLD collision
(to STA1)
Rx PPDU (from STA2)
2
1
0
AP2 (6 GHz)
AP1 (5 GHz)
Tx
ACK
SIFS
SIFS
4
3
Tx STA info
(non-STR relationship with STA1)
No ACK
2
1
0
STR
AP
MLD
Random()=
[0,CW]
Tx
Random()=
[0,(same) CW]

## Slide 6: Summary
We discussed intra-MLD collision scenario where a STA of a non-STR MLD cannot receive a PPDU due to the intra-MLD collision
We propose not to increase CW value of a STA of a STR MLD when it recognizes that its transmission is failed due to intra-MLD collision of the receiving STA of non-STR MLD
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 7: SP1
Do you agree to add the following in the SFD:
  A STA of a STR MLD that attempted unsuccessful transmission to a STA that is an intended receiver shall select a new random number using the current value of CW, if all of the following conditions are satisfied:
    The intended receiver is an affiliated STA with a non-STR MLD.
    While the STA of the STR MLD performing the transmission, another STA of the STR MLD receives a PPDU from another STA of the non-STR MLD.
  Y/N/A
July 2020
Sanghyun Kim (WILUS), et al.

## Slide 8: References
[1] 11-19/1305 Synchronous Multi-link Operation
[2] 11-20/0026 MLO: Sync PPDUs
[3] 11-20/0638 STR AP Sync. MLO Operation
[4] 11-20/0670 Synchronous Multi-link Operation Follow Up
[5] 11-19/1547 Multi-link Operation and Channel Access Discussion
[6] 11-19/1836 Multi-link Channel Access Follow-up
[7] 11-20/0469 Multi-link Channel Sensing
[8] 11-20/0487 Multiple Link Operation Follow Up
[9] 11-20/0577 RTS and CTS Procedure in Synchronous Multi-link Operation
[10] 11-20/0968 Multi-link RTS-CTS Operations with non-STR STA MLD
July 2020
Sanghyun Kim (WILUS), et al.