## Slide 1: 11be Spectral Mask
Date: 2020-08-01
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Youhan Kim |  |  |  | 
Bin Tian |  |  |  | 
Notes: September 2012

## Slide 2: Overview of 11ax Spectral Mask
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11ax 20 | 9.75 | 10.5 | 20 | 30
11ax 40 | 19.5 | 20.5 | 40 | 60
11ax 80 | 39.5 | 40.5 | 80 | 120
11ax 160 | 79.5 | 80.5 | 160 | 240
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11ax 20 |  |  |  | 
11ax 40 |  |  |  | 
11ax 80 |  |  |  | 
11ax 160 |  |  |  | 
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
9.75
10.5
20
30
-
9.75
-
10.5
-
20
-
30
Freq
[
MHz
]
Transmit Spectral Mask for HE 20 MHz PPDU
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
19.5
20.5
40
60
-
19.5
-
20.5
-
40
-
60
Freq
[
MHz
]
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
39.5
40.5
80
120
-
39.5
-
40.5
-
80
-
120
Freq
[
MHz
]
Transmit Spectral Mask for HE 80 MHz PPDU
Transmit Spectral Mask for HE 40 MHz PPDU
Transmit Spectral Mask for HE 160 MHz PPDU
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
79.5
80.5
160
240
-
79.5
-
80.5
-
160
-
240
Freq
[
MHz
]
Propose to leverage over for 11be, except for puncture mask
  11ax puncturing mask with 20dBr down at the puncture edge is too loose

## Slide 3: Spectral Mask for a EHT 320 MHz PPDU
Propose EHT 320MHz spectral mask has the skirt scaled to that of HE 160MHz and 1st rolloff identical to HE 40/80/160MHz
    320MHz tone plan has same number of guard tones ([12, 11]) as HE 40/80/160MHz
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
159.5
160.5
320
480
-
159.5
-
160.5
-
320
-
480
Freq
[
MHz
]
Spectral Mask for a EHT 320 MHz PPDU
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11be 320 | 159.5 | 160.5 | 320 | 480
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11be 320 |  |  |  | 

## Slide 4: Spectral Mask for EHT 240 MHz Transmission
Passed SP : 240Mhz transmission is defined as 320MHz PPDU with 80Mhz punctured
  320MHz mask + tightened puncturing mask is good to go

## Slide 5: Discussion on Puncturing Mask (ETSI (top) vs. 11ax (bottom) )
Edge puncture
Mid puncture>20MHz
Mid puncture=20MHz
Edge puncture
Mid puncture
 | 11ax | ETSI
RBW | 100KHz | 1MHz
1st slope transition | 0.5MHz | 1MHz
Mask floor | -20dBr | -28/-25/-23dBr

## Slide 6: Proposal on 11be Puncturing Mask
 | 11ax | ETSI | 11be
RBW | 100KHz | 1MHz | 100KHz
1st slope transition | 0.5MHz | 1MHz | 0.5MHz
Mask floor | -20dBr | -28/-25/-23dBr | -28/-25/-23dBr
Take RBW=100KHz to avoid smearing in measurement
  Same as 11ax
0.5MHz transition band at 1st slope, starting at the punctured band edge
  Same as 11ax
  Depends on the adoption of RBW=100kHz
  Less interference to adjacent band, as the guard band of 11ax/11be is < 1 MHz
Mask floor: Same as ETSI for lower ACI

## Slide 7: SP #1
Do you support the following mask for 320MHz transmission in EHT PPDU?
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
159.5
160.5
320
480
-
159.5
-
160.5
-
320
-
480
Freq
[
MHz
]
Spectral Mask for an EHT 320 MHz PPDU
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11be 320 | 159.5 | 160.5 | 320 | 480
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11be 320 |  |  |  | 

## Slide 8: SP #2
Do you support using a 100 kHz resolution bandwidth for 11be spectrum measurement?
  Same as 11ax

## Slide 9: SP #3
For 11be puncturing mask do you support using 0.5MHz transition band at the 1st slope from 0dBr to -20dBr, starting at the punctured band edge?
  [N*10, N*10+0.5] at the right edge of transmission band
  [N*10-0.5, N*10] at the left edge of transmision band
  Note: This is for EHT PPDU
  Note: Same as 11ax