## Slide 1: EHT Punctured NDP and Partial BW Feedback Tones
Date: 2020-08-25
Authors:
Name | Affiliations | Address | Phone | Email
Alice Chen | Qualcomm |  |  | alicel@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Cheng-Ming Chen |  |  |  | chec@qti.qualcomm.com
Chi-Lin Su |  |  |  | clsu@qti.qualcomm.com
Notes: September 2012

## Slide 2: Abstract
In this presentation, we would like to discuss changes to punctured NDP for sounding and CSI feedback in the following areas
  Punctured NDP for sounding
  CSI feedback request granularity
  Feedback tone set
  Partial BW CSI feedback tone indices table
Note that it has been agreed that the EHT80 OFDMA tone plan for RU<996 will be changed from the HE80 OFDMA tone plan to duplication of two HE40 SU/OFDMA tone plans
  This tone plan change may lead to some changes in the aforementioned areas, compared to 11ax

## Slide 3: Changes in r1
Changed the partial BW CSI feedback start/end tone indices table to feedback tone indices table for RU242 granularity (slide 11)
  Essentially same feedback tones for each RU242
Added feedback tone indices table for RU996 (slide 12) for easier presentation of rules of determining feedback tones (slide 13)
  Note that the feedback tone indices for RU996 (when the entire 80MHz segment is requested in feedback) remain the same as in r0, where we referred to them as feedback tones in each RU242 plus additional feedback tones (outside of RU242)
Changed SP4 to reflect the aforementioned changes

## Slide 4: Recap: HE80 Versus EHT80
EHT80 tone plan: DUPed HE40 for OFDMA + RU996 for SU
HE80 tone plan
HE80
12 Edge
12 Edge
12 Edge
12 Edge
13
13
13
13
13
13
13
13
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
7
DC
7
DC
7
DC
7
DC
12 Edge
996 usable tones +5 DC
26
26
26
26
26
26
26
2
52
52
52
52
26
242
106
106
1
2
1
1
2
1
2
1
1
2
2
1
1
26
26
26
26
2
52
52
26
26
26
26
26
26
52
52
52
52
26
242
106
106
1
2
1
1
2
1
1
2
1
1
1
26
26
26
26
26
1
2
1
26
26
26
26
26
26
26
2
52
52
52
52
26
242
106
106
1
2
1
1
2
1
2
1
1
2
2
1
1
26
26
26
26
2
52
52
26
26
26
26
26
26
52
52
52
52
26
242
106
106
1
2
1
1
2
1
1
2
1
1
1
26
26
26
26
26
1
2
1
484
484
12 Edge
13
13
7
DC
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
12 Edge
11 Edge
EHT80
12 Edge
12 Edge
12 Edge
12 Edge
23
DC
23
DC
23
DC
996 usable tones +5 DC
484 + 5
484+5
12 Edge
23
DC
5
DC
242
5
DC
242
242
242
23
DC
5
DC
5
DC
5
DC
26
26
26
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
26
26
26
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
5
DC
5
DC
5
DC
26
26
26
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
26
26
26
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1
106
26
52
26
1
1
26
52
26
1
2
1
2
1
1

## Slide 5: LTF in Punctured NDP: 80MHz
The non-punctured 80MHz NDP uses non-OFDMA tone plan, same as in 11ax
For punctured NDP, propose to use OFDMA tone plan for EHT-LTF for 80MHz PPDUs and each 80MHz segment within >80MHz PPDUs
  The populated LTF tones for 1x/2x/4x EHT-LTF are listed in the following table
  The cases with a 40MHz punctured are for each 80MHz segment within >80MHz PPDUs
 | RU & Tone Indices | 1x LTF Tones | 2x LTF Tones | 4x LTF Tones
Non-punctured | RU996, [-500:-3, 3:500] | A=[-500:4:-4, 4:4:+500] | A=[-500:2:-4, 4:2:500] | A=[-500:-3, 3:500]
1st 20MHz punctured | RU242+484, [-253:-12, 12:253, 259:500] | B1=[-252:4:-12, 12:4:252, 260:4:500] | B1=[-252:2:-12, 12:2:252, 260:2:500] | B1=[-253:-12, 12:253, 259:500]
2nd 20MHz punctured | RU242+484, [-500:-259, 12:253, 259:500] | B2=[-500:4:-260, 12:4:252, 260:4:500] | B2=[-500:2:-260, 12:2:252, 260:2:500] | B2=[-500:-259, 12:253, 259:500]
3rd 20MHz punctured | RU242+484, [-500:-259, -253:-12, 259:500] | B3=[-500:4:-260, -252:4:-12, 260:4:500] | B3=[-500:2:-260, -252:2:-12, 260:2:500] | B3=[-500:-259, -253:-12, 259:500]
4th 20MHz punctured | RU242+484, [-500:-259, -253:-12, 12:253] | B4=[-500:4:-260, -252:4:-12, 12:4:252] | B4=[-500:2:-260, -252:2:-12, 12:2:252] | B4=[-500:-259, -253:-12, 12:253]
1st 40MHz punctured | RU484, [12:253, 259:500] | C1=[12:4:252, 260:4:500] | C1=[12:2:252, 260:2:500] | C1=[12:253, 259:500]
2nd 40MHz punctured | RU484, [-500:-259, -253:-12] | C2=[-500:4:-260, -252:4:-12] | C2=[-500:2:-260, -252:2:-12] | C2=[-500:-259, -253:-12]

## Slide 6: LTF in Punctured NDP: >80MHz
For >80MHz PPDUs, different 80MHz segment may have different LTF populated tones, according to the puncturing pattern
  Example 1: For 160MHz, if the 1st 20MHz is punctured, the LTF populated tones are [B1 - 512, A + 512]
  Example 2: For 160MHz, if the 3rd 40MHz is punctured, the LTF populated tones are [A - 512, C1 + 512]
  Example 3: For 320MHz, if the 2nd 80MHz is punctured, the LTF populated tones are [A - 1536, A + 512, A + 1536]
  Example 4: For 320MHz, if the last 40MHz is punctured, the LTF populated tones are [A - 1536, A - 512, A + 512, C2 + 1536]
  Example 5: For 240MHz transmission, if the 4th 40MHz within the contiguous 240MHz is punctured, the LTF populated tones are [A - 1536, C2 - 512, A + 512] or [A - 512, C2 + 512, A + 1536]

## Slide 7: CSI Feedback Request Granularity
11ax partial BW CSI feedback with RU26 granularity seems to be over-designed
  Flexibility allowed by 11ax cannot be realistically utilized by AP (e.g., RU allocated to a STA may vary in size across PPDUs).
  Increased complexity for STAs to support this feature, making it unappealing
  In practice, AP is more likely to request feedback with larger granularity, e.g., 20MHz
Propose to restrict the CSI feedback request granularity, which is indicated in NDPA, with 20MHz (essentially RU242) granularity for 11be
  How to indicate partial BW info in 11be NDPA is TBD
  Note this change is only on the feedback request granularity. It doesn’t affect feedback computation. For example, CQI feedback computation is still based on RU26 granularity (the same as 11ax) but according to 11be tone plan

## Slide 8: Feedback Tone Set (1/2)
20/40MHz: Reuse 11ax feedback tone sets for 11be
80MHz: Define feedback tone sets based on duplication of the feedback tone set of 40MHz plus extra feedback tones
  Ng=4: Reuse the 11ax feedback tones of Ng=4 for 11be
    Note that we can rewrite 11ax feedback tone set X=[-500:4:-4, 4:4:500] as [[-244:4:-4, 0, 4:4:244]-256, -8, -4, 4, 8, [-244:4:-4, 0, 4:4:244]+256] which consists of duplication of feedback tones of HE40 (i.e., [-244:4:-4, 4:4:244]) plus 6 additional feedback tones (±4, ±8, ±256)
  Ng=16: Redefine the feedback tones of Ng=16 for 11be by shifting the 11ax feedback tones of Ng=16 within 2nd & 3rd 20MHz (i.e., [-244:16:-4] and [4:16:244]) by -8 and 8 tones, respectively, plus 2 additional feedback tones (±4): X=[-500:16:-260, -252:16:-12, -4, 4, 12:16:252, 260:16:500]
    Note that we can rewrite the feedback tone set as [[-244:16:-4, 4:16:244]-256, -4, 4, [-244:16:-4, 4:16:244]+256], which consists of duplication of feedback tones of HE40 (i.e., [-244:16:-4, 4:16:244]) plus 2 additional feedback tones (±4)

## Slide 9: Feedback Tone Set (2/2)
160/320MHz: Duplicate the feedback tone set of 80MHz
  160MHz: Use the feedback tone set [X - 512, X + 512]
  320MHz: Use the feedback tone set [X - 1536, X - 512, X + 512, X + 1536]
  This is to reuse the 11ax rule of defining feedback tone set for >80MHz
The feedback tone set is used for the full BW CSI feedback

## Slide 10: Partial BW CSI Feedback Start/End Tone Indices Table
11ax partial BW CSI feedback Start/End tone indices tables (Tables 9-93c & 9-93d) are not suitable for 11be
  11ax tables are not aligned with RU26 in 2nd and 3rd 20MHz in EHT80 tone plan
  The RU26 indices are different: 11ax has 37 RU26 but 11be has 36 RU26
  11ax tables with RU26 granularity may not be efficient when the CSI feedback request uses 20MHz (essentially RU242) granularity
Propose to redesign feedback tone indices tables for 11be based on new EHT80 OFDMA tone plan with RU242 granularity
  If the requested feedback range doesn’t cover entire 80MHz segment, use the table for RU242
  When the entire 80MHz segment is requested, there are additional feedback tones outside RU242, and we use the tables for RU996

## Slide 11: Determine Feedback Tones
80MHz
  If the requested feedback tone range is full BW, the entire feedback tone set X is fed back, i.e., use the feedback tones of RU996-1
  If the requested feedback tone range is partial BW, the feedback tone set consists of all the feedback tones of the RU242 within the specified range
    E.g., if the 2nd 20MHz is requested, the feedback tone set is the feedback tones of RU242-2
Each 80MHz segment within 160MHz / 320MHz
  If the requested feedback range doesn’t cover entire 80MHz segment, the feedback tone set consists of all the feedback tones of the RU242 within the specified range
    E.g., if the 1st 40MHz within 320MHz is requested, the feedback tone set is the feedback tones of (RU242-1, RU242-2)
  If the requested feedback range covers entire 80MHz segment, the feedback tone set includes the entire feedback tone set of the particular 80MHz (e.g., RU996-n)
    E.g., if the 1st 80MHz within 160MHz is requested, the feedback tone set is the feedback tones of RU996-1
    E.g., if the 2nd 40MHz and 2nd 80MHz within 320MHz is requested, the feedback tone set is the feedback tones of (RU242-3, RU242-4, RU996-2)

## Slide 12: Partial BW CSI Feedback with 20MHz (RU242) Granularity
Propose the following table for both Ng=4 and Ng=16
  If the requested feedback range doesn’t cover entire 80MHz segment, use the following table
RU242 Index | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
1 | [-122:Ng:-4, 4:Ng:122] | [-244:Ng:-4] | [-500:Ng:-260] | [-1012:Ng:-772] | [-2036:Ng:-1796]
2 |  | [4:Ng:244] | [-252:Ng:-12] | [-764:Ng:-524] | [-1788:Ng:-1548]
3 |  |  | [12:Ng:252] | [-500:Ng:-260] | [-1524:Ng:-1284]
4 |  |  | [260:Ng:500] | [-252:Ng:-12] | [-1276:Ng:-1036]
5 |  |  |  | [12:Ng:252] | [-1012:Ng:-772]
6 |  |  |  | [260:Ng:500] | [-764:Ng:-524]
7 |  |  |  | [524:Ng:764] | [-500:Ng:-260]
8 |  |  |  | [772:Ng:1012] | [-252:Ng:-12]
9 |  |  |  |  | [12:Ng:252]
10 |  |  |  |  | [260:Ng:500]
11 |  |  |  |  | [524:Ng:764]
12 |  |  |  |  | [772:Ng:1012]
13 |  |  |  |  | [1036:Ng:1276]
14 |  |  |  |  | [1284:Ng:1524]
15 |  |  |  |  | [1548:Ng:1788]
16 |  |  |  |  | [1796:Ng:2036]

## Slide 13: Partial BW CSI Feedback with Entire 80MHz Segment
When the entire 80MHz segment is requested, define feedback tones for RU996 including additional feedback tones outside RU242
  Feedback tone table for Ng=4
  Feedback tone table for Ng=16
RU996 Index | 80MHz | 160MHz | 320MHz
1 | [-500:4:-4, 4:4:500] | [-1012:4:-516, -508:4:-12] | [-2036:4:-1540, -1532:4:-1036]
2 |  | [12:4:508, 516:4:1012] | [-1012:4:-516, -508:4:-12]
3 |  |  | [12:4:508, 516:4:1012]
4 |  |  | [1036:4:1532, 1540:4:2036]
RU996 Index | 80MHz | 160MHz | 320MHz
1 | [-500:16:-260, -252:16:-12, -4, 4, 12:16:252, 260:16:500] | [-1012:16:-772, -764:16:-524, -516, -508, -500:16:-260, -252:16:-12] | [-2036:16:-1796, -1788:16:-1548, -1540, -1532, -1524:16:-1284, -1276:16:-1036]
2 |  | [12:16:252, 260:16:500, 508, 516, 524:16:764, 772:16:1012] | [-1012:16:-772, -764:16:-524, -516, -508, -500:16:-260, -252:16:-12]
3 |  |  | [12:16:252, 260:16:500, 508, 516, 524:16:764, 772:16:1012]
4 |  |  | [1036:16:1276, 1284:16:1524, 1532, 1540, 1548:16:1788, 1796:16:2036]

## Slide 14: SP 1
Do you support that for 80MHz NDP or each 80 MHz segment of >80MHz bandwidth NDP
  If not punctured, using non-OFDMA 80 MHz tone plan
  If punctured, using OFDMA 80MHz tone plan
Y/N/A
 | RU & Tone Indices | 1x LTF Tones | 2x LTF Tones | 4x LTF Tones
Non-punctured | RU996, [-500:-3, 3:500] | A=[-500:4:-4, 4:4:+500] | A=[-500:2:-4, 4:2:500] | A=[-500:-3, 3:500]
1st 20MHz punctured | RU242+484, [-253:-12, 12:253, 259:500] | B1=[-252:4:-12, 12:4:252, 260:4:500] | B1=[-252:2:-12, 12:2:252, 260:2:500] | B1=[-253:-12, 12:253, 259:500]
2nd 20MHz punctured | RU242+484, [-500:-259, 12:253, 259:500] | B2=[-500:4:-260, 12:4:252, 260:4:500] | B2=[-500:2:-260, 12:2:252, 260:2:500] | B2=[-500:-259, 12:253, 259:500]
3rd 20MHz punctured | RU242+484, [-500:-259, -253:-12, 259:500] | B3=[-500:4:-260, -252:4:-12, 260:4:500] | B3=[-500:2:-260, -252:2:-12, 260:2:500] | B3=[-500:-259, -253:-12, 259:500]
4th 20MHz punctured | RU242+484, [-500:-259, -253:-12, 12:253] | B4=[-500:4:-260, -252:4:-12, 12:4:252] | B4=[-500:2:-260, -252:2:-12, 12:2:252] | B4=[-500:-259, -253:-12, 12:253]
1st 40MHz punctured | RU484, [12:253, 259:500] | C1=[12:4:252, 260:4:500] | C1=[12:2:252, 260:2:500] | C1=[12:253, 259:500]
2nd 40MHz punctured | RU484, [-500:-259, -253:-12] | C2=[-500:4:-260, -252:4:-12] | C2=[-500:2:-260, -252:2:-12] | C2=[-500:-259, -253:-12]

## Slide 15: SP 2
Do you support the following feedback tone sets for 11be?
  20/40MHz: Reuse 11ax feedback tone sets for 11be
  80MHz
    Ng=4: Reuse the 11ax feedback tones of Ng=4 for 11be
    Ng=16: Redefine the feedback tones of Ng=16 for 11be as [-500:16:-260, -252:16:-12, -4, 4, 12:16:252, 260:16:500]
  160/320MHz: Duplicate the feedback tone set of 80MHz
  Full BW sounding feedback entire tone set
Y/N/A

## Slide 16: SP 3
Do you support the following for 11be?
  The partial BW CSI feedback request uses 20MHz (RU242) granularity
  Note: Feedback request granularity change doesn’t impact the CSI computation scheme. For example, CQI feedback computation is still based on RU26
Y/N/A

## Slide 17: SP 4
Do you support the following feedback tone indices table with RU242 granularity for both Ng=4 and Ng=16 for 11be?
  If feedback request does not cover entire 80MHz segment, use the following table
  If feedback request covers entire 80MHz segment, feedback the entire 80MHz segment feedback tone set (using the tables for RU996 in next slide)
Y/N/A
RU242 Index | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
1 | [-122:Ng:-4, 4:Ng:122] | [-244:Ng:-4] | [-500:Ng:-260] | [-1012:Ng:-772] | [-2036:Ng:-1796]
2 |  | [4:Ng:244] | [-252:Ng:-12] | [-764:Ng:-524] | [-1788:Ng:-1548]
3 |  |  | [12:Ng:252] | [-500:Ng:-260] | [-1524:Ng:-1284]
4 |  |  | [260:Ng:500] | [-252:Ng:-12] | [-1276:Ng:-1036]
5 |  |  |  | [12:Ng:252] | [-1012:Ng:-772]
6 |  |  |  | [260:Ng:500] | [-764:Ng:-524]
7 |  |  |  | [524:Ng:764] | [-500:Ng:-260]
8 |  |  |  | [772:Ng:1012] | [-252:Ng:-12]
9 |  |  |  |  | [12:Ng:252]
10 |  |  |  |  | [260:Ng:500]
11 |  |  |  |  | [524:Ng:764]
12 |  |  |  |  | [772:Ng:1012]
13 |  |  |  |  | [1036:Ng:1276]
14 |  |  |  |  | [1284:Ng:1524]
15 |  |  |  |  | [1548:Ng:1788]
16 |  |  |  |  | [1796:Ng:2036]

## Slide 18: SP 4 (Cont’d)
  Feedback tone table for Ng=4
  Feedback tone table for Ng=16
RU996 Index | 80MHz | 160MHz | 320MHz
1 | [-500:4:-4, 4:4:500] | [-1012:4:-516, -508:4:-12] | [-2036:4:-1540, -1532:4:-1036]
2 |  | [12:4:508, 516:4:1012] | [-1012:4:-516, -508:4:-12]
3 |  |  | [12:4:508, 516:4:1012]
4 |  |  | [1036:4:1532, 1540:4:2036]
RU996 Index | 80MHz | 160MHz | 320MHz
1 | [-500:16:-260, -252:16:-12, -4, 4, 12:16:252, 260:16:500] | [-1012:16:-772, -764:16:-524, -516, -508, -500:16:-260, -252:16:-12] | [-2036:16:-1796, -1788:16:-1548, -1540, -1532, -1524:16:-1284, -1276:16:-1036]
2 |  | [12:16:252, 260:16:500, 508, 516, 524:16:764, 772:16:1012] | [-1012:16:-772, -764:16:-524, -516, -508, -500:16:-260, -252:16:-12]
3 |  |  | [12:16:252, 260:16:500, 508, 516, 524:16:764, 772:16:1012]
4 |  |  | [1036:16:1276, 1284:16:1524, 1532, 1540, 1548:16:1788, 1796:16:2036]