## Slide 1: NGV 11bd Architecture Discussion
Date: 2020-09-DD
Authors:

## Slide 2: Abstract
This submission provides the view of 802.11 TGbd that the 802.11bd amendment will not impact the 802.11 architecture. For discussion purposes information is provided regarding the proposed NGV MAC service update.

## Slide 3: Architecture of OCB (.11p)
OCB is defined as [1]:
outside the context of a basic service set (BSS) (OCB): A mode of operation in which a station
(STA) is not a member of a BSS and does not utilize IEEE 802.11 authentication, association, or
data confidentiality services.
STA behaviour OCB is summarized in Clause 4.3.7 [1]:
  The 802.11 architecture of STAs using OCB is a simple broadcast and receive architecture
  There is no “network” in the 802.11 OCB architecture, only STA to STA (point to point) or STA to STAs (broadcast) communication over the wireless media.
  No 802.11 MAC sublayer authentication services are used.
  OCB STAs can support ITS applications, providing IEEE 1609 or other higher layer standards communication services over the wireless media.
There are currently no architecture figures related to OCB in 802.11 [1]

## Slide 4: Architecture of NGV (.11bd) Thoughts
There are no planed changes to the OCB concept, hence:
  There are no 802.11 BSSs in NGV
  There is no 802.11 authentication, association, or data confidentiality services in NGV
There is no planned changes to the STA behaviour OCB (Clause 4.3.7):
  So there are no significant 802.11 architecture impacts
  NGV STAs operating in a OCB mode are targeted to support ITS applications
  NGV STAs will provide IEEE 1609 or other higher layer standards next generation communication services over the wireless media.
There are currently no architecture figures proposed to be added to the 802.11 specification

## Slide 5: Possibly of Interest to the 802.11 ARC SC
There is a proposal to “clean up” the MAC service interface so that it is more compatible with IEEE 1609 and other higher layer ITS specifications
[need to provide the details of the changes, for discussion and maybe some figures]

## Slide 6: References
IEEE 802.11REVmdD3.0, http://www.ieee802.org/11/private/Draft_Standards/11md/Draft%20P802.11REVmd_D3.0.pdf
11-19/1805r1 MAC Service Update for NGV, Michael Fischer
11-19/1031r0 The MAC Services Mismatch Between 802.11 and 1609.4, Michael Fischer
11-19/0083r5 Indicating NGV Capabilities in MAC Header, Michael Fischer