## Slide 1: S1G EU New Band
Date: 2020-08-04
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com

## Slide 2: Abstract
CID 4036
The EU has recently added a band suitable for use by S1G devices
1 MHz channels only
These newly available channels should be included in the global channels listing in Annex E
  Table E-4—Global operating classes
  That table references Table E-5 S1G operating classes
    So this table also needs to be updated

## Slide 3: CID 4036
CID 4036
CID | Commenter | Page | Clause | Comment | Proposed Change | Proposed Resolution
4036 | David Goodall | 4382.00 | E | The 915.8 MHz to 919.4 MHz band has become available for use by S1G devices in Europe. | Add an operating class for the new band available in Europe to table E-5. This will support 1 MHz channels only. It will also need a global operating class added to table E-4. | Revise – TGmd editor to make changes shown in 11-20-1182r1 which add operating classes to the Annex E Global operating classes table and the Annex E S1G operating classes table to include the new band and channels

## Slide 4: New Channels
The following channels are recently available in the EU, but are not included in the Global operating classes table in Annex E, nor in the S1G operating classes table in Annex E
1 MHz channels within the range:
  915.8 – 919.4 MHz
    i.e. 3 or 4 channels, depending on where you start

## Slide 5: Example Of S1G Operating Classes (1)
Table E-4—Global operating classes
Note that Channel Set is not provided directly (in contrast to non-S1G cases)
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
71 | E-5-4, E-5-25, E-5-29 | 0.902 | 8 | - | Reserved | -
72 | E-5-5 | 0.902 | 16 | - | Reserved | -
73 | E-5-8 | 0.9165 | 1 | - | Reserved | -
74 | E-5-14 | 0.9175 | 1 | - | Reserved | -
An existing example of S1G classes:
S1G Table references

## Slide 6: Determining S1G Channel Numbers
23.3.14 Channelization
  Extracted text:
  Channel center frequency determination:
    fc = ChannelStartingFrequency + fseparation x ChannelCenterFrequencyIndex
  fseparation has the value 0.5 MHz
  ChannelStartingFrequency and ChannelCenterFrequencyIndex are region and operating class specific and given in Annex E.
The global table entries show “reserved” – so you need to consult Table E-5 S1G operating class table
  See next slide

## Slide 7: Example Of S1G Operating Classes (2)
Table E-5—S1G operating classes
Currently, only S1G operating classes 6 and 7 are defined for the EU
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
4 (United States) | 71 | 0.902 | 8 | 44 | Type 1 (920-928 MHz) | -
 |  |  |  | 12, 28 | Type 2 (904-920 MHz) | 
5 (United States) | 72 | 0.902 | 16 | 20 | Type 2 (904-920 MHz) | -
6 (Europe) | 66 | 0.863 | 1 | 1, 3, 5, 7, 9 | Type 1 (863-868 MHz) | -
7 (Europe) | 67 | 0.863 | 2 | 2, 6 | Type 1 (863-868 MHz) | -
How to find S1G channels:
S1G Channel Numbers!

## Slide 8: Where Does the New EU Band Fit? (1)
Only two S1G operating classes currently defined for the EU
  They share a starting frequency which is different from the new one
  They share a channel number system/set/organization (with each other)
    Two classes exist because channel widths are different: 1 v 2 MHz
Some countries have multiple starting frequencies, i.e. “bands”
  China, Singapore
  Both of them restart the numbering for each “band” (i.e. class)
  See next slide

## Slide 9: Example Of S1G Operating Classes (3)
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
17 (Singapore) | 66 | 0.863 | 1 | 7, 9, 11 | Type 1 (866-869 MHz) | -
18 (Singapore) | 68 | 0.902 | 1 | 37, 39, 41, 43, 45 | Type 2 (920-925 MHz) | -
9 (China) | 61 | 0.755 | 1 | 1, 3, 5, 7, 9, 11, 13, 15, 17, 19, 21, 23, 25, 27, 29, 31, 33, 35, 37, 39, 41, 43, 45, 47 | Type 1 (755-779 MHz) | -
10 (China) | 62 | 0.779 | 1 | 1, 3, 5, 7, 9, 11, 13, 15 | Type 1 (779-787 MHz) | -
Table E-5 - Mutliple bands for Singapore and China:

## Slide 10: Where Does the New Band Fit? (2)
EU needs a new starting frequency (i.e. new “band”)
  Based on existing examples:
    RESTART channel numbering for the new “band”
    E.g. first channel 1, last channel 6 for the new 915.8 - 919.4 band
      i.e. 7x0.5 = 3.5 MHz total (919.4 – 915.8 = 3.6)
How much guard band?
  1 MHz wide channels
  Centers are on 0.5 MHz frequencies
    Center of channel with index 1, at 916 or 916.5?
      fc = ChannelStartingFrequency + fseparation x ChannelCenterFrequencyIndex
    E.g. ChannelStartingFrequency = 916, index = 1, center = 916.5
      i.e. index == channel number

## Slide 11: Proposed Changes (1)
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
77-80 | -E-5-30 | Reserved0.916 | Reserved1 | Reserved- | -Reserved | -Reserved
78-80 | - | Reserved | Reserved | Reserved | - | Reserved
TGmd editor to make the following changes to Table E-4 – Global operating classes (note that one new row is being added to the table):

## Slide 12: Proposed Changes (2)
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
30 (Europe) | 77 | 0.916 | 1 | 1, 3, 5 | Type 1 (916-919 MHz) | -
TGmd editor to add the following new row to Table E-5 – S1G operating classes:

## Slide 13: Channel Options
Band extends from 915.8 - 919.4
Starting frequency = 916.0
  1, 3, 5
    916.5, 917.5, 918.5
  2, 4, 6
    917, 918, 919
    Index 0 = 916 center?
      Oddly, channel index 0 is never used!
Starting frequency = 915.5 (below the band!)
  1, 3, 5, 7
    916, 917, 918, 919

## Slide 14: Straw poll #1
Do you support the proposed changes to Draft P802.11REVmd_D3.2 Annex E Table E-4 – Global operating classes and Annex E Table E-5 – S1G operating classes as described in 11-20-1182-01-000m-S1G-EU-New-Band Proposed Changes (1) and Proposed Changes (2)?
  YES
  NO
  ABS

## Slide 15: References
[1] Draft P802.11REVmd_D3.4