## Slide 1: TB PPDU Format Signaling in Trigger Frame
Authors:
Date: 2020-08-06

## Slide 2: Introduction
11be defined EHT TB PPDU format [1].
  EHT STAs would be capable of transmitting HE TB PPDU as well as EHT TB PPDU.
HE STAs and EHT STAs will coexist, and AP may want to schedule UL MU transmissions from HE and EHT STAs at the same time.
The spec needs to define a clear rule which PPDU format between HE TB PPDU and EHT TB PPDU is used to respond to a Trigger frame for MU operation.
This contribution proposes methods to indicate TB PPDU format and addresses an issue when using UORA.

## Slide 3: Problem without TB PPDU format determination rule
If there is no rule to determine TB PPDU format, HE TB PPDU (from EHT STAs and HE STAs) and EHT TB PPDU (from EHT STAs) may be transmitted on the same channel.
Therefore, 11be can define a Trigger frame including the signaling that indicates which TB PPDU format is used.
  Another solution is that EHT STAs always use EHT TB PPDU.
  However, with this solution, when EHT STAs and HE STAs coexist, it is difficult to solicit responses from them at the same time.
AP
Trigger frame
HE STA
HE TB PPDU
EHT STA 1
EHT TB PPDU
EHT STA 2
HE TB PPDU

## Slide 4: How to signal TB PPDU format?
Several contributions proposed methods to indicate EHT information in a Trigger frame [2-4]. For example,
  (Method 1) Indication by Common Info field
  (Method 2) Indication by User Info field
MAC header | Common Info | User Info | … | User Info | Padding | FCS
MAC header | Common Info | User Info | User Info | User Info (AID12: EHT TB PPDU) | User Info | User Info (AID12: beyond EHT TB PPDU) | User Info | Padding | FCS
Response as indicated by Version ID
Version ID
EHT TB PPDU response
Beyond EHT TB PPDU response
HE TB PPDU response

## Slide 5: (Method 1) Indication by Common Info field
The Common Info field can include the Version ID subfield.
  Then TB PPDU format can be determined based on the Version ID subfield.
Trigger frame format can be redefined from the Common Info field considering each standard.
  The Trigger frame format is determined based on the Version ID subfield.
    The format should be transparent to HE STAs.
  The Common Info field carries information for EHT (or beyond EHT) standard such as U-SIG version dependent bits.
MAC header | Common Info | User Info | … | Padding | FCS
Response as indicated by Version ID
Version ID

## Slide 6: (Method 1) How to indicate Version ID subfield?
Some bits in the Common Info field can be used as the indication whether the Version ID subfield is present.
  (Example 1. Trigger Type) Trigger Type specifies whether the Version ID subfield is present.
    Multiple values of the Trigger Type subfield or a new subfield need to be used to indicate the Trigger frame variant.
  (Example 2. UL Length) It is determined if the Version ID subfield is present based on UL Length mod 3.
    UL Length mod 3 is not equal to 0 for the current Trigger frame.
 | B0 B3 | B4 B15
 | Trigger Type | UL Length
Bits: | 4 | 12
If UL Length mod 3 != 0
If UL Length mod 3 == 0
 | B16 | B17 | B18 B19 | 
 | More TF | CS Required | UL BW | …
Bits: | 1 | 1 | 2 | 
HE variant
EHT variant
Beyond EHT variant
 | More TF | … | Version ID | …
Then Version ID is included in a Trigger frame.
Bitwidth and location are TBD.

## Slide 7: (Method 2) Indication by User Info field
When the AID12 subfield is set to a specific value, it indicates TB PPDU format.
  STAs triggered by following User Info fields use TB PPDU format indicated by the AID12 subfield set to the specific value.
Additional information for extended features of EHT (or beyond EHT) can be obtained by reinterpreting existing subfields or by including it in the User Info field with the specific AID12 subfield value.
This method can trigger A-PPDU with a single Trigger frame.
MAC header | Common Info | User Info 1 | User Info 2 | User Info 3 (AID12: EHT TB PPDU) | User Info 4 | User Info 5 (AID12: beyond EHT TB PPDU) | User Info 6 | Padding | FCS
EHT TB PPDU response
Beyond EHT TB PPDU response
HE TB PPDU responses

## Slide 8: UORA consideration (1)
It is also required to consider UORA.
  RA-RUs are indicated by the AID12 subfield set to 0 or 2045.
  If we design a Trigger frame to be transparent to HE STAs, HE STA would respond with HE TB PPDU on RA-RU without understanding the TB PPDU format signaling.
MAC header | Common Info | User Info 1 | User Info 2 | User Info 3 (AID12: EHT TB PPDU) | User Info 4 (AID12: 0) | User Info 5 | User Info 6 | Padding | FCS
HE STAs may respond on RA-RU indicated by User Info 4 using HE TB PPDU.
Example (Method 2)

## Slide 9: UORA consideration (2)
Under method 1, when the Version ID subfield of a Trigger frame indicates EHT (or beyond EHT), the Trigger frame should not include the User Info field with the AID12 subfield set to 0 or 2045.
  New values to indicate RA-RUs for EHT STAs can be considered for this case.
MAC header | Common Info | User Info (AID12: New value for RA-RU) | … | Padding | FCS
Response as indicated by Version ID
Version ID

## Slide 10: UORA consideration (3)
Under method 2, a Trigger frame can include the User Info field with its AID12 subfield set to 4095 in the middle of User Info fields.
  An HE STA cannot recognize RA-RUs indicated by User Info 4, since User Info 4 is located after User Info 2.
  When an EHT STA transmits a frame on RA-RU indicated by User Info 1, HE TB PPDU is used.
  When an EHT STA transmits a frame on RA-RU indicated by User Info 4, EHT TB PPDU is used.
MAC header | Common Info | User Info 1 (AID12: 0 for RA-RU) | User Info 2 (AID12: 4095) | User Info 3 (AID12: EHT TB PPDU) | User Info 4 (AID12: 0 for RA-RUs) | Padding | FCS
HE STAs interpret User Info 2 and the following User Info fields as Padding field.

## Slide 11: Conclusion
Considering the coexistence of STAs of various generations, a Trigger frame can include the TB PPDU format indication signaling.
This contribution proposed signaling methods for indicating TB PPDU format and addressed the UORA issue.

## Slide 12: References
[1] 11-19/1262r12 Specification Framework for TGbe
[2] 11-20/0764 Trigger Consideration
[3] 11-20/0831 Trigger Frame for Frequency-domain A-PPDU Support
[4] 11-20/0840 Backward Compatible EHT Trigger Frame

## Slide 13: Straw poll 1
Do you support that a Trigger frame includes the signaling that indicates TB PPDU format to be used.
  Which of fields between Common Info field and User Info field includes the signaling is TBD.
  Y/N/A

## Slide 14: Straw poll 2
Do you support that a Trigger frame can include the User Info field with its the AID12 subfield set to 4095 before the other User Info field?
  Y/N/A