## Slide 1: M/O of 20MHz NGV PPDU
Date: 2020-08-10
Authors:

## Slide 2: Introduction
TGbd already decides to make most PHY features mandatory for better interop and OCB service.
  10MHz NGV PPDU format
  All modulation and coding: MCS0~10
  All NGV-LTF formats
  LDPC
  Midamble with all periodicity
  non-NGV 10MHz and repetition transmission
Support of two spatial streams is optional.
One pending M/O decision: 20MHz NGV PPDU.
  20MHz NGV PPDU is the PPDU format that can coexist with 10MHz NGV PPDU and 10MHz non-NGV PPDU.

## Slide 3: 20MHz NGV PPDU
Some debates on this topic in the teleconference and TGbd maillist.
Mandatory:
  Easier interop across different geographical regions.
  Compatible with 10MHz NGV/non-NGV PPDU, good differentiation feature to 11p STA.
Optional:
  Limited DSRC/ITS 20MHz channel availability.
  20MHz channel is not generally available across the world.
  Allow 10MHz-only NGV STA for lower cost/complexity.
Notice slightly more preference to make it optional.

## Slide 4: Straw Poll
Do you agree to define 20MHz NGV PPDU as an optional feature?
  Note: 20MHz NGV PPDU is the PPDU format that coexists with 10MHz NGV PPDU and 10MHz non-NGV PPDU.
Y
N
A

## Slide 5: Motion
Move to include the following text to section 3 of the 11bd SFD:
An NGV STA optionally supports 20MHz NGV PPDU.
  Note: 20MHz NGV PPDU is the 20MHz PPDU format that coexists with 10MHz NGV PPDU and 10MHz non-NGV PPDU.
Y
N
A