## Slide 1: 4x 320MHz EHT-LTF Design
Date: 2020-08-12
Authors:
Name | Affiliations | Address | Phone | email
Leo Montreuil | Broadcom |  |  | leo.montreuil@broadcom.com
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Introduction
Designing a good sequence with low PAPR for all puncturing cases of 320MHz proves to be a challenge.
[1] and [2] propose a 4x 320MHz LTF design.
In here we propose a new sequence that fulfils our preference for a modular design while having the lowest PAPR possible.
The 320MHz EHT-LTF sequence is constructed using a 996 tones base sequence and 8 coefficient values

## Slide 3: 80 MHz 4X base sequence
LTF80_4x = [ ...
+1 +1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 ...
-1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 ...
+1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 ...
-1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 ...
+1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 ...
+1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 ...
-1 +1 +1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 ...
+1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 ...
+1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 ...
-1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 0 0 ...
0 ...
0 0 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 +1 ...
+1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 ...
-1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 ...
+1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 ...
+1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 ...
-1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 ...
-1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 ...
+1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 ...
-1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 ...
+1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1];
Covering 1001 tones [-500:500] for RU996 in any 80MHz

## Slide 4: 320MHz 4X EHT-LTF
LTF320_4x = [ ...
[(+1)*LTF80_4x(1:500), (+1)*LTF80_4x(501:1001)], zeros(1,23), ...
[ (-1)*LTF80_4x(1:500), (+1)*LTF80_4x(501:1001)], zeros(1,23), ...
[(+1)*LTF80_4x(1:500), (+1)*LTF80_4x(501:1001)], zeros(1,23), ...
[(+1)*LTF80_4x(1:500), (-1)*LTF80_4x(501:1001)] ];
Coefficient values = [ +1 +1, -1 +1, +1 +1, +1 -1 ]

## Slide 5: Multi-RU PAPR
RU size | BPSK data | LTF Nss=1:8
996 | 8.84 | 5.89
 |  | 6.24
 |  | 5.89
 |  | 6.24
996 + 484 | 9.17 | 8.28
 |  | 8.13
 |  | 8.30
 |  | 7.99
 |  | 8.31
 |  | 8.04
 |  | 8.24
 |  | 7.81
2*996 | 9.27 | 7.01
 |  | 6.75
3*996 | 9.54 | 8.44
 |  | 8.39
 |  | 8.31
 |  | 8.54
3*996 + 484 | 9.55 | 8.29
 |  | 8.16
 |  | 8.11
 |  | 8.50
 |  | 7.46
 |  | 7.12
 |  | 8.39
 |  | 8.45
4*996 | 9.60 | 6.30
RU size | BPSK data | LTF Nss=1:8
2*996 + 484 | 9.50 | 7.97
 |  | 7.63
 |  | 8.74
 |  | 8.72
 |  | 7.97
 |  | 7.81
 |  | 8.50
 |  | 8.86
 |  | 8.50
 |  | 8.86
 |  | 10.09
 |  | 9.67
 |  | 9.00
 |  | 9.22
 |  | 7.61
 |  | 7.98
 |  | 8.17
 |  | 8.04
 |  | 8.66
 |  | 8.55
 |  | 9.75
 |  | 9.99
 |  | 8.66
 |  | 8.55
2*996 discrete | 9.28 | 8.69
 |  | 9.05
 |  | 7.01
 |  | 6.62
RU size | BPSK data | LTF Nss=1:8
3*996+484+242 | 9.57 | 7.59
 |  | 7.92
 |  | 7.55
 |  | 7.38
 |  | 8.32
 |  | 7.74
 |  | 7.89
 |  | 7.55
 |  | 7.53
 |  | 7.43
 |  | 7.53
 |  | 7.63
 |  | 7.14
 |  | 7.31
 |  | 8.00
 |  | 7.79

## Slide 6: Worst case PAPR for Nss = 1 to 8
Sequence | BPSK Median | Legacy 11ax 4X HE-LTF | Legacy 11ax 4X HE-LTF | [1] LGE 4X EHT-LTF | [2] Huawei 4X EHT-LTF | BRCM 4X EHT-LTF
Tone Plan |  | 11ax | 11be |  |  | 
RU26 |  | 4.25 | 7.29 | 7.29 | 7.29 | 3.78
RU52 |  | 4.97 | 8.48 | 8.48 | 8.48 | 5.12
RU106 |  | 5.53 | 6.69 | 6.69 | 6.69 | 5.27
RU242 |  | 5.60 | 7.07 | 7.07 | 7.07 | 5.41
RU484 |  | 6.00 | 7.38 | 7.38 | 7.38 | 6.54
RU996 | 8.84 | 6.29 | 6.74 | 7.41 | 7.41 | 6.24
4*RU996 | 9.60 |  |  | 10.12 | 7.39 | 6.30
3*RU996 | 9.54 |  |  | 9.41 | 9.50 | 8.54
3*RU996 + RU484 | 9.55 |  |  | 10.02 | 9.47 | 8.50
2*RU996 + RU484 | 9.50 |  |  | 10.12 | 10.87 | 10.09
2*RU996 | 9.27 |  |  | 7.25 | 9.55 | 7.01
2*RU996 discrete | 9.28 |  |  | 10.05 | 7.94 | 9.05
RU996 + RU484 | 9.17 |  |  | 9.31 | 9.22 | 8.31

## Slide 7: Conclusion
In this contribution, a modular and low PAPR 4x 320MHz EHT-LTF sequence is proposed
The sequence is optimized for 320 MHz and all multi-RU cases of a punctured 320MHz (including punctured 240MHz and including small RU)

## Slide 8: References
“4x EHT-LTF sequence”, IEEE 802.11-20/1066r0 Slide 4, Case 1 Option 1
“EHT-LTFs Sequences Design”, IEEE 802.11-20/0926r0 Slide 16, Option 2

## Slide 9: SP #1
Do you support the proposed sequence construction on slide 3 and 4 ?
Y
N
A