## Slide 1: RTS Trigger SU PPDU
Date: 2020-08-11
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Notes: November 2012

## Slide 2: Abstract
Some EHT non-AP STA devices will have operating conditions with restrictions on TX and RX behavior
  E.g. Simultaneous TX/RX might be restricted for certain link channel combinations for non-AP STA aka NSTR
Need mechanism to attain access to >1 links for maximum MLO performance
  E.g. synchronize PPDUs
When a NSTR STA starts a TX on one Link1, medium state of Link2 is lost due to NEXT
  Need assistance to maintain Link2 medium state during Link1 TX operation, e.g. synchronize PPDUs

## Slide 3: Proposed Trigger Modifications (1)
Allow any STA to transmit a Trigger
  I.e. currently only an AP is allowed to transmit a Trigger
Allow trigger in response to an RTS, not only as an initiating PPDU
The Trigger should include parameter values which create alignment with other PPDUs
Include a field to indicate whether the response to the Trigger is an SU PPDU or HE TB PPDU
Existing MU Trigger may still be used for this purpose

## Slide 4: Trigger Modifications (2)
The trigger is modified to allow the trigger to specify that the recipient is allowed to choose some of the parameters of the trigger response PPDU
  E.g. the trigger includes some means to signal that specific parameters are to be chosen by the trigger recipient, parameters, such as:
    MCS, RSSI Target, Spatial Reuse
  But the PPDU duration must be present and must be used by the trigger recipient
    In order to align the PPDU with the PPDU on other link(s)
CS is not required for the response to the Trigger that is a response to RTS
  When RTS was used to solicit the Trigger, both RTS and Trigger examined the medium before TX, so that the CS requirement is already satisfied

## Slide 5: TX TX Case RTS Trigger (1)
MLD AP has declared Link2 as Triggered only (optional)
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw estimates time when backoff==0 on Link2
    Potentially after the RTS reception
  STAw prepares Link1 Trigger response to RTS based on expected start time of Trigger on Link2, to align Trigger end times
    E.g. create Link1 Trigger that is longer than it needed to be
  STAw prepares Link1 and Link2 Triggers to have identical elicited response PPDU end times
  Link2 EDCA backoff==0 time is fairly predictable because of Trigger-only restricted operation on Link2
  Data PPDUs potentially need TRS or Trigger to ensure that BA response PPDU durations are equal
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
DATA PPDUs

## Slide 6: UTA TX TX Case RTS Trigger (2)
MLD AP has declared Link2 as Triggered only (optional)
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw sees start of RTS transmission
  STAw Link2 backoff expires during or even before RTS reception
    Backoff on Link2 might have expired long before Link1 RTS reception begins!
    In any case, STAw optionally waits for outcome of RTS reception before transmitting on Link2
  STAw detects opportunity for parallel Triggers to STA1 on Link1 and Link2
  STAw transmits parallel Triggers to STA1 on Link1 and Link2
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
STAw chooses to delay transmission

## Slide 7: RTS Trigger Sequence
Trigger response to RTS
  Link1 recipient either:
    Wins contention on Link2 and transmits a Data PPDU that matches the duration of the Link1 transmission
      Not shown in the diagram
    Receives an RTS from some other STA and responds with a Trigger to force alignment of that STA transmission with the Link1 PPDU
      As depicted in the diagram
RA=STAw, TA=STA2
RA=STAw, TA=STA1
BA+T
RA=STAz, TA=STAw+T
R
C
R
T
BA+T
RA=STAx, TA=STA1+T
EDCA
LINK1
LINK2
BA+T
BA+T
Don’t care, potential loss of MPDUs

## Slide 8: Straw Poll 1
Do you support the inclusion of the following in the SFD:
  802.11be shall define a trigger message that may be transmitted by an AP or a non-AP STA that elicits an SU PPDU as a means to assist in creating an alignment of PPDU start and or end times on different links and to improve MLO utilization by NSTR devices
  YES
  NO
  ABS

## Slide 9: Straw Poll 2
Do you support the inclusion of the following in the SFD:
  802.11be shall define a frame exchange sequence that allows
    A trigger-like frame transmission in response to the receipt of an RTS
  YES
  NO
  ABS

## Slide 10: Reference
[1] Draft P802.11REVmd_D3.4
[2] Draft P802.11ax_D6.1