## Slide 1: RTS Trigger SU PPDU
Date: 2020-08-30
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Notes: November 2012

## Slide 2: Abstract
Some EHT non-AP STA devices will have operating conditions with restrictions on TX and RX behavior
  E.g. Simultaneous TX/RX might be restricted for certain link channel combinations for non-AP STA aka NSTR
Need mechanism to attain access to >1 links for maximum MLO performance
  E.g. synchronize PPDUs
When a NSTR STA starts a TX on one Link1, medium state of Link2 is lost due to NEXT
  Need assistance to maintain Link2 medium state during Link1 TX operation, e.g. synchronize PPDUs

## Slide 3: Proposed Trigger Modifications (1)
Allow any STA to transmit a Trigger
  I.e. currently only an AP is allowed to transmit a Trigger
Allow trigger in response to an RTS, not only as an initiating PPDU
The Trigger should include parameter values which create alignment with other PPDUs
Include a field to indicate whether the response to the Trigger is an SU PPDU or HE TB PPDU
Existing MU Trigger may still be used for this purpose

## Slide 4: Trigger Modifications (2)
The trigger is modified to allow the trigger to specify that the recipient is allowed to choose some of the parameters of the trigger response PPDU
  E.g. the trigger includes some means to signal that specific parameters are to be chosen by the trigger recipient, parameters, such as:
    MCS, RSSI Target, Spatial Reuse
  But the PPDU duration must be present and must be used by the trigger recipient
    In order to align the PPDU with the PPDU on other link(s)
CS is not required for the response to the Trigger that is a response to RTS
  When RTS was used to solicit the Trigger, both RTS and Trigger examined the medium before TX, so that the CS requirement is already satisfied

## Slide 5: TX TX Case RTS Trigger (1)
MLD AP has declared Link2 as Triggered only (optional)
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw estimates time when backoff==0 on Link2
    Potentially after the RTS reception
  STAw prepares Link1 Trigger response to RTS based on expected start time of Trigger on Link2, to align Trigger end times
    E.g. create Link1 Trigger that is longer than it needed to be
  STAw prepares Link1 and Link2 Triggers to have identical elicited response PPDU end times
  Link2 EDCA backoff==0 time is fairly predictable because of Trigger-only restricted operation on Link2
  Data PPDUs potentially need TRS or Trigger to ensure that BA response PPDU durations are equal
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
DATA PPDUs

## Slide 6: UTA TX TX Case RTS Trigger (2)
MLD AP has declared Link2 as Triggered only (optional)
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw sees start of RTS transmission
  STAw Link2 backoff expires during or even before RTS reception
    Backoff on Link2 might have expired long before Link1 RTS reception begins!
    In any case, STAw optionally waits for outcome of RTS reception before transmitting on Link2
  STAw detects opportunity for parallel Triggers to STA1 on Link1 and Link2
  STAw transmits parallel Triggers to STA1 on Link1 and Link2
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
STAw chooses to delay transmission

## Slide 7: TX TX Case RTS Trigger (3)
MLD AP has declared Link2 as Triggered only (optional)
  Some STA2 is using Link2
STAw forces alignment of STA1 TX by sending a trigger in response to RTS
  I.e. no opportunity for dual-trigger multi-link UL TX by STA1
  Helps NSTR STA1 recover from deafness during LINK1 TX operation
    No need to modify any deafness recovery protocol, but forcing the alignment makes that protocol work better because the formerly deaf STA is likely to get it right, i.e. what STA1 believes to be IDLE is actually IDLE
  STAw should make both BA the same Length
RA=STAw, TA=STA1
RA=STAw, TA=STA2
BA
R
T
BA
LINK1
LINK2
BUSY
STA1 EDCA counts down to 0
DATA PPDUs

## Slide 8: RTS Trigger Sequence
Trigger response to RTS
  Link1 recipient either:
    Wins contention on Link2 and transmits a Data PPDU that matches the duration of the Link1 transmission
      Not shown in the diagram
    Receives an RTS from some other STA and responds with a Trigger to force alignment of that STA transmission with the Link1 PPDU
      As depicted in the diagram
RA=STAw, TA=STA2
RA=STAw, TA=STA1
BA+T
RA=STAz, TA=STAw+T
R
C
R
T
BA+T
RA=STAx, TA=STA1+T
EDCA
LINK1
LINK2
BA+T
BA+T
Don’t care, potential loss of MPDUs

## Slide 9: Non-AP STA Trigger Sequence
Trigger response to RTS
  Link1, e.g. AP DL TX to STAX
  Link2, e.g. AP DL TX to STAY
    STAY responds to AP RTS with Trigger to align DL TX
      E.g. AP does not have cross-link information
    Note that STAA should attempt to align BA
      STAA can include Trigger in Data PPDU for non-cross link AP
RA=STAX, TA=STAA
RA=STAY, TA=STAA+T
BA
R
C
R
T
EDCA
LINK1
LINK2
BA

## Slide 10: Additional Uses for Triggered SU PPDU
For polling-like UL triggering
  E.g. AP gains access and loans the TXOP to a selected STA
  Various parameters of the UL TX can be left as choices for the triggered STA
    E.g. Length, MCS, NSS, etc
For use in P2P exchanges, for example
  When the AP gains a TXOP and loans it to a STA for P2P use
  When one peer has intermittent availability, the is effectively a notification of the availability
  Various parameters of the UL TX can be left as choices for the triggered STA
    E.g. Length, MCS, NSS, etc

## Slide 11: Details TBD
In some instances, the STA transmitting the Trigger might specify
  Some strict parameters
  Some parameters whose exact values are left as choices for the triggered STA
    Or perhaps within a range of values
The mechanism for expressing such restrictions and choices is TBD
The scenarios for which various parameters would be strict or choices is TBD

## Slide 12: Triggered Only Link Restriction
As noted in the slides
  Probability of being able to transmit Trigger on more than one link is enhanced if the AP has declared linkB as Triggered-only
    AP does not have to deal with MyBSS competition
Limitation of Triggered-only link
  Reduces ability of any STA to gain lowest latency UL access
    I.e. non-AP STA does not gain a latency advantage of having multiple links on which to compete for access when it is not allowed to compete for more than one link
  Latency performance can be regained if non-AP STAs are allowed to compete on the triggered link when it is not being used
    See Trigger-limited link definition

## Slide 13: Trigger-limited Link
Trigger-limited link:
  Triggered-only limitation only applies until one link is occupied
  When only one link is occupied, then triggered limitation is relaxed to allow EDCA access of the unoccupied, trigger-limited link
    Provided that the winner of a TXOP on the Trigger-limited link performs alignment with the occupied link
    EDCA access is delayed until it is known whether both links will be triggered
      E.g. EDCA access on trigger-limited link begins PIFS after the start of the triggered PPDU on the occupied link
        I.e. at the time that a trigger-aligned PPDU would have appeared, but has not appeared

## Slide 14: Comparison to Wait Slot (1)
Wait Slot
  NSTR STA optionally holds a backoff count of a link at or near zero to wait for another link’s backoff to reach zero
  Simultaneous, aligned PPDU transmission on multiple links is achieved, see [3]
  [3] indicates that as loads increase, the probability of acquiring more than one link rapidly reduces
  Without alignment, as load increases, winning NSTR transmitters are effectively punished after each transmission, awaiting re-alignment on deaf channel
    Losing latency benefit of having multiple channels

## Slide 15: Comparison to Wait Slot (2)
The RTS-Trigger method with Trigger-limited access rule allows multi-link access to be acquired under higher load conditions
  Enforcement of PPDU alignment makes operation more efficient for small competing node counts
    Restores latency benefit
  Centralized decision on number of links occupied by an NSTR competitor allows centralized decision regarding tradeoff between throughput and latency

## Slide 16: Straw Poll 1
Do you support the inclusion of the following in the SFD:
  802.11be shall define a trigger message in R1 that may be transmitted by an AP or a non-AP STA and that elicits SU PPDUs
  YES
  NO
  ABS

## Slide 17: Straw Poll 2
Do you support the inclusion of the following in the SFD:
  802.11be shall define a frame exchange sequence in R1 that allows
    A trigger-like frame transmission in response to the receipt of an RTS
  YES
  NO
  ABS

## Slide 18: Straw Poll 3
Do you support the inclusion of the following in the SFD:
  An AP may indicate a link to be Trigger-limited in R1 such that
    UL access on the link is limited to Triggered access, except that:
      If a PPDU is transmitted on a non-trigger-limited link, then EDCA access may proceed on the Trigger-limited link aRXPHYDelay + PIFS after the start of a PPDU on the non-trigger-limited link, when that PPDU has a PHY LENGTH indication >= 0.50 ms
      Any PPDU transmitted by a non-AP STA on the trigger-limited link shall terminate at or before the end of the aligned PPDU on the other link
  YES
  NO
  ABS

## Slide 19: Reference
[1] Draft P802.11REVmd_D3.4
[2] Draft P802.11ax_D6.1
[3] 11-20-0993-03-00be-sync-ml-operations-of-non-str-device