## Slide 1: Subcarrier Grouping for EHT
Date: 2020-08-13
Authors:

## Slide 2: Introduction
802.11be shall supports that [1]
  Wideband band and noncontiguous spectrum utilization
  Large size RU combination assigned to a single STA.
  Maximum 16 spatial streams
Beamforming feedback overhead is significantly increased, compared to 11ax [2]
In order to reduce feedback overhead, the subcarrier grouping method was adopted in 11ac and 11ax
In this slide, we propose the subcarrier grouping size (Ng) for 802.11be

## Slide 3: Recap: Subcarrier grouping
Subcarrier grouping
  Only a single compressed beamforming feedback matrix is reported for each group of Ng adjacent subcarriers.
Feedback overhead reduction vs. channel information accuracy
  By using the grouping method, we can reduce the feedback overhead (i.e., total length of CBR frame)
  However, the channel information becomes inaccuracy

## Slide 4: Subcarrier grouping size (Ng) for EHT
Proposal of Ng for EHT
The reason for the proposal
  In most HE SU-MIMO cases, we observed that there was little PER performance difference between Ng=4 and Ng=16
  In most HE MU-MIMO cases, we observed that there was large PER performance difference between Ng=4 and Ng=16
 | SU | MU
VHT | 1, 2, 4 | 
HE | 4, 16 | 
EHT | 16, 32 | 4, 8
Subcarrier spacing for VHT: 312.5 KHz Subcarrier spacing for HE and EHT: 78.125 KHz |  | 

## Slide 5: Simulation parameters
Parameter | Value
Frame format | HE
Packet size | 4,096 byte
Channel model | B, D
Impairment | Freq. offset: 20 PPM
Channel coding | LDPC
Channel estimation | LS (w/o smoothing)
GI+LTF Size | 4x HE-LTF and 3.2μs GI
Number of transmit antennas (Ntx) | 3, 4, 6, 8
Number of receive antennas (Nrx) | 1, 2
Number of spatial antennas (Nss) | 1, 2
Number of users | 1, 2, 3, 4
Codebook information | Fine codebook
MCS | 2, 4, 6, 8, 10

## Slide 6: PER for SU-MIMO (4 )
Channel B
  Performance is almost same for Ng=4, Ng=16 and Ng=32
Channel D
  Compared with Ng=4, performance loss for Ng=16 is negligible
  Compared with Ng=4, performance loss for Ng=32 is < 0.5dB at PER=0.1
[Channel B]
[Channel D]

## Slide 7: PER for SU-MIMO (4)
Channel B
  Performance is almost same for Ng=4, Ng=16 and Ng=32
Channel D
  Compared with Ng=4, performance loss for Ng=16 is negligible
  Compared with Ng=4, performance loss for Ng=32 is < 1.0dB at PER=0.1
[Channel B]
[Channel D]

## Slide 8: PER for MU-MIMO (4 )
Channel B
  Performance is almost same for Ng=4 and Ng=8
Channel D
  Performance loss for Ng=16 is significantly large, especially for high MCS
  Performance loss for Ng=8 is < 0.5dB at PER=0.1
[Channel B]
[Channel D]

## Slide 9: PER for MU-MIMO (4)
Channel B
  Performance is almost same for Ng=4 and Ng=8
Channel D
  Performance loss for Ng=16 is significantly large, especially for high MCS
  Performance loss for Ng=8 is < 0.5dB at PER=0.1
[Channel B]
[Channel D]

## Slide 10: Feedback overhead reduction for SU
Feedback overhead reduction is approximately same as the CBR size reduction
  CBR size can be calculated by (bits) [1]
  Assuming 8x2, 40MHz, fine codebook, then
    = 26
    = 6, = 4
    = 122, 62, 32, 17 for Ng = 4, 8, 16, 32 respectively
Ng | 4 | 8 | 16 | 32
CBR size (byte) | 1985 | 1010 | 522 | 278
Reduction compared with Ng=4 | 0% | 49% | 74% | 86%

## Slide 11: Summary
In this slide, we propose the subcarrier grouping size (Ng) for 802.11be
  Proposal of Ng for EHT
 | SU | MU
VHT | 1, 2, 4 | 
HE | 4, 16 | 
EHT | 16, 32 | 4, 8
Subcarrier spacing for VHT: 312.5 KHz Subcarrier spacing for HE and EHT: 78.125 KHz |  | 

## Slide 12: Reference
[1] 802.11-20/0566r23, Specification Framework for TGbe.
[2] 802.11-19/0828r4, Feedback Overhead Analysis for 16 Spatial Stream MIMO
[3] “IEEE P802.11ax,” Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications. Amendment 1: Enhancements for High Efficiency WLAN, Feb. 2019.

## Slide 13: SP #1
Do you agree to add the following to the TGbe SFD ?
  802.11be spec shall support Ng = 16, 32 for sounding feedback with SU-MIMO.
  802.11be spec shall support Ng = 4, 8 for sounding feedback with MU-MIMO.
  Y / N / Abstain

## Slide 14: Appendices

## Slide 15: PER for SU-MIMO (6 8

## Slide 16: PER for SU-MIMO (6 8 , )

## Slide 17: PER for MU-MIMO (3 4

## Slide 18: PER for MU-MIMO (3 4