## Slide 1: 2x 320MHz EHT-LTF Design
Date: 2020-08-26
Authors:
Name | Affiliations | Address | Phone | email
Leo Montreuil | Broadcom |  |  | leo.montreuil@broadcom.com
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Introduction
Designing a good sequence with low PAPR for all puncturing cases of 320MHz proves to be a challenge.
[1] and [2] propose a 2x 320MHz LTF design.
Here we propose a set of designs based on new base 80MHz sequences. We have one preferred sequence in the main part of the deck and two more alternatives in the Appendix

## Slide 3: 80 MHz 2x base sequence
LTF80_2x = [ ...
+1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 ...
-1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 ...
+1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 ...
-1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 ...
-1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 ...
+1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 ...
+1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 ...
-1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 ...
+1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 ...
-1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 0 0 ...
0 ...
0 0 0 -1 0 -1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 ...
0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 ...
0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 ...
0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 ...
0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 ...
0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 ...
0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 ...
0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 ...
0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 ...
0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1];
Covering 1001 tones [-500:500] for RU996 in any 80MHz

## Slide 4: 320MHz 2x EHT-LTF
LTF320_2x = [ ...
[C(1)*LTF80_2x(1:245), C(2)*LTF80_2x(246:500), 0, C(3)*LTF80_2x(502:756), C(4)*LTF80_2x(757:1001)], zeros(1,23), ...
[C(5)*LTF80_2x(1:245), C(6)*LTF80_2x(246:500), 0, C(7)*LTF80_2x(502:756), C(8)*LTF80_2x(757:1001)], zeros(1,23), ...
[C(9)*LTF80_2x(1:245), C(10)*LTF80_2x(246:500), 0, C(11)*LTF80_2x(502:756), C(12)*LTF80_2x(757:1001)], zeros(1,23), ...
[C(13)*LTF80_2x(1:245), C(14)*LTF80_2x(246:500), 0, C(15)*LTF80_2x(502:756), C(16)*LTF80_2x(757:1001)] ];
C = [+1 +1 +1 +1, +1 -1 +1 -1, +1 -1 -1 +1, +1 +1 -1 -1];

## Slide 5: Multi-RU PAPR for Nss = 1 to 8
RU size | BPSK | LTF
996 | 8.84 | 6.74
 |  | 7.11
 |  | 7.15
 |  | 6.88
996 + 484 | 9.17 | 7.12
 |  | 7.81
 |  | 7.44
 |  | 7.17
 |  | 7.35
 |  | 7.48
 |  | 7.67
 |  | 7.51
2*996 | 9.27 | 7.45
 |  | 7.07
3*996 (puncture 80MHz) | 9.54 | 7.28
 |  | 7.22
 |  | 7.72
 |  | 7.80
3*996 + 484 (puncture 40MHz) | 9.55 | 7.70
 |  | 8.30
 |  | 7.35
 |  | 7.85
 |  | 8.04
 |  | 7.38
 |  | 8.49
 |  | 8.11
4*996 | 9.60 | 7.04
RU size | BPSK | LTF
2*996 + 484 | 9.50 | 7.96
 |  | 7.92
 |  | 8.32
 |  | 8.11
 |  | 8.09
 |  | 7.33
 | 9.50 | 7.94
 |  | 8.54
 |  | 8.40
 |  | 7.55
 |  | 8.21
 |  | 8.57
 | 9.50 | 8.50
 |  | 9.23
 |  | 8.03
 |  | 7.09
 |  | 8.17
 |  | 8.83
 | 9.50 | 7.99
 |  | 7.75
 |  | 8.08
 |  | 8.16
 |  | 8.26
 |  | 8.02
2*996 discrete | 9.28 | 7.48
 |  | 7.80
 |  | 7.63
 |  | 7.55
RU size | BPSK | LTF
3*996+484+242 (puncture 20MHz) |  | 7.61
 |  | 7.23
 |  | 8.30
 |  | 7.67
 |  | 7.98
 |  | 7.06
 |  | 7.06
 |  | 7.75
 |  | 8.13
 |  | 7.33
 |  | 7.41
 |  | 7.78
 |  | 8.21
 |  | 7.63
 |  | 7.60
 |  | 8.01

## Slide 6: Worst case PAPR for Nss = 1 to 8
Sequence | BPSK Median | Legacy 11ax | Legacy 11ax | [1] LGE M-HE | [2]Opt1 Huawei | [2] New Huawei | BRCM
Tone Plan |  | 11ax | 11be |  |  |  | 
RU26 | 5.89 | 4.46 | 7.95 | 4.46 | 7.95 | 5.26 | 5.30
RU52 | 6.71 | 4.69 | 7.43 | 4.69 | 7.43 | 4.58 | 4.31
RU106 | 7.29 | 5.42 | 6.71 | 5.42 | 6.71 | 5.19 | 4.92
RU242 | 7.94 | 5.58 | 8.23 | 5.58 | 8.23 | 5.42 | 5.14
RU484 | 8.44 | 6.40 | 6.97 | 6.58 | 7.45 | 5.51 | 6.34
RU996 | 8.84 | 6.08 | 6.48 | 9.26 | 8.63 | 5.78 | 7.15
4*RU996 | 9.60 |  |  | 7.79 | 9.59 | 9.07 | 7.04
3*RU996 | 9.54 |  |  | 9.40 | 9.22 | 9.04 | 7.80
3*RU996 + RU484 | 9.55 |  |  | 9.49 | 9.95 | 9.48 | 8.49
2*RU996 + RU484 12 & (24) cases | 9.50 |  |  | 9.61 (9.61) | 10.04 (10.04) | 8.64 (9.15) | 8.32 (9.23)
2*RU996 | 9.27 |  |  | 8.99 | 10.05 | 8.40 | 7.45
2*RU996 discrete | 9.28 |  |  | 9.03 | 9.49 | 8.56 | 7.80
RU996 + RU484 | 9.17 |  |  | 9.12 | 9.98 | 7.52 | 7.81
RU484 + RU242 | 8.83 |  |  | 8.59 | 9.65 | 6.98 | 7.63
RU106 + RU26 | 7.44 |  |  | 6.62 | 7.17 | 5.19 | 6.61
RU52 + RU26 | 7.10 |  |  | 5.94 | 6.37 | 5.98 | 6.78
3*996+484+242 |  |  |  | 8.58 | 10.43 | 9.72 | 8.30
Highest worst case PAPR of each sequence is in RED

## Slide 7: Conclusion
Proposed one sequence with overall lowest maximum PAPR across all cases and very low PAPR for 320MHz

## Slide 8: References
“2x EHT-LTF sequence” 802.11-20/1065r1
“2x EHT-LTFs Sequences Design”, IEEE 802.11-20/1072r2

## Slide 9: SP #1
Do you support the 2x 320MHz LTF sequence described in slides 3 and 4?

## Slide 10: Appendix
Alternative Sequences

## Slide 11: 320 MHz 2x Sequence, Alternative 1
LTF80_2x = [ ...
-1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 ...
+1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 ...
+1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 ...
-1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 ...
+1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 ...
+1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 ...
+1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 ...
+1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 ...
+1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 ...
-1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 0 0 ...
0 ...
0 0 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 ...
0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 ...
0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 ...
0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 ...
0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 ...
0 +1 0 +1 0 +1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 ...
0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 ...
0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 -1 ...
0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 ...
0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1];
LTF320_2x = ...
[ C(1)*LTF80_2x, zeros(1,23), C(2)*LTF80_2x, zeros(1,23), C(3)*LTF80_2x, zeros(1,23), C(4)*LTF80_2x ];
C = [+1, +1, -1, -1];

## Slide 12: 320 MHz 2x Sequence, Alternative 2
LTF80_2x = [ ...
-1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 ...
+1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 ...
-1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 ...
+1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 ...
-1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 ...
-1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 ...
+1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 ...
-1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 ...
-1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 ...
-1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 0 0 ...
0 ...
0 0 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 ...
0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 ...
0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 ...
0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 ...
0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 ...
0 +1 0 +1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 ...
0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 ...
0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 +1 0 -1 0 -1 0 -1 0 +1 ...
0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 +1 0 -1 0 +1 0 +1 0 +1 0 +1 0 +1 0 -1 0 +1 0 +1 0 -1 0 -1 ...
0 -1 0 +1 0 +1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1 0 +1 0 +1 0 -1 0 -1 0 +1 0 -1 0 -1 0 -1 0 -1 0 -1 0 +1 0 -1 0 +1];
LTF320_2x = [ ...
[ C(1)*LTF80_2x(1:500), C(2)*LTF80_2x(501:1001) ], zeros(1,23), ...
[ C(3)*LTF80_2x(1:500), C(4)*LTF80_2x(501:1001) ], zeros(1,23), ...
[ C(5)*LTF80_2x(1:500), C(6)*LTF80_2x(501:1001) ], zeros(1,23), ...
[ C(7)*LTF80_2x(1:500), C(8)*LTF80_2x(501:1001)] ];
C = [+1 +1, -1 +1, +1 +1, +1 -1];

## Slide 13: Worst case PAPR for Nss = 1 to 8
Highest worst case PAPR of each sequence is in RED
Sequence | BPSK Median | Legacy 11ax | Legacy 11ax | [1] LGE M-HE | [2]Opt1 Huawei | [2] New Huawei | BRCM Opt1 | BRCM Opt2
Tone Plan |  | 11ax | 11be |  |  |  |  | 
RU26 | 5.89 | 4.46 | 7.95 | 4.46 | 7.95 | 5.26 | 5.09 | 4.79
RU52 | 6.71 | 4.69 | 7.43 | 4.69 | 7.43 | 4.58 | 4.55 | 4.31
RU106 | 7.29 | 5.42 | 6.71 | 5.42 | 6.71 | 5.19 | 5.10 | 4.92
RU242 | 7.94 | 5.58 | 8.23 | 5.58 | 8.23 | 5.42 | 5.89 | 5.14
RU484 | 8.44 | 6.40 | 6.97 | 6.58 | 7.45 | 5.51 | 5.80 | 5.55
RU996 | 8.84 | 6.08 | 6.48 | 9.26 | 8.63 | 5.78 | 5.60 | 5.89
4*RU996 | 9.60 |  |  | 7.79 | 9.59 | 9.07 | 9.04 | 5.89
3*RU996 | 9.54 |  |  | 9.40 | 9.22 | 9.04 | 9.01 | 8.11
3*RU996 + RU484 | 9.55 |  |  | 9.49 | 9.95 | 9.48 | 9.44 | 8.23
2*RU996 + RU484 12 & (24) cases | 9.50 |  |  | 9.61 (9.61) | 10.04 (10.04) | 8.64 (9.15) | 8.51 (9.11) | 9.68 (9.68)
2*RU996 | 9.27 |  |  | 8.99 | 10.05 | 8.40 | 8.59 | 6.39
2*RU996 discrete | 9.28 |  |  | 9.03 | 9.49 | 8.56 | 8.63 | 8.90
RU996 + RU484 | 9.17 |  |  | 9.12 | 9.98 | 7.52 | 8.06 | 8.25
RU484+RU242 | 8.83 |  |  | 8.59 | 9.65 | 6.98 | 7.84 | 7.69
RU106+RU26 | 7.44 |  |  | 6.62 | 7.17 | 5.19 | 5.80 | 5.58
RU52+RU26 | 7.10 |  |  | 5.94 | 6.37 | 5.98 | 6.64 | 6.44
3*996+484+242 |  |  |  | 8.58 | 10.43 | 9.72 | 10.03 | 7.92