## Slide 1: Discussion on TXOP and BSS Color fields in U-SIG
Date: 2020-08-26
Authors:

## Slide 2: Background
802.11ax defined the TXOP field in the SIG-A field
  TXOP field: 7 bits
    B0 = 0: TXOP_DURATION is less than 512 µsec, 8 µsec resolution
      B1-B6 = floor(TXOP_DURATION/8)
    B0 = 1: TXOP_DURATION is larger than or equal to 512 µsec, 128 µsec resolution
      B1-B6 = floor((TXOP_DURATION-512)/128)
      TXOP_DURATION is limited to 63*128+512 = 8,576 µsec
The Duration field in the MAC header is 15 bits (0-32,767 µsec) and 1 µsec resolution
The current TXOP field defined in 802.11ax doesn’t fully represent TXOP_DURATION
802.11be defined U-SIG for better coexistence with future gen. of 802.11 and the TXOP field needs to be improved to support better coexistence

## Slide 3: Example using the current TXOP field for a future generation of 802.11
EHT STA can only decode the TXOP field of EHT+ PPDU (future gen. 802.11)
There could be max 128 µsec difference between TXOP_DURATION and TXOP
128 µsec less protection could cause collision
EHT+ PPDU
EHT+ PPDU
TXOP_DURATION >512 µsec
STA1(EHT+)
STA2(EHT+)
STA3(EHT)
- Blind to STA2
Defer: L-SIG (Length)
This might cause collision at STA1
TXOP (7-bit)
Defer: TXOP
EHT PPDU
Difference between TXOP_DURATION and TXOP (max 128 µsec)
STA1
STA2
STA3
TXOP

## Slide 4: Finer time resolution for TXOP field in U-SIG
We suggest a finer time resolution for the TXOP field for better coexistence support
  8 µsec resolution
In the latest draft of the 5GHz spec in ETSI (BRAN-230016), COT (channel occupancy time) could be up to 10ms
  Most likely these values will also be applied to the 6GHz spec
Proposed size and resolution of the TXOP field in U-SIG
  Extend to 11-bit with 8 µsec resolution: represents 0-16376 µsec TXOP_DURATION
    Current discussion in PHY group [11-20/1238r0]: 6 reserved bits available in the Version Dependent section in U-SIG; 4 bits can be moved to the Version Independent section.
  B0-B10 = floor(TXOP_DURATION/8)

## Slide 5: Example using TXOP field with 8 µsec resolution
EHT STA can only decode the TXOP field of EHT+ PPDU (future gen. 802.11)
There could be max 8 µsec difference between TXOP_DURATION and TXOP
No collision issue
EHT+ PPDU
EHT+ PPDU
TXOP_DURATION
STA1(EHT+)
STA2(EHT+)
STA3(EHT)
- Blind to STA2
Defer: L-SIG (Length)
TXOP (11-bit)
Defer: TXOP
EHT PPDU
Difference between TXOP_DURATION and TXOP (max 8 µsec)
STA1
STA2
STA3
TXOP

## Slide 6: BSS Color field
Current BSS Color field in 11ax is 6 bits: 1-63
If APs randomly select their BSS color value, the collision probability (at least two APs using the same color) is quite high:
  50% collision prob. with 9 co-channel APs
  20% collision prob. with 5 co-channel APs
  10% collision prob. with 4 co-channel APs
Increasing BSS Color field to 8 bits reduces collision probability:
  10% collision prob. with 8 co-channel APs
If APs select BSS color more intelligently (i.e. selecting a value that is not used by other co-channel APs), this BSS collision issue could be mitigated and may not need to increase BSS Color field

## Slide 7: Summary
TXOP field in U-SIG
  For better coexistence support and the latest draft of the 5 GHz spec in ETSI, we recommend to use 11-bit with 8 µsec time resolution to represent TXOP_DURATION = 0… 16376 µsec
BSS Color field in U-SIG
  Current 6-bit seems to be okay if BSS color is chosen intelligently
  If we want to reduce collision probability for the case of random selection, the BSS Color field could be extended to 7 or 8 bits.

## Slide 8: SP
Do you support the size of the TXOP field in U-SIG to be 11 bits?
TXOP field = floor(TXOP_DURATION/8)
TXOP field represents TXOP_DURATION = 0… 16376 µsec