## Slide 1: EHT Pre-FEC Padding and Packet Extension
Date: 2020-08-26
Authors:

## Slide 2: Introduction
Discuss about EHT FEC padding and packet extension.
  EHT uses the same OFDM numerology as 11ax.
  Prefer to keep the same FEC padding and packet extension (PE) procedure.
Updates needed for EHT:
  Pre-FEC padding parameters for MRUs and wider BW
  Maximum allowed PE for new BW/Nss/QAM.

## Slide 3: Recap: HE PPDU Padding Procedure
Two step FEC padding:
  Pre-FEC padding to the closest quarter symbol: “a” factor.
  Post-FEC padding to 4x symbol boundary.
Packet extension to allow more receiver processing time.
PE

## Slide 4: EHT PPDU Padding
EHT can keep the same two-step padding procedure.
  pre-FEC padding factor is computed from APEP_LENGTH.
  NDBPS for new BW and MRUs are already agreed on.
  NDBPS,short need to be updated for new BW/MRUs and DUP mode.
NSD, short definition general goals:
  close to one quarter of to minimize Npad and
  meet integer NDBPS requirements

## Slide 5: NSD,short Table
RU Size | NSD | NSD,short | 
 | DCM=0 | DCM=0 | DCM=1
26 | 24 | 6 | 2
52 | 48 | 12 | 6
52+26 | 72 | 18 | 8
106 | 102 | 24 | 12
106+26 | 126 | 30 | 14
242 | 234 | 60 | 30
484 | 468 | 120 | 60
484+242 | 702 | 180 | 90
996 | 980 | 240 | 120
996+484 | 1448 | 360 | 180
996+(484+242) | 1682 | 420 | 210
2x996 | 1960 | 492 | 246
2x996+484 | 2428 | 612 | -
3x996 | 2940 | 732 | 366
3x996+484 | 3408 | 852 | -
4x996 | 3920 | 984 | 492

## Slide 6: Notes on NSD,short Table
MRU:
  Nsd,short = sum of Nsd,short of component RUs
For MCS0+DCM+EHT DUP
  MCS0+DCM is applied for each half BW.
  Nsd,short is defined as the Nsd,short for BW/2 with DCM.
  Example:
    320MHz MCS0+DCM+EHT DUP: Nsd,short for 996*2 with DCM.
    160MHz MCS0+DCM+EHT DUP: Nsd,short for 996 with DCM.
    80MHz MCS0+DCM+EHT DUP: Nsd,short for 484 with DCM.

## Slide 7: Recap: HE Packet Extension
Maximum nominal PE is 16us.
Nominal TPE is determined based on “a” factor and receiver’s nominal packet padding.

## Slide 8: EHT Packet Extension
Follow the same HE approach to determine nominal TPE
  based on “a” factor and receiver’s nominal packet padding.
EHT maximum nominal TPE
  EHT allows wider BW, more Nss and higher QAM.
    Receiver needs to finish decoding each data symbol within symbol time.
  No need to increase the maximum PE in general.
    Additional processing latency may be needed for preamble for some new higher throughput modes.
  Can define one longer PE to account only for the new modes.
  No need for 11ax allowed modes, as HE PPDU has to satisfy 16us limit.

## Slide 9: Maximum PE values
11ax PE disambiguity calculation
  PE disambiguity bit is set to 1 if the above equation satisfies.
  If we increase max TPE values, the PE disambiguity bit is valid until
  With 1-bit ambiguity, longer PE is allowed for different Tsym, i.e. different GI:

## Slide 10: EHT max PE and Disambiguity
EHT PE can keep the same 1-bit ambiguity signaling
Define one longer PE = 20us to allow some design flexibility for new modes, like 320MHz, 16ss, etc.
  Not to sacrifice the PE efficiency for 11ax allowed rates.
Proposal:
  Allow max TPE=16us for RU<=996*2, Nss<=8 and M<=1024.
  Allow max TPE=20us for other cases.
Tsym | Allowed max PE
12.8+0.8 us | 20us
12.8+1.6 us | 24us
12.8+3.2 us | 28us

## Slide 11: Nominal Packet Padding Capability
Keep definition of 0~2, and redefine value 3 as:
  16us for [constellation<=1024QAM, Nss<=8, RU<=996*2].
  20us PE for all other modes.
Nominal Packet Padding | Encoding
0 | Set to 0 if the nominal packet padding is 0 μs for all constellations, NSS and RU allocations the STA supports.
1 | Set to 1 if the nominal packet padding is 8 μs for all constellations, NSS and RU allocations the STA supports.
2 | Set to 2 if the nominal packet padding is 16 μs for all constellations, NSS and RU allocations the STA supports.
3 | Reserved Set to 3 if the nominal packet padding is 16 μs for all modes with constellation<=1024, NSS<=8 and RU<=996*2, and 20us for all other modes the STA supports.

## Slide 12: TPE for EHT NDP
HE NDP PPDU uses fixed 4us TPE.
EHT NDP
  Keep 4us for BW<=160MHz and Nss<=8.
  Use 8us for BW>160MHz or Nss>8 to allow more turnaround time.

## Slide 13: Summary
Propose EHT to reuse basic procedure of HE FEC padding and packet extension.
Update NDBPS,short for new BW/MRUs and DUP mode.
Define 20us PE for large [RU, Nss, QAM] modes to allow some flexibility in product design.
Use longer PE for EHT NDP with large [BW, Nss].

## Slide 14: SP1
Do you agree that EHT uses the same two-step padding procedure as 11ax? i.e.
  pre-FEC padding to one of the four pre-FEC padding boundary.
  Post-FEC padding to the OFDM symbol boundary.
  Y
  N
  A

## Slide 15: SP2
Do you agree that the NSD,short is defined as in the following table:
RU Size | NSD,short | 
 | DCM=0 | DCM=1
26 | 6 | 2
52 | 12 | 6
52+26 | 18 | 8
106 | 24 | 12
106+26 | 30 | 14
242 | 60 | 30
484 | 120 | 60
484+242 | 180 | 90
996 | 240 | 120
996+484 | 360 | 180
996+(484+242) | 420 | 210
2x996 | 492 | 246
2x996+484 | 612 | -
3x996 | 732 | 366
3x996+484 | 852 | -
4x996 | 984 | 492
  For EHT PPDU of X MHz modulated with MCS0+DCM+EHT DUP, uses the Nsd,short values for RU size corresponding to X/2 MHz and with DCM=1.
  X = 80 or 160 or 320.

## Slide 16: SP3
Do you agree that the duration of PE field in EHT MU PPDU may take value of 20us for any modes with constellation>1024 or NSS>8 or RU>996*2?
  Y
  N
  A

## Slide 17: SP4
Do you agree that EHT Nominal Packet Padding has two capability bits, defined as follows?
  Y N
  A
Nominal Packet Padding | Encoding
0 | Set to 0 if the nominal packet padding is 0 μs for all constellations, NSS and RU allocations the STA supports.
1 | Set to 1 if the nominal packet padding is 8 μs for all constellations, NSS and RU allocations the STA supports.
2 | Set to 2 if the nominal packet padding is 16 μs for all constellations, NSS and RU allocations the STA supports.
3 | Set to 3 if the nominal packet padding is 16 μs for all modes with constellation<=1024, NSS<=8 and RU<=996*2, and 20us for all other modes the STA supports.

## Slide 18: SP5
Do you agree that the TPE value for EHT sounding NDP is
  4us for BW<=160MHz and Nss<=8
  8us, otherwise
  Y
  N
  A