## Slide 1: Discussion on EHT Sounding Feedback Request Parameters
Date: 19-08-2020
Authors:
Name | Affiliation | Address | Phone | Email
Genadiy Tsodik | Huawei Technologies |  |  | 
Shimi Shilo |  |  |  | 
Oded Redlich |  |  |  | 

## Slide 2: Introduction
802.11be increases maximum throughput (increasing MCS, Nss and BW( which requires to update both feedback request and feedback response parameters
For example, it was already accepted to extend the number of columns in feedback (Nc) up to 16 [1]
In this contribution we review additional parameters and suggest the required extension or modification of existing fields

## Slide 3: Parameters to review
Three fields indicated in STA Info Subfield, as defined in 11ax, should be reviewed with respect to 802.11be requirements:
  Feedback Type and Ng
  Codebook Size
  Partial BW Info – this field is not discussed in this contribution
We examined different scenarios introduced by 802.11be with respect to Ng values and Codebook Size
In the next slides we will present simulation results and our suggestions for Ng value and Codebook Size in 802.11be

## Slide 4: Subcarrier Grouping - Ng
802.11ax introduced two possible values of subcarrier grouping: Ng=4 and Ng=16
Larger Ng values allow smaller feedback size but provide a less accurate precoder (and hence degrade performance)
SU case
  In [2] a throughput analysis was presented, showing that for the SU case feedback reduction results in very small throughput gain
  Thus we see no motivation to change/extend Ng values for SU case
MU case
  Involving multiple STAs in sounding procedure may lead to very large feedback size
  On the other hand, MU case requires a more accurate precoder
  Hence we simulate and analyze the MU case

## Slide 5: Simulation Parameters - Ng
We compared the performance of both Ng (4 and 16) values in different scenarios, focusing on MU-MIMO
Although cases with a small number of antennas (< 8) are not relevant for feedback size reduction (no change from 802.11ax), we still simulated them to get a better understanding of achievable performance
Simulation parameters are:
  4/8/16 Tx antennas
  2/3/4 STAs with 1SS each (BF size per STA is 4x1, 8x1, 16x1)
  6 STAs with 2SS each (total of 12SS)
  TGn-D NLOS
  Practical CHEST
  MCS 4/6/8/10
  No Compression of feedback precoder

## Slide 6: Simulation Results - 4 Tx Antennas

## Slide 7: Simulation Results – 8/16 Tx Antennas
8 Tx Ant,
4 STA
16 Tx Ant,
4 STA
8/16 Tx Ant,
6 STA, 6SS in Total
16 Tx Ant,
6 STA, 12SS in Total

## Slide 8: Ng Values - Conclusions
The simulations reveal that:
  Ng = 16 provides reasonable performance degradation (and no error floor) in most simulated scenarios
  Larger number of antennas decreases the degradation caused by Ng=16, and for 16 Tx antennas the gap is very small (even for large MU-MIMO with 12SS total)
  Ng = 8 also yields some performance degradation in scenarios with a larger number of Tx antennas (cannot be considered as an alternative for Ng = 4)
Based on these results we conclude the following:
  Ng = 16 may be used for many practical cases, such as smaller MU-MIMO groups, low and mid MCS values
  Larger MIMO schemes (more relevant for 11be) require Ng=4 to achieve desired performance
  Ng=16 may still be applied for MU-MIMO grouping algorithms where the accuracy of the precoder has little impact on the grouping algorithm (this allows to collect feedback from many STAs with lower feedback overhead)
Thus following the above we suggest to reuse Ng values defined in 11ax
  For SU and MU Feedback types, Ng = 4 and Ng = 16 may be used

## Slide 9: Codebook Size
802.11ax supports two codebook size values per feedback type
  (2,4) and (4,6) bits for SU feedback type
  (5,7) and (7,9) bits for MU feedback type
We examined different codebook size valuess (including un-supported sizes of (8, 10) and (9,11) bits) in typical and extreme scenarios introduced by 802.11be, including high MCS and large MU-MIMO cases
Simulation parameters:
  Codebook size: (5,7), (7,9), (8,10) and (9,11)
  TGn-D NLOS
  16Tx Ant
  2/4/6/8 STAs
  Nss =2/4
  Practical CHEST
  Extreme Cases:
    4 STAs, Nss = 4 (16SS total)
    6 STAs, Nss = 2 (12SS total) MCS11

## Slide 10: Simulation Results
Total Nss = 8 (50%)
Total Nss = 12 (75%)
Total Nss = 16 (Full Rank)
Total Nss = 16 (Full Rank)

## Slide 11: Simulation Results – Extreme Scenarios
Total Nss = 16 (Full Rank)
Total Nss = 12 (75%)
MCS11

## Slide 12: Codebook Size – Conclusions
From the simulation results we can see that for full rank MU-MIMO cases or high MCS with total Nss equal to 75% of Tx antennas, a codebook size of (7,9) bits results in non-negligible performance degradation
A codebook size of (9,11) bits provided no performance degradation for all the scenarios whereas codebook size of (8,10) slightly degrades the performance in full rank MU-MIMO
The performance gain of codebook size (9,11) yields higher goodput (taking into account the higher respective overhead)
For example, in case of 8 STAs, the PER is reduced from 0.1 to 0.05, which means (assuming 30msec sounding period) that we save ~1.5msec of retransmission time by increasing the feedback size by ~400usec
Thus, following those above, we suggest to support a codebook size of (11,9) bits for MU feedback type in addition to existing codebook sizes

## Slide 13: Proposed Changes in STA Info Subfield
Following our suggestions we propose to extend Codebook Size field in STA Info Subfield by one bit
The proposed change in Table 9-31a for indication of Feedback Type and Ng and Codebook Size will be as following (when B0 is ‘0’ original settings are preserved )
Codebook Size
Bits
2
B0 B1
Feedback Type and Ng |  | Codebook Size |  | Description
B0 | B1 | B0 | B1 | 
0 | 0 | 0 | 0 | SU, Ng = 4, quantization resolution (ϕ,φ) = {4,2}
0 | 0 | 0 | 1 | SU, Ng = 4, quantization resolution (ϕ,φ) = {6,4}
0 | 1 | 0 | 0 | SU, Ng = 16, quantization resolution (ϕ,φ) = {4,2}
0 | 1 | 0 | 1 | SU, Ng = 16, quantization resolution (ϕ,φ) = {6,4}
1 | 0 | 0 | 0 | MU, Ng = 4, quantization resolution (ϕ,φ) = {7,5}
1 | 0 | 0 | 1 | MU, Ng = 4, quantization resolution (ϕ,φ) = {9,7}
1 | 1 | 0 | 0 | CQI
1 | 1 | 0 | 1 | MU, Ng = 16, quantization resolution (ϕ,φ) = {9,7}
1 | 0 | 1 | 1 | MU, Ng = 4, quantization resolution (ϕ,φ) = {11,9}
1 | 1 | 1 | 1 | MU, Ng = 16, quantization resolution (ϕ,φ) = {11,9}
Other |  |  |  | Reserved

## Slide 14: Proposed Changes in EHT MIMO Control
Similar to the previous slide we suggest to extend Codebook Information field size by one bit
The proposed change in Table 9-93a for indication of Codebook Information will be as following (when B0 is ‘0’ original settings are preserved )
Codebook Information | Indicates the size of codebook entries. If the Feedback Type subfield indicates SU: Set to 00 for 4 bits for ϕ and 2 bits for ψ Set to 01 for 6 bits for ϕ and 4 bits for ψ If the Feedback Type subfield indicates MU: Set to 00 for 7 bits for ϕ and 5 bits for ψ Set to 01 for 9 bits for ϕ and 7 bits for ψ Set to 10 for 11 bits for ϕ and 9 bits for ψ Set to 11 Reserved If the Feedback Type subfield indicates CQI, then the Codebook Information subfield is reserved. NOTE—The codebook size for MU Feedback with Ng = 16 is limited to (ϕ, ψ) = {9, 7} or {11,9}
Codebook
Information
Bits
2
B0 B1

## Slide 15: Summary
We examined 802.11be supported schemes with respect to Ng values and Codebook Size
Based on simulation results we proposed to preserve existing Ng values and codebook sizes and to add a new codebook size of (9,11) bits
Following those suggestions, we proposed the relevant changes in STA Info Subfield and EHT MIMO Control Field
We preserve the existing definitions and add new options by extending Codebook Size and Codebook Information fields by one bit

## Slide 16: References
[1] 11-20-0566-54-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-19-1495-02-00be-further-discussion-on-feedback-overhead-reduction

## Slide 17: SP1
Do you agree to support Ng values defined in 802.11ax?
  Ng = 4 and Ng = 16 for SU and MU feedback type

## Slide 18: SP2
Do you agree to support to add a new codebook size of (9,11) bits for MU feedback type?
  Note: the codebook sizes defined by 802.11ax will also be supported

## Slide 19: SP3
Do you agree to extend Codebook Size field in STA Info Subfield by 1 bit and update the table 9-31a as defined in slide 13?
Codebook Size
Bits
2
B0 B1
Feedback Type and Ng |  | Codebook Size |  | Description
B0 | B1 | B0 | B1 | 
0 | 0 | 0 | 0 | SU, Ng = 4, quantization resolution (ϕ,φ) = {4,2}
0 | 0 | 0 | 1 | SU, Ng = 4, quantization resolution (ϕ,φ) = {6,4}
0 | 1 | 0 | 0 | SU, Ng = 16, quantization resolution (ϕ,φ) = {4,2}
0 | 1 | 0 | 1 | SU, Ng = 16, quantization resolution (ϕ,φ) = {6,4}
1 | 0 | 0 | 0 | MU, Ng = 4, quantization resolution (ϕ,φ) = {7,5}
1 | 0 | 0 | 1 | MU, Ng = 4, quantization resolution (ϕ,φ) = {9,7}
1 | 1 | 0 | 0 | CQI
1 | 1 | 0 | 1 | MU, Ng = 16, quantization resolution (ϕ,φ) = {9,7}
1 | 0 | 1 | 1 | MU, Ng = 4, quantization resolution (ϕ,φ) = {11,9}
1 | 1 | 1 | 1 | MU, Ng = 16, quantization resolution (ϕ,φ) = {11,9}
Other |  |  |  | Reserved

## Slide 20: SP4
Do you agree to extend Codebook Information field in EHT MIMO Control Field by 1 bit and update the table 9-93a as defined in slide 14?
Codebook Information | Indicates the size of codebook entries. If the Feedback Type subfield indicates SU: Set to 00 for 4 bits for ϕ and 2 bits for ψ Set to 01 for 6 bits for ϕ and 4 bits for ψ If the Feedback Type subfield indicates MU: Set to 00 for 7 bits for ϕ and 5 bits for ψ Set to 01 for 9 bits for ϕ and 7 bits for ψ Set to 10 for 11 bits for ϕ and 9 bits for ψ Set to 11 Reserved If the Feedback Type subfield indicates CQI, then the Codebook Information subfield is reserved. NOTE—The codebook size for MU Feedback with Ng = 16 is limited to (ϕ, ψ) = {9, 7} or {11,9}
Codebook
Information
Bits
2
B0 B1