## Slide 1: Access mechanisms to meet the requirements of low latency traffics
Date: 2020-08-31
Authors:
Name | Affiliations | Address | Email
Boyce Bo Yang | Huawei | Nanjing, China | yangbo59@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Wayne Wei Qiu |  | Nanjing, China | wayne.qiuwei@huawei.com
Notes: September 2012

## Slide 2: Introduction
Latency is critical important for some traffics.
  NS/EP service is agreed to be supported in 11be which requires guaranteed transmission even in worst cases[1].
  Emerging services like online gaming, realtime video, industrial automation are also sensitive to latency[2]
In one-hop WLAN systems, latency is mainly consist of buffer delay, channel access delay, retransmission delay
  buffer delay is highly related to the rate gap between backhaul and WLAN air links, which can be greatly alleviated by high throughput feature in 11be.
  Channel access delay is challenging for realtime applications in some cases, and requires some new mechanisms in 11be.
  Retransmission delay is also highly related to channel access delay.
This contribution provides a resource reservation method offering a access ‘window’ to improve access delay performance.

## Slide 3: Challenges for low latency traffic
Large access delay is even worse than packet failure
  The transmitter can retransmit failed packet with lower MCS
  The transmitter have nothing to do but wait, if it is unable to get access to the channel
    Note: collision contributes to large access delay
EDCA based mechanism has good delay performance in most cases. However, in case of heavy congestion, access delay could be very large
Simulation setup
 | Lowlatency | Regular
User Num | n | 10*n
EDAC para | VO | BE
PPDU Length | 400us | 4ms
Retran delay | 300us | 300us

## Slide 4: Component mechanisms for low latency traffic transmission
Description of low latency traffic
  How to differentiate low latency traffics from regular traffics (new TID mapping?)
  How to label traffic requirements by means of access priority(TSPEC, new AC?)
Notification of priority access by non-AP STA
  non-AP STA need a mechanism to notify AP of the start or end of uplink time sensitive traffics
Access mechanisms to meet the requirements of low latency traffics
  How to improve the access mechanism.
  Requirements:
    Worst case performance improvement
    Almost guaranteed maximum access delay
    Little influence on regular traffic
    Little changes for STAs not supporting low latency traffics

## Slide 5: Basic IDEAs
In case of heavy congestion, AP should be able to assign some dedicated resources for critical communications
  An dedicated resource is an time-frequency resource where none but some specified traffic is allowed to transmit.
  Reservation of resources for some specified traffic can be announced using a new element in Beacon or Probe Response frames
  STAs without the specified traffic shall not transmit on reserved resources
  STAs with the specified traffic are allowed to transmit on reserved resources
  Transmissions of any PPDU but those containing the specified traffic shall complete before the start of reserved resources.
  This would create a much less congested channel access window for critical communications.

## Slide 6: Illustrations and Notes
Channel access on reserved resources could be EDCA based or other protocols.
The following information is need in the new defined element
  Type of traffics allowed to be sent on reserved resources, RR offset, RR interval, RR duration, RR period
The resource reservation is setup and released dynamically according to link status and traffic buffer status.
  For a AP MLD, resource reservation can be setup on one link only
Identification/notification of traffics that requires resource reservation is out of scope of this contribution:
  Similar topics are under discussion by many contributions[3][4][5]
TBTT
TBTT
EDCA based access for all traffics
Reserved for specified traffic
Interval
Duration
Offset

## Slide 7: Application Examples
Resource reservation for low latency and NS/EP traffics
Resource reservation for AP coordinated transmission
AP MLD 1
AP MLD 2
AP coordinated transmission
Interference to AP coordinated transmission
Ch36
Ch149
Ch149
Ch52
Note: Alignment of reserved resources might be needed for multi-APs which can be easily achieved in AP coordination

## Slide 8: Influence on regular traffics
Efficiency of regular traffics would be degraded because the channel is even more congested
  The cost paid to support higher priority traffics can be reduced by dynamic setup and release.
  The scheduling algorithm in AP should decide whether to setup/release the resource reservation which is out of scope of 11be.
  In case of heavy congestion, it’s worthwhile to satisfy QoS of some traffic with minor cost.
Regular traffics may be allowed to be sent with a lower priority depending on the access mechanism adopted on reserved resources. For example
  EDCA based access mechanism: regular traffic can access channel with a low-priority set of EDCA parameters(e.g. a very large AIFSN and CWmin)
  Trigger based access mechanism: regular traffic are schedule only if there is no low latency traffics to be sent.

## Slide 9: Coexistence with Pre-EHT STAs
In a actual WLAN network, both EHT and pre-EHT STAs may exist. It’s not fair to mute EHT STAs only.
Quiet element can be used with a new defined resource reservation element when both EHT and pre-EHT STAs need to be muted.
  Multiple Quiet elements can setup/release reserved resources a shown in previous pages
  Resource reservation element is used to notify EHT STA which traffic is allowed to transmit
  Pre-EHT STAs are muted by Quiet elements
  EHT STAs without the traffic specified in RR element are also muted
  EHT STAs with the traffic specified in RR element are can access channel to transmit the specified traffic
Resource reservation element should have a short variant when used together with quiet elements
  STAs can obtain the information(like resource reservation period, offset, interval, duration) from quiet elements. It would be redundant to include those information in resource reservation element.

## Slide 10: Summary
A resource reservation mechanism is proposed to improve delay performance in heavy congestion cases.
  Reservation of resources can be announced using a resource reservation element in Beacon or Probe Response frames
  The resource reservation mechanism supports transmission of multiple low-latency traffics with different delay requirements.
  Any access mechanism is supported on reserved resources.
  Influence on regular traffics is very little and can be reduced by dynamic setup and release
  Latency performance would not be degraded with the existence of pre-EHT STAs

## Slide 11: Straw Poll 1
Do you agree that 11be introduces a resource reservation mechanism allowing only specified traffic being sent on reserved resources.
Note:
  The resource reservation can be setup and released dynamically using a new element in Beacon or Probe Response frames.

## Slide 12: Straw Poll 2
Do you agree that 11be introduces a resource reservation element including the following information.
  Type of traffics allowed to be sent on reserved resources
  Resource reservation period
  Resource reservation offset
  Resource reservation interval
  Resource reservation duration
Note:
  The description/identification of traffics allowed to be sent on reserved resources is TBD.

## Slide 13: References
[1] 11-20-0566-59-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-20-0566-59-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[3] 11-20-0418-03-00be-low-latency-service-in-802-11be
[4] 11-20-1006-01-00be-new-methods-to-meet-low-latency-requirements
[5] 11-20-1067-00-00be-traffic-indication-of-latency-sensitive-application

## Slide 14: Backup

## Slide 15: Definition of Delays in slide 2
  Buffer Delay (MSDU based)
    Buffer delay is measured from the time the MSDU is passed to MAC until the point at which the corresponding MPDU/trigger starts EDCA access (i.e. set backoff counter).
    Buffer delay consist of the time in DDR waiting for scheduling, scheduling time, the time waiting in AC queue
  Channel access delay(MPDU based)
    Channel access delay is measured from the time the EDCAF begins CSMA/CS access until the actual frame transmission start time.
  Retransmission delay(MPDU based)
    Retransmission delay depends on the scheduling algorithm in AP
    Retransmission delay is approximately the sum of retransmission scheduling delay and channel access delay

## Slide 16: Discussion on Low latency features in 11be
The standard (i.e. 11be) can provide not any guaranteed QoS of Low latency traffic but a supportive mechanism.
  The implementation specific algorithms are responsible for the QoS performance which seems to be extremely difficult, if not impossible, under current EDCA channel access mechanism
Guaranteed access delay is not a deterministic delay but a high probabilistic delay.
  The numerical delay bound guaranteed by an AP is a implementation related parameter, which depends on the scheduling algorithms adopted.
    For example, an AP may provide access delay up bound 10ms with 90% and 50ms with 99.9%
    Note that: the description is related to reliability as well. Since reliability is also related to MCS selection, ARQ, TX power adaptation, etc, we should focus on delay of a single access.

## Slide 17: data cursor for simulations results on access latency under EDCA
 | 10%ile (ms) | 1%ile (ms) | 0.1%ile (ms)
1-10 | 12.56 | 25.41 | 41.64
2-20 | 14.54 | 31.85 | 50.58
3-30 | 17.29 | 30.04 | 56.55
4-40 | 20.59 | 43.26 | 66.56
5-50 | 26.57 | 54.93 | 84.07
6-60 | 34.7 | 70.68 | 106.5
7-70 | 44.9 | 91.39 | 136.3
8-80 | 58.45 | 117.4 | 176.1
9-90 | 74.96 | 151.1 | 226.5
Note that: access delay shown here only count low latency traffic.

## Slide 18: Discussion of resource reservation
  Resources reserved for specified STA or specified Traffic?
    QoS mechanisms should be designed based on traffics not devices
      If a STA has more than one type of traffic, it’s not right to let a low priority traffic (e.g. downloading) have same QoS as high priority traffic (e.g. online game)
    Very limited types of traffics vs variable number of STAs
      A STA has at least one type of traffic, so the number of types is smaller than that of STAs. The notification procedure would be simpler and less cost.
    For STAs having more than one priority access traffics (different delay requirements), it is very difficult to use device based resource reservation to handle this.
      For example, a STA has 2 traffics whose access delay requirements are 20ms and 100ms respectively. Both traffics need 1ms to transmit
      The STA needs 2 different reserved resources which is actually traffic based.
    For non-periodic traffics, statistic multiplexing can be used for traffic based resource reservation to improve channel efficiency.
      Periodic resource reservation can be setup based on concurrency rate of the specified traffic over all STAs

## Slide 19: Alignment of reserved resources for M-AP
Hidden node problem would be very serious in case of AP-AP communication. Resource reservation can be used to mute STAs during AP-AP transmission. In this case, the reserved resources need to be aligned between 2 or more BSS. The TBTTs of multiple AP can be set as follows to avoid Beacon collisions.
AP1
AP2
AP1
AP2
Option 1
Option 2
Reserved Resources
Beacon
Note that: the exact strategy adopted by AP is implementation dependent.

## Slide 20: Quiet element for resource reservation
TBTT
Duration
Offset
Period (=1)
Multiple Quiet elements and one short resource reservation element can setup multiple reserved resources as follows
Note that: For scenarios with no pre-EHT STAs, one resource reservation element can setup multiple reserved resources as well.