## Slide 1: On TBD MCSs
Date: 2020-05-28
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com

## Slide 2: Passed Motions related to MCSs
802.11be shall define 4096 QAM as one of the optionally supported modulations. [Motion 111, #SP0611-21, [13] and [31]]
DCM+MCS0 for Nss=1 as defined in 802.11ax is a MCS in 802.11be.
  The detailed MCS number for DCM+MCS0 is TBD.
  This is an R1 feature.
  [Motion 112, #SP147, [8] and [36]]

## Slide 3: Passed Motions related to MCSs
802.11be agrees to define a DUP mode for non-punctured 80 MHz, 160 MHz and 320 MHz PPDUs transmitted to a single user, limited to {MCS0+DCM, Nss=1}.
  80 DUP = 40 (RU 484) duplicated.
  160 DUP = 80 (RU 996) duplicated.
  320 DUP = 160 (RU 2×996) duplicated.
  PAPR reduction scheme is TBD. Additional diversity scheme is TBD.
  This is an R1 feature.
  The mode defined above is limited to 6 GHz.
  Note: Whether to further limit this to LPI mode is TBD.
    The duplication in the mode defined above is done only on the data tones of the payload portion and that EHT-STF/LTF are based on the total BW.
  [Motion 122, #SP162, [8] and [37]]
  [Motion 122, #SP163, [8] and [37]]
  [Motion 122, #SP170, [8] and [38]]

## Slide 4: MCSs
We propose that for 4096QAM, only coding rates ¾ and 5/6 shall be included in IEEE 802.11be.
We propose to define the following MCSs:
  MCS12: 4096-QAM with ¾ coding rate
  MCS13: 4096-QAM with 5/6 coding rate
  MCS14: MCS0 + DCM + EHT Dup
  MCS15: MCS0 + DCM
The rational for MCS 14 and MCS 15 is
  In two’s complement, MCS0+DCM as MCS 15 is MCS -1.
  In two’s complement, MCS0 + DCM + EHT Dup as MCS 14 is MCS -2.

## Slide 5: Straw Poll #1
Do you agree to define the following MCSs in IEEE 802.11be?
  MCS14: BPSK+1/2 rate coding + DCM + Dup
  MCS15: BPSK+1/2 rate coding + DCM
  Theses MCSs are only applicable to NSS=1.