## Slide 1: Multi-Link Probe Request Design
Date: 2020-09-14
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
We discuss multi-link discovery in this contribution.
There are two kinds of discovery methods defined in the 802.11 SPEC
  Passive scanning: STA receives a Beacon frame which carries the complete information of a BSS
  Active scanning: STA transmits a probe request frame to solicit the complete information of one or more BSSes
In MLO, the Beacon frame may not carry the complete information of all links to avoid Beacon bloating.
  Motion 115, #SP93: 802.11be shall define mechanism(s) for an AP of an AP MLD to advertise complete or partial information of other links:
    • Partial information to prevent frame bloating.
    • For example, frames exchanged during ML setup are expected to carry complete information while Beacon frame is expected to carry partial information.
In that case, a non-AP MLD needs to transmits a probe request frame to solicit complete information of a AP MLD

## Slide 3: MLD based or Link based
Motion 119, #SP109
  802.11be agrees to define a mechanism for a STA of a non-AP MLD to send a probe request frame to an AP belonging to an AP MLD, which enables to request a probe response from the AP that includes the complete set of capabilities, parameters and operation elements of other APs affiliated to the same MLD as the AP
    The complete information is defined as all elements that would be provided if the reported AP was transmitting that same frame (exceptions TBD).
    It is TBD if the AP is mandated or not to respond with the requested information.
    Note: Such a directed probe request requesting complete MLO information for one or more APs of the MLD is referred to as an ML probe request.
    Note: A probe response sent in response to an ML probe request containing complete MLO Information for the requested AP(s) is referred to as an ML probe response
Question: Is the requested information MLD based or Link based?
  Opt 1 (MLD based): we only allow the non-AP MLD to probe the complete information of the whole AP MLD
  Opt 2 (Link based): we allow the non-AP MLD to probe only a subset of the supported links
We believe opt 2 is better, because
  The non-AP MLD may already know the complete information of some links, e.g.,
    By scanning on those links previously
    The non-AP MLD was associated on some links, and now wants to connect on a new link
    …

## Slide 4: Probe for multiple BSSID
Another aspect is the multiple BSSID case
Multiple virtual MLDs may be collocated in the same physical device
A non-AP MLD should be able to probe all or parts of the collocated/cohosted MLDs
  Those APs are reported in the RNR without complete information
Link 1
Link 2
Link 3
MLD 1
MLD 2
MLD 3
MBSSID1
MBSSID2
MBSSID3

## Slide 5: Probe for partial information
It is agreed that the non-AP MLD can request partial information of the AP MLD
  Passed SP: A STA of a non-AP MLD can request a peer AP of AP MLD a part of complete information of other APs of the same AP MLD [1]
The non-AP MLD may only wants to know specific IEs of other APs of the AP MLD

## Slide 6: Motivation
According to the previous discussion, the ML probe request should be able to
  Probe the complete information of an AP MLD
  Probe the complete information of specific links of an AP MLD
  Probe the complete information of multiple AP MLDs
  Probe partial information of each AP of an AP MLD
In this contribution, we propose a unified design to serve the above purpose.

## Slide 7: ML probe request (1)
We propose to allow the probe request frame to carry the Multi-Link element to indicate the target of this probing.
  The MLD MAC address field indicates the MLD MAC address of the target AP MLD
  One or more per-STA profile subelements indicate the specific links of the target AP MLD that the non-AP MLD wants to probe
  The per-STA profile subelements are not present if the non-AP MLD intends to probe the complete information of all the supported links of the AP MLD
Frame Control
Duration
A1
A2
A3
Sequence Control
HT Control
……
Multi-Link Element
……
FCS
Element ID
Length
Element ID Extension
MLD MAC Address
……
Per-STA Profile (x)
Per-STA Profile (y)
Subelement ID
Length
Data
Probe Request Frame
Link Identifier
Multi-Link Control

## Slide 8: ML probe request (2)
In the case of multiple BSSID, the probe request frame can carry multiple multi-link element, each of which indicates a target MLD
Besides, this structure is flexible enough to allow the non-AP MLD to probe the complete information of different link sets for different MLDs
Frame Control
Duration
A1
A2
A3
Sequence Control
HT Control
……
Multi-Link Element (1)
……
FCS
MLD MAC Address
……
Per-STA Profile (1x)
Per-STA Profile (1y)
Subelement ID
Length
Data
Probe Request Frame
Link Identifier
……
MLD MAC Address
……
Per-STA Profile (2y)
Per-STA Profile (2z)
Subelement ID
Length
Data
Link Identifier
……
Multi-Link Element (2)

## Slide 9: ML probe request (3)
The non-AP MLD may need to carry a multi-link element in the probe request frame to indicate its own MLD information
Need a bit in the Multi-Link field to differentiate the type of the multi-link element, e.g.,
  0 means this multi-link element carries the MLD information of the non-AP MLD
  1 means this multi-link element indicates the target AP MLD for the probe request
    In this case, the per-STA profile Subelement only carries the Link Identifier Subelement
Frame Control
Duration
A1
A2
A3
Sequence Control
HT Control
……
Multi-Link Element
……
FCS
Element ID
Length
Element ID Extension
MLD MAC Address
……
Per-STA Profile (x)
Per-STA Profile (y)
Subelement ID
Length
Data
Probe Request Frame
Link Identifier
Multi-Link Control
……
Target MLD
TBD
TBD

## Slide 10: ML probe request (4)
In order to request partial information (specific IEs) of an AP MLD, we propose to reuse the non-inheritance element carried in the per-STA profile Subelement to indicate the Information Elements that the non-AP MLD wants to probe
  Note that the “target MLD” subfield is set to 1 in this case
Frame Control
Duration
A1
A2
A3
Sequence Control
HT Control
……
Multi-Link Element
……
FCS
Element ID
Length
Element ID Extension
MLD MAC Address
……
Per-STA Profile (x)
Per-STA Profile (y)
Subelement ID
Length
Data
Probe Request Frame
Link Identifier
Multi-Link Control
Non-inheritance element

## Slide 11: Conclusion
  We propose a unified design of multi-link probe request, which carries multi-link element to indicate:
    The target MLD
    Multiple MLDs
    The target links of one or more MLDs
    The target information elements of one or more links of one or more MLDs

## Slide 12: Straw Poll 1
  Do you agree that a non-AP MLD can carry a multi-link element in the probe request frame to probe complete information of an AP MLD?
    The MLD MAC Address field indicates the MLD address of the target AP MLD
    The per-STA profile subelements indicate the specific links of the target AP MLD that the non-AP MLD wants to probe

## Slide 13: Straw Poll 2
  Do you agree that the multi-link element can carry a subfield in the multi-link control field to indicate whether the multi-link element carries the MLD information of the non-AP MLD, or it carries the information of the target AP MLD for the probe request?

## Slide 14: Straw Poll 3
  Do you agree that the probe request frame can carry multiple multi-link elements to probe the information of multiple MLDs?

## Slide 15: Straw Poll 4
  Do you agree that the per-STA profile Subelement of the multi-link element in the probe request frame can carry non-inheritance element to indicate the list of information elements that the non-AP MLD requests to probe?

## Slide 16: References
  [1] 11-20-0411-04-00be-mlo-information-exchange-for-link-switching