## Slide 1
Issues on MLD Power Saving
Date: 2020-09-04
Authors:

## Slide 2: Introduction
Basic power saving operation including TIM indication for multilink has been defined.
However, some issues are not clearly discussed for the following cases
  Link status from STAs’ perspective (Interference from OBSS, STAs’ link status)
    In certain cases, STAs may not receive BU through certain links due to interference form OBSS or STA’s status (low battery), etc.
  Non-STR MLD (both AP and non-AP)
    Soft AP can be a non-STR MLD and power saving operation may impact the other link’s normal operation.
This contribution discusses possible issues on multi-link power saving.

## Slide 3: Recap: TIM indication and TID-to-Link Mapping
In TIM, an AP indicates pending BU with STAs’ AID.
In the SFD, one AID shall be used for all STAs of a non-AP MLD:
  When a non-AP MLD made a multi-link setup with an AP MLD, one AID is assigned to the non-AP MLD across all links.
  Therefore, AID can not indicate which STAs of a MLD shall wake up.
Wake up decision of STAs of a MLD : TID-to-Link-Mapping
  By default, after a multi-link setup, all TIDs are mapped to all setup links.
  The multi-link setup may include the TID-to-link mapping negotiation.
  TID-to-link mapping can have the same or different link-set for each TID unless a non-AP MLD indicates that it requires to use the same link-set for all TIDs during the multi-link setup phase.
However, since TID information is not included in TIM, a TID mapping to all links can only be used.
  All STAs of a MLD shall wake up once pending BU is indicated by TIM.

## Slide 4: Basic Single Link Power Saving Operation
PS-Poll is required to pull BU from the AP
TID can be only known at the time of data delivery
  In multi-link, all links shall be in normal mode at the time of Data delivery since STA doesn’t know the TID of BU.

## Slide 5: Issues on MLD Power Saving
Issue 1: Efficient multi-link power saving procedure is required
  Due to default TID to all link mapping, waking up all STAs of a non-AP MLD is not power efficient.
  In certain situations like low battery, some STAs of a MLD need to stay in sleep mode.
  Each link has different channel condition
    Certain link (STA) can not be used due to interference of OBSS
Issue 2: Non-STR AP MLD like soft AP shall also be considered
  In case of Non-STR AP MLD, STAs transmission (e.g., PS-Poll, U-APSD, QoS Null) may impact non-STR AP MLD’s transmission.

## Slide 6: Issue 1: Efficient multi-link power saving
Optimal power saving operation on multi-link can be performed with STAs’ presence check (PS-Poll)
  Due to hidden nodes or interference from OBSS, a certain link may not be available to receive BU.
  Each link’s status can be correctly checked by STAs of Non-AP MLD.
  In ML Power saving, STAs shall make a decision on link availability and transmit PS-Poll.
  AP shall only transmit buffered BUs using the links through which PS-Poll is received.

## Slide 7: Issue 1: Efficient multi-link power saving
Each STA of a non-AP MLD transmits PS-Poll if its link status is normal to receive BU
After certain time, AP MLD transmits BU via links which STAs transmitted PS-Poll

## Slide 8: Issue 2: Non-STR AP
If an AP MLD is not STR capable (e.g., Soft AP), busy period in one link might affect the other links’ availability.

## Slide 9: Issue 2: Non-STR AP
If trigger-enabled TWT is used for multi-link power saving, both non-STR AP issue and link unavailability issue can be solved.
  From AP side: Trigger frame transmission
  From STA side: PS-Poll transmission

## Slide 10: Conclusion
In this presentation, some issues on multi-link power saving were discussed.
  link unavailability from STA side
  non-STR AP MLD’s deaf period
If STAs’ presence check based ML power saving operation is used, link unavailability problem and efficient link power management can be addressed.
If Triggered-enabled TWT is used for ML power saving, non-STR AP MLD’s deaf period problem can be addressed.
In IEEE 802.11be, both ML PS-Poll based power saving and ML Trigger-enabled TWT shall be considered.

## Slide 11: Reference
[1] 11-20/0566r56, “Compendium of straw polls and
potential changes to the Specification Framework Document”
[2] 11-20-0066r3, “Multi-Link TIM”
[3] 11-20-0084r1, “Multi-Link TIM – Follow Up”

## Slide 12: Straw Poll #1
Do you agree to add the following to R1 of 11be SFD:
  Upon the reception of TIM with buffered BU, STAs of a MLD shall make a decision on link availability and transmit PS-Poll through the available link.
  AP MLD shall transmit buffered BUs using the links among the available links through which PS-Poll is received.

## Slide 13: Straw Poll #2
Do you agree to add the following to R2 of 11be SFD:
  If AP MLD is not STR capable, AP MLD shall use trigger-enabled TWT for ML power saving.