## Slide 1: Abbreviation and Definitions related to STR
Date: 2020-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yiqing Li |  |  |  | 
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Notes: September 2012

## Slide 2: Motivation
There are a lot of Motions mentioned STR, but there is still no definition of STR;
STR MLD and non-STR MLD are used in many motions, but also without clear definitions of them;
The definitions of these Abbreviations are provided in this document.
Some examples in spec or motion text:
6.8.1 STR: General
6.8.2 Non-STR: General
For R1, each AP affiliated with an STR AP MLD shall follow the baseline rules for scheduling Beacon frame transmissions.
802.11be supports the following cases in R1:
  STR AP MLD with STR non-AP MLD
  STR AP MLD with non-STR non-AP MLD
When a STA in a non-STR MLD receives an RTS addressed to itself, if the NAV of the STA indicates idle but another STA in the same MLD is either a TXOP holder or a TXOP responder, the STA may not respond with a CTS frame.

## Slide 3: Abbreviation and Definitions
Abbreviation：
STR: simultaneous transmission and reception;
Definitions：
A STR MLD is an MLD that support STR on all link pairs;
A Non-STR MLD is an MLD that at least one link pair is non-STR.

## Slide 4: Straw Poll 1
Do you agree to add below abbreviation of STR in 11be spec?
  STR: simultaneous transmission and reception

## Slide 5: Straw Poll 2
Do you agree to add below definitions in 11be spec?
  A STR MLD is an MLD that support STR on all link pairs;
  A Non-STR MLD is an MLD that at least one link pair is non-STR.