## Slide 1: Enhanced Trigger Frame for EHT Support
Date: 2020-12-07
Authors:
Name | Affiliations | Address | email
Steve Shellhammer | Qualcomm |  | shellhammer@ieee.org
Bin Tian |  |  | btian@qti.qualcomm.com
Yanjun Sun |  |  | yanjuns@qti.qualcomm.com
Alfred Asterjadhi |  |  | aasterja@qti.qualcomm.com

## Slide 2: Introduction
Here we propose an Enhanced Trigger Frame that is backward compatible with HE STAs with additional support for EHT STAs
Benefits of this Design
  Leverage 802.11ax Trigger Frame Design
Updates in this revision
  Given we are developing a better understanding of the U-SIG in the TB PPDU, we show how the information needed for the U-SIG in the TB PPDU can be carried in the Trigger Frame
  For the User Info Field RU Allocation Table, we consider using Primary/Secondary Channels versus Lower/Upper Channels

## Slide 3: Requirements
Item | Requirement
Backward Compatibility | An HE STA decoding the Enhanced Trigger Frame will not have any modified behavior
EHT Support | An EHT STA can decode the Enhanced Trigger Frame and support new EHT Features
320 MHz Support | The Enhanced Trigger Frame signals 320 MHz for EHT STAs
16 Spatial Stream Support | The Enhanced Trigger Frame signals up to 16 Total Spatial Streams for EHT STAs
RU Allocation | The Enhanced Trigger Frame supports EHT RU Allocations including MRU allocations

## Slide 4: Trigger Frame – Reserved Bits
Available Reserved Bits
Common Info Field, the UL HE SIG-A2 Reserved subfield (B54-B62)
  These bits are currently set to all ones
  These bits are copied into the SIG-A2 Reserved subfield in the HE UL TB PPDU
Common Info Field, the Reserved Bit (B63)
  This bit is currently set to zero
User Info Field, the Reserved bit (B39)
  This bit is currently set to zero
User Info Field, the MSB of AID12 is unused except for a few special cases, and can be reused
  See Table 9-31h
Summary
We have 10 available reserved bits in the Common Info Field
We have 2 available reserved bits in the User Info Field

## Slide 5: UL HE SIG-A2 Reserved Subfield (B54-B62)
Text from 802.11ax Draft 7
  The UL HE-SIG-A2 Reserved subfield of the Common Info field carries the value to be included in the Reserved field in the HE-SIG-A2 subfield of the solicited HE TB PPDUs. An HE AP sets the UL HE-SIG-A2 Reserved subfield to all 1s.
This ensures that all HE STAs transmit the same bits in the SIG-A2 Reserved subfield
These bits are must cut from the Trigger Frame and pasted into the HE-SIG-A2 field
These bits are not used for any other purpose in HE
These bits can be modified for EHT without causing an impact on HE STAs

## Slide 6: Common Information

## Slide 7: Reference – 802.11ax Common Info Field
For reference, here is the 802.11ax Common Info Field

## Slide 8: Latest TB PPDU U-SIG
In [1] we have the latest U-SIG contents for the TB PPDU
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 2
 |  | TBD1 | 4
 | Version Dependent | PPDU format & EHT-SIG Compression | 2
 |  | Reserved | 1
 |  | Spatial Reuse 1 | 4
 |  | Spatial Reuse 2 | 4
 |  | TBD2 | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
Like in 11ax, STAs transmitting in the same 20 MHz need to transmit the same U-SIG, so Third-Party STAs can decode the U-SIG
The necessary information is better to be carried in the Trigger Frame, versus having assigning fixed values
Fields for some of these entries are already available in the Common Info Field
We need to account for the new fields
Alice Chen, Sameer Vermani, Bin Tian and Youhan Kim, “U-SIG Design for TB PPDU,” IEEE 802-11/20-1546r0, September 2020

## Slide 9: U-SIG in TB PPDU
If the BW and the Spatial Reuse subfields of the Common Info in the Trigger Field are not redefined, then we have around 23 to 26 bits to be carried in the Trigger Frame
This is more than can be carried in the Common Info Reserved bits (10 bits)
We can carry this in a Special User Info Field, using a Special AID12 value
  The Special User Info Field can carry 28 bits ()
Field | Category | Subfield | Bits | From Trigger Frame
U-SIG | Version Independent | Version identifier | 3 | 0 to 3
 |  | PPDU BW | 3 | 3
 |  | UL/DL | 1 | Derived as in 11ax
 |  | BSS color | 6 | Derived as in 11ax
 |  | TXOP | 7 | Derived as in 11ax
 |  | Reserved | 2 | 2
 |  | TBD1 | 4 | 4
 | Version Dependent | PPDU format & EHT-SIG Compression | 2 | Derived as in 11ax
 |  | Reserved | 1 | 1
 |  | Spatial Reuse 1 | 4 | 4
 |  | Spatial Reuse 2 | 4 | 4
 |  | TBD2 | 5 | 5
 | CRC & Tail | CRC in U-SIG | 4 | Derived as in 11ax
 |  | Tail in U-SIG | 6 | Derived as in 11ax
 | Total # of Bits in U-SIG |  | 52 | 

## Slide 10: Proposal for Carrying Necessary U-SIG Subfields in Special User Info Field
Define a special AID12 value in Table 9-31h “AID12 Subfield Encoding” to indicate that the User Info Field with this special AID12 value is a Special User Info Field carrying the non-derived content for the U-SIG of the TB PPDU
The first 12 bits (B0-B11) of the User Info Field is AID12
The remaining 28 bits (B12-B39) are allocated to the following U-SIG Subfields
Subfield | Length (Bits)
PHY Version Identifier | 3
PPDU Bandwidth | 3
Spatial Reuse 1 | 4
Spatial Reuse 2 | 4
U-SIG Reserved | 12
Reserved | 2
The exact bit assignments can be done once the U-SIG format is finalized for the TB PPDU
This Special User Info Field is sent right after the Common Info Field

## Slide 11: Mapping Content from Trigger Frame to TB PPDU Preambles

## Slide 12: 802.11ax Draft Statement
The following statement is in the 802.11ax Draft, Clause 26.5.2.2.4
  “The AP shall place User Info fields with the AID12 subfield set to 0 or a value greater than 2007 after User Info fields with the AID12 subfield set to a value in the range 1 to 2007 (if any present).”
Here we propose a way of keeping the Special User Info Field right after the Common Info Field while still addressing this statement in the 802.11ax Draft

## Slide 13: Proposal for AID12 Value
Instead of using one of the currently reserved AID12 values we propose to use a currently unreserved value, AID12 = 2007
Make that a special value in EHT, indicating the Special User Info Field
Place the Special User Info Field right after the Common Info Field
  This is consistent with the statement in the 11ax draft, since the AID12 value is not greater than 2007
Set the Common Info Field Reserved bit (B63) to the Enhanced Trigger Frame Flag
  The current value of B63 in 11ax is zero
  If set to one the STA knows this is an Enhanced Trigger Frame
  This indicates the presence of the Special User Info Field with AID12=2007 to convey additional Common Information, as shown below

## Slide 14: Number of HE LTFs and Midamble Periodicity
Number of HE LTFs and Midamble Periodicity Value | Number of HE LTFs (Doppler = 0) | Number of HE LTFs Midamble Periodicity (Doppler = 1) | Number of EHT LTFs (Doppler = 0) (FOR EHT) | Number of EHT LTFs Midamble Periodicity (Doppler = 1) (FOR EHT)
0 | 1 | 1 (10 symbols) | 1 | 1 (10 symbols)
1 | 2 | 2 (10 symbols) | 2 | 2 (10 symbols)
2 | 4 | 4 (10 symbols) | 4 | 4 (10 symbols)
3 | 6 | Reserved | 6 | Reserved
4 | 8 | 1 (20 symbols) | 8 | 1 (20 symbols)
5 | Reserved | 2 (20 symbols) | 12 | 2 (20 symbols)
6 | Reserved | 4 (20 symbols) | 16 | 4 (20 symbols)
7 | Reserved | Reserved | Reserved | Reserved
It is possible to expand the “Number of HE LTFs and Midamble Periodicity” subfield to support up to 16 LTFs

## Slide 15: Common Info Summary
B63 is the Enhanced Trigger Frame Flag
  In 802.11ax B63 is a reserved bit and is set to zero
  In 802.11be B63 is the Enhanced Trigger Frame Flag and is set to one
    This indicates it is an Enhanced Trigger Frame and supports EHT
    It also indicates that AID12=2007 is a Special AID12 value
A Special User Info field is placed right after the Common Info Field
  It uses Special AID12=2007
  It carries the non-derived information for the U-SIG in the TB PPDU
    PHY Version Identifier, PPDU Bandwidth, Spatial Reuse 1, Spatial Reuse 2, U-SIG Reserved bits
The Number of HE LTFs and Midamble Periodicity subfield has been extended to support 12 and 16 LTFs

## Slide 16: User Information

## Slide 17: Update
The update proposal for the User Info Field includes the following changes
  Change RU Allocation table bits (LU, B0) from Lower/Upper meaning to Primary/Secondary meaning
  Remove the HE/EHT bit from the User Info Field
This approach provides backward compatibility with 11ax and provides an EHT Reserved bit
Material from the earlier proposal is in the Backup

## Slide 18: Clarification of HE/EHT User Info Field Format
HE STAs
  User Info Field is always the HE format
R1 EHT STAs
  If Enhanced Trigger Frame Flag is zero, User Info Field is HE format
    EHT STA transmits HE TB PPDU
  If Enhanced Trigger Frame Flag is one, User Info Field is EHT Format
    EHT STA transmits EHT TB PPDU
R2 EHT STAs
  It is possible to support both HE or EHT User Info Field formats in one Trigger Frame to support A-PPDU in R2

## Slide 19: User Info Field Subfields
B25 EHT Reserved Bit
  Set to zero in R1
B39 PS160 Bit

## Slide 20: Primary/Secondary Definition for B0 and Additional bit
B0 is the Primary/Secondary 80 MHz bit for RUs/MRUs less than or equal to 80 MHz
  For larger MRUs, B0 is a bit used in the indication of the specific MRU, and no longer has a primary/secondary meaning
PS160 is the Primary/Secondary 160 MHz bit for RUs/MRUs less than or equal to 160 MHz
  For larger MRUs PS160, is a bit used in the indication of the specific MRU, and no longer has a primary/secondary meaning

## Slide 21: Backward Compatibility with 802.11ax
Here we show it is possible for an STA to determine its RU/MRU location, looking only at the User Info Field, without knowing a priori if the User Info Field is, HE or EHT Format
If this is possible, then in R2 we can use that RU/MRU location in combination with A-PPDU signaling in the Common Info about which 80 MHz is HE and which is EHT to determine if the EHT STA is to transmit an HE or EHT TB PPDU
We begin with the following bit definitions in the User Info Field
  B0 P80/S80
  HE Reserved Bit (B39) P160/S160, call this the PS160 bit

## Slide 22: Logic – Primary/Secondary Approach
PS160 | Value of (R7-R1) | Implication
1 |  | STA knows that this is an EHT Formatted User Info Field (Reserved bit is set to zero in HE)
0 | > 68 | STA knows that this is an EHT Formatted User Info Field (This is a reserved value of (R7-R1) in HE)
0 | 68 | From SP160 and the value of (R7-R1) the STA does not know the User Info Field Format However, the RU is the same for both HE and EHT because, Since (PS160 == 0) , then that indicates P160, so that is the same for HE and EHT Format Since B0 indicates P80/S80, that is the same for HE and EHT Format Since (B7-B1) ≤ 68, and the RU Allocation Table is Backward compatible, the table values are the same
PS160 | Value of (R7-R1) | Implication
1 |  | STA knows that this is an EHT Formatted User Info Field (Reserved bit is set to zero in HE)
0 | > 68 | STA knows that this is an EHT Formatted User Info Field (This is a reserved value of (R7-R1) in HE)
0 |  | From SP160 and the value of (R7-R1) the STA does not know the User Info Field Format However, the RU is the same for both HE and EHT because, Since (PS160 == 0) , then that indicates P160, so that is the same for HE and EHT Format Since B0 indicates P80/S80, that is the same for HE and EHT Format Since (B7-B1) ≤ 68, and the RU Allocation Table is Backward compatible, the table values are the same
Hence the STA can determine the exact RU/MRU location looking only at {PS160, B0, B7-B1}
This means in R2 we can signal which 80 MHz is HE and which is EHT to support A-PPDU
  Exact signaling for A-PPDU TB PPDU to be deferred to R2
In R1 the User Info Field is always formatted for EHT

## Slide 23: Clarification – RU Allocation Table (RUs/MRUs 80 MHz)
B0 indicates P80/S80
PS160 indicates P160/S160
For all RUs/MRUs that fit in 80 MHz, these two bits uniquely identify the 80 MHz segment

## Slide 24: Clarification – RU Allocation Table (80 MHz < RUs/MRUs 160 MHz)
B0 and B7-B1 indicate MRU within 160 MHz
PS160 indicates whether this is in P160 or S160
B0
B7-B1
0
0
96
97
0
0
98
99
1
1
96
97
1
1
98
99

## Slide 25: Clarification – RU Allocation Table (160 MHz < RUs/MRUs 320 MHz)
For MRUs larger than 160 MHz, the bits B0 and PS160 are just bits identifying the specific MRU and have no meaning of Primary/Secondary
B0
B7-B1
1
0
104
104
1
0
104
104
PS160
0
0
1
1

## Slide 26: SS Allocation Subfield
Four bits allow indexing the starting spatial stream over the full 16-bit range, supporting up to a total of 16 spatial streams in UL MU-MIMO
Two bits for the Number of Spatial Streams supports up to 4 spatial streams per-user

## Slide 27: User Info Field Summary
B25 is an EHT Reserved bit. In R1 it is set to zero.
B39 is the PS160 Bit
  Used in the RU Allocation Table
B26-29 is a 4-bit subfield indicating the Starting Spatial Stream Number
B30-B31 is a 2-bit subfield indicating the number of per-User Spatial Streams
As described earlier
  In R2 TB A-PPDU signaling can be included in the Common Info
  Since the STA can determine its RU/MRU location processing only the User Info Field, without knowing a priori if the User Info Field is, HE or EHT format

## Slide 28: Straw Poll #1
Do you agree to set the Trigger Frame Common Info Field Reserved Bit (B63), Enhanced Trigger Frame Flag, to one to indicate this is an Enhanced Trigger Frame?
  Note: This indicates the presence of the Special User Info Field, immediately after the Common Info Field, which carries the non-derived subfields of the U-SIG in the TB PPDU
  Note: This indicates that the User Info Field addressed to an R1 EHT STA is in the EHT Format

## Slide 29: Straw Poll #2
Do you agree that,
  If Enhanced Trigger Frame Flag is zero, the User Info Field is HE format
    EHT STA transmits HE TB PPDU
  In R1, if Enhanced Trigger Frame Flag is one, the User Info Field is EHT Format
    EHT STA transmits EHT TB PPDU

## Slide 30: Straw Poll #3
Do you agree that in the Trigger Frame, immediately after the Common Info Field, there is a Special User Info Field which carries the following non-derived subfields of the U-SIG in the TB PPDU,
  PHY Version ID (3 bits)
  PPDU Bandwidth (3 bits)
  Spatial Reuse 1 (4 bits)
  Spatial Reuse 2 (4 bits)
  U-SIG Reserved Bits (12 bits)

## Slide 31: Straw Poll #4
Do you agree to assign a Special AID12 value of 2007 in the Trigger Frame for the Special User Info Field which carries the non-derived subfields of the U-SIG in the TB PPDU?

## Slide 32: Straw Poll #5
Do you agree to change the following reserved values in the Trigger Frame Common Info Field Number of HE LTFs and Midamble Periodicity table, for the case Doppler = 0, as follows?
  Number of HE LTFs and Midamble Periodicity subfield value = 5 indicates the Number of LTFs = 12
  Number of HE LTFs and Midamble Periodicity subfield value = 6 indicates the Number of LTFs = 16

## Slide 33: Straw Poll #6
Do you agree that in the User Info Field of the Trigger Frame the following bits indicate the following?
  B0 of the RU Allocation subfield indicates Primary/Secondary 80 MHz Channel for RU/MRU 80 MHz
    Note: This is the same as in 11ax
    Note: For RUs/MRUs > 80 MHz, B0 is used to indicate a specific MRU and does not have a primary/secondary meaning
  PS160 (B39) indicates Primary/Secondary 160 MHz for RU/MRU 160 MHz
    Note: For RUs/MRUs > 160 MHz, PS160 is used to indicate a specific MRU and does not have a primary/secondary meaning

## Slide 34: Straw Poll #7
Do you agree that in the EHT User Info Field of the Trigger Frame B25 is an EHT Reserved and set to zero in R1?

## Slide 35: Straw Poll #8
Do you agree to use four bits of the Trigger Frame User Info Field Spatial Stream Allocation subfield to indicate the starting spatial stream, and two bits to indicate the number of per-user spatial streams?
  Note: This supports up to a total of 16 spatial streams with up to four spatial streams per-user

## Slide 36: Straw Poll 9
Do you agree with the following EHT User Info Field format in the EHT Enhanced Trigger Frame?

## Slide 37: Backup

## Slide 38: EHT R1 AP Behavior
To trigger an HE TB PPDU the AP sends an HE Tigger Frame
  Note that B63 of the Common Info Field is set to zero
  User Info Field formatted as HE format
To trigger an EHT TB PPDU the AP sets the following in the Trigger Frame:
  Sets the Enhanced Trigger Frame Flag (B63) to one
  Sets subfields in Common Info Field
  Sends a Special User Info Field immediately after the Common Info Field
    The AID12 value of the Special User Info Field is set to 2007
    The Special User Info Field carries the non-derived subfields of the U-SIG in the TB PPDU
      PHY Version Identifier, PPDU Bandwidth, Spatial Reuse 1, Spatial Reuse 2, U-SIG Reserved bits
  For each User Info Field
    Sets B25 (EHT reserved) to zero
    Sets {PS160, B0, B1-B7} to signal the appropriate RU/MRU
    Sets B26-B29 to indicate the Starting Spatial Stream
    Sets B30-B31 to indicate the Number of per-User Spatial Streams
    Sets the other subfields in the User Info Field

## Slide 39: EHT R1 STA Behavior
If Enhanced Trigger Frame Flag (B63) of the Common Info Field is set to zero, the STA processes the HE Tigger frame and sends a HE TB PPDU
If Enhanced Trigger Frame Flag (B63) of the Common Info field is set to one it:
  Decodes the necessary fields of the Common Info Field
  Decodes the Special User Info Field, with AID12=2007, which is immediately after the Common Info Field, and uses that info to populate the U-SIG of the EHT TB PPDU
  Uses {PS160, B0, B1-B7} to identify the RU/MRU
    Decodes B26-B29 to identify the Starting Spatial Stream number
    Decodes B30-B31 to identify the Number of per-User Spatial Streams
  Decodes the rest of the User Info Field
  Transmits an EHT TB PPDU

## Slide 40: Material from Earlier Version

## Slide 41: Enhanced User Info Field
For Reference here is the 802.11ax User Info
The main issue is to expand the functionality of the User Info Field to support EHT features while maintaining forward compatibility for R2
In the following we provide an example which achieves these goals

## Slide 42: Example – Enhanced User Info Field
Here we provide an example of the Enhanced User Info Field
Provides support for
  Full set of RUs/MRUs
  Support up to 16 Spatial Streams
  HE/EHT bit to indicate to each EHT STA if it is to transmit an HE or EHT TB PPDU

## Slide 43: Lower/Upper 160 MHz Segment Bit
Combining this bit with the 8-bit RU Allocation subfield, provides an effective 9-bit subfield
This is sufficient for supporting all RUs and MRUs

## Slide 44: SS Allocation Subfield
Four bits allow indexing the starting spatial stream over the full 16-bit range, supporting up to a total of 16 spatial streams in UL MU-MIMO
Two bits for the Number of Spatial Streams supports up to 4 spatial streams per-user

## Slide 45: HE/EHT Format (Reserved Bit B39)
We use the Reserved Bit (B39) to indicate to the EHT STA whether the User Info Field is the original format or the enhanced format
  If the HE/EHT Format bit is set to HE, then the EHT STA will transmit an HE TB PPDU
  If the HE/EHT Format bit is set to EHT, then the EHT STA will transmit an EHT TB PPDU
HE/EHT Format (B39) | Meaning | Comment
HE (value = 0) | The User Info Field is unchanged | STA to transmit an HE TB PPDU
EHT (value = 1) | Enhanced User Info Field | STA to transmit an EHT TB PPDU

## Slide 46: Enhanced User Info Field
Subfield | HE Bits | EHT Bits | Comments for EHT
AID12 | 12 | 12 | No Change
RU Allocation | 8 | 8 | Combining Lower/Upper 160 MHz bit with 8-bit RU Allocation subfield provides 9-bits, which is sufficient for all RUs and MRUs.
UL FEC Coding Type | 1 | 1 | No Change
MCS | 4 | 4 | DCM is Merged into MCS Subfield
DCM | 1 | 0 | Merges DCM with MCS
SS Allocation | 6 | 6 | Four bits for starting spatial stream and two bits for the number of spatial streams. Supports up to four spatial streams per-user
UL Target RSSI | 7 | 7 | No Change
HE/EHT Format |  | 1 | Indicated to EHT STA whether to behave as HE or EHT STA
Lower/Upper 160 MHz Segment |  | 1 | Used to indicate if RU Allocation is for Lower or Upper 160 MHz Segment
Reserved | 1 | 0 | The MSB of AID12 is available for Future Use There is also a Reserved bit in the Trigger Dependent User Info Field of the Basic Trigger Frame Variant