## Slide 1: NDPA and MIMO Control Field Design for EHT
Date: 2020-09-09
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Yanjun Sun |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Lin Yang |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Things that may impact NDPA & EHT MIMO Control Field Design in EHT
  Spatial streams increase to 16
  Bandwidth increase to 320MHz
  Puncturing information
  Granularity of feedback changing to 242 tones
In these slides we share our view of the NDPA & EHT MIMO Control Field Design
  Incorporate the above changes
  Keep as much of the 11ax design as possible; minimize design work
  Make sure that there is scope for accommodating R2 features in the same framework

## Slide 3: Background: 11ax NDPA
Below shows the 11ax NDPA
This field tells
that this is HE
Or VHT

## Slide 4: EHT NDPA: High Level Signaling
Recommend not defining a new sub-type in frame control
Use the sounding dialogue token to tell that this is an EHT NDPA
  Unused state of [B0,B1] bits in the sounding dialogue token can be used to signal that this is an EHT NDPA
  Also recommend adding a reserved bit; the most significant bit of sounding dialogue token for future-proofing
 | Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | … | STA Info n | FCS
Octets: | 2 | 2 | 6 | 6 | 1 | 4 |  | 4 | 4
NDPA frame
 | B0 | B1 | B2 B6 | B7
 | Ranging | HE | Sounding Dialog Token Number | Reserved
Bits: | 1 | 1 | 5 | 1
 | B0 | B1 | B2 B7
 | Reserved | HE | Sounding Dialog Token Number
Bits: | 1 | 1 | 6
11ax:
11az:
EHT:
NDPA mode | B0 | B1
VHT | 0 | 0
HE | 0 | 1
11az | 1 | 0
EHT | 1 | 1
 | B0 | B1 | B2 B6 | B7
 | EHT NDPA | HE | Sounding Dialog Token Number | Reserved
Bits: | 1 | 1 | 5 | 1

## Slide 5: Puncturing information
This was sent through a special AID in the STA Info field in 11ax
  The information on what tones to feedback was scattered across two fields
    The RU-start and RU-end index in the regular STA Info Field
    Disallowed channel bitmap in STA Info Field with special AID of 2047
  Was an ad-hoc solution as puncturing information could not be carried in NDP
Suggest carrying puncturing information in the NDP for EHT
Moreover, since we can now signal the exact RU/M-RU we want feedback on, we recommend just having an 7 bit field called ‘RU Index’ in the STA Info Field
  RU Index maps to an 7 bit RU allocation table similar to a trigger frame that contains all possible RU/M-RUs of size >=242 tones
  Single field to tell where the feedback is being requested
  Similar approach as RU allocation in trigger frame

## Slide 6: EHT NDPA: STA Info Field
STA Info Field: When AID is NOT a special value
STA Info Field: When AID takes a special value (e.g., 2044), we can use it to convey special information
Special STA Info Version bits can be used to convey different parsing of this field for R2 features

## Slide 7: Use of ‘Special STA Info Version’ bits
These bits act as a “version” for the STA info field with the special AID of 2044
  Every version value can carry different pieces of information
    Slightly more efficient than reserving new AIDs
Example usage
  These bits can be set to a new value for conveying other information for R2 features that might require additional NDPA information, E.g.,
    Multi-AP sounding information can be carried with bits being 00
    Implicit sounding information can be carried with bits being 01

## Slide 8: MIMO Control Field
HE MIMO Control Field (in 11ax) is shown below

## Slide 9: EHT MIMO Control Field
Proposal for EHT MIMO Control Field is below
  The Disallowed Subchannel Bitmap Present subfield is not needed
  Note: RU Start and RU End Index have been combined into a single trigger frame like RU index that maps to an 7-bit table

## Slide 10: NDP U-SIG and U-SIG Overflow Contents
Puncturing indication can be the same 5 bit indication as is used for the non-OFDMA case
The fields in red are un-used
EHT-SIG sent at fixed MCS0
EHT-SIG is shown below
  Common field and User Field are encoded together
    17 overflow, 3 bits #user, 22 user field bits and 10 bits CRC/Tail= 52 bits total
  User Field carries the Nsts just like SU
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 3
 |  | Number of EHT-LTF symbols and midamble periodicity | 3
 |  | Doppler | 1
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 2
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17
NDP | Common Field |  | User Specific Field
Content channel #1 | U-SIG Overflow | #User = 1 | User Field
Content channel #2 | U-SIG Overflow | #User = 1 | User Field

## Slide 11: SP1
Do you agree that we can use [B0,B1] bits in the sounding dialogue token to signal that the frame is an EHT NDPA?
  Y
  N
  A

## Slide 12: SP2
Do you agree that instead of the partial BW info field in the NDPA (as was the case in 11ax), there will be a single RU index in EHT NDPA mapping to the RU/M-RU on which the feedback is being requested?
  There will be reserved bits following it to allow for future expansion
  The RU index field may be unified with trigger frame and may have 7-10 bits

## Slide 13: SP3
Do you agree with the EHT MIMO Control Field Design shown below?
  Size of codebook information may increase
  Reserved bits (number and location) may change
  Sounding Dialogue Token and Feedback Segment related bits are TBD per MAC discussions

## Slide 14: SP4
Do you agree that the U-SIG in NDP will carry the puncturing information for the entire PPDU BW covering all non-OFDMA puncturing cases?
  Y
  N
  A

## Slide 15: SP5
Do you agree that in an NDP, the EHT-SIG
  Will carry a SU-like per-user info field with a special AID
    Nsts of the NDP will be signaled in it
  Will always be sent at MCS0, jointly encoded 2 symbols
  Carries an EHT-SIG MCS field that is set to MCS0

## Slide 16: NDPA RU Index table
Appendix

## Slide 17: Embedded word object has table below