## Slide 1: NDPA and MIMO Control Field Design for EHT
Date: 2020-09-09
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Yanjun Sun |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Lin Yang |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Things that may impact NDPA & EHT MIMO Control Field Design in EHT
  Spatial streams increase to 16
  Bandwidth increase to 320MHz
  Puncturing information
  Granularity of feedback changing to 242 tones
In these slides we share our view of the NDPA & EHT MIMO Control Field Design
  Incorporate the above changes
  Keep as much of the 11ax design as possible; minimize design work
  Make sure that there is scope for accommodating R2 features in the same framework

## Slide 3: Background: 11ax NDPA
Below shows the 11ax NDPA
This field tells
that this is HE
Or VHT

## Slide 4: EHT NDPA: High Level Signaling
Recommend not defining a new sub-type in frame control
Use the sounding dialogue token to tell that this is an EHT NDPA
  Unused state of [B0,B1] bits in the sounding dialogue token can be used to signal that this is an EHT NDPA
  Also recommend adding a reserved bit; the most significant bit of sounding dialogue token for future-proofing
 | Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | … | STA Info n | FCS
Octets: | 2 | 2 | 6 | 6 | 1 | 4 |  | 4 | 4
NDPA frame
 | B0 | B1 | B2 B6 | B7
 | Ranging | HE | Sounding Dialog Token Number | Reserved
Bits: | 1 | 1 | 5 | 1
 | B0 | B1 | B2 B7
 | Reserved | HE | Sounding Dialog Token Number
Bits: | 1 | 1 | 6
11ax:
11az:
EHT:
NDPA mode | B0 | B1
VHT | 0 | 0
HE | 0 | 1
11az | 1 | 0
EHT | 1 | 1
 | B0 | B1 | B2 B6 | B7
 | EHT NDPA | HE | Sounding Dialog Token Number | Reserved
Bits: | 1 | 1 | 5 | 1

## Slide 5: Puncturing information
This was sent through a special AID in the STA Info field in 11ax
  The information on what tones to feedback was scattered across two fields
    The RU-start and RU-end index in the regular STA Info Field
    Disallowed channel bitmap in STA Info Field with special AID of 2047
  Was an ad-hoc solution as puncturing information could not be carried in NDP
Suggest carrying puncturing information in the NDP for EHT
Partial BW Info field in the STA Info field can be 7-9 bits
  An RU Index that maps to an RU allocation table that contains all possible RU/M-RUs of size >=242 tones or a bitmap that indicates the 242RUs for channel feedback

## Slide 6: EHT NDPA: STA Info Field
STA Info Field: When AID is NOT a special value
STA Info Field: When AID takes a special value (e.g., 2044), we can use it to convey special information
Special STA Info Version bits can be used to convey different parsing of this field for R2 features

## Slide 7: Use of ‘Special STA Info Version’ bits
These bits act as a “version” for the STA info field with the special AID of 2044
  Every version value can carry different pieces of information
    Slightly more efficient than reserving new AIDs
Example usage
  These bits can be set to a new value for conveying other information for R2 features that might require additional NDPA information, E.g.,
    Multi-AP sounding information can be carried with bits being 00
    Implicit sounding information can be carried with bits being 01

## Slide 8: MIMO Control Field
HE MIMO Control Field (in 11ax) is shown below

## Slide 9: EHT MIMO Control Field
Proposal for EHT MIMO Control Field is below
  The Disallowed Subchannel Bitmap Present subfield is not needed
  Partial BW Info field can be 7-9 bits

## Slide 10: NDP U-SIG Puncturing Info
Puncturing indication can be the same 5 bit indication as is used for the non-OFDMA case for EHT MU PPDU[1]
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52

## Slide 11: Consistency of puncturing information across NDPA, NDP and MIMO Control Fields
NDPA is requesting feedback on certain 242RUs
NDP is indicating, what channels are punctured in the NDP for the purposes of channel estimation block
To avoid conflicting situations, it is good to make sure that the populated tones in NDP are a super-set of all the feedback tones being requested in the NDPA
Propose to add a rule which says
  NDPA shall not request feedback on a 242RU that is signaled as punctured in the U-SIG of the ensuing NDP
MIMO Control Field’s RU Index will be the same as the one in NDPA

## Slide 12: SP1
Do you agree that we can use [B0,B1] bits in the sounding dialogue token to signal that the frame is an EHT NDPA?
  Y
  N
  A

## Slide 13: SP2
Do you agree the design of STA Info field as shown below
  Partial BW Info field can be 7-9 bits
  Size of codebook size may increase

## Slide 14: SP3
Do you agree with the EHT MIMO Control Field Design shown below?
  Size of codebook information may increase
  Reserved bits (number and location) may change
  Sounding Dialogue Token and Feedback Segment related bits are TBD

## Slide 15: SP4
Do you agree that the U-SIG in NDP will carry the puncturing information for the entire PPDU BW?
  Same 5 bit field as other non-OFDMA PPDUs
  Y
  N
  A

## Slide 16: SP5
Do you agree with the following two rules
  NDPA shall not request feedback on a 242RU that is signaled as punctured in the U-SIG of the NDP that follows it
  MIMO Control Field’s RU Index field will be the same as the one in NDPA

## Slide 17: NDPA RU Index table
Appendix

## Slide 18: Embedded word object has table below

## Slide 19: References
[1] Document 11-20/1238r4, “Open Issues on Preamble Design”, Sameer Vermani (Qualcomm)