## Slide 1: 11be CCA Levels
Date: 2020-09-10
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In this presentation we will discuss CCA operations for 11be transmission and corresponding CCA levels for wider BW

## Slide 3: Review: 11ax CCA Rules
Support up to 160MHz or 80+80MHz
11ax CCA operations
  CCA check for primary 20MHz channel
    Check for the start of any 20/40/80/160 WLAN signal occupying primary20
  CCA check for any signal not occupying primary 20MHz channel
    Assuming primary 20 is idle, further check for any WLAN signal on sec20/sec40/sec80 within a period aCCAMidTime
  Per 20MHz CCA
    Check on each 20MHz subchannel within a period aCCAMidTime, if there is any passing 20/40/80MHz WLAN signal higher than a BW dependent threshold
  Note: -62dBm ED for any signal in 20MHz subchannels

## Slide 4: Primary 20MHz CCA Level
The existing 11ax CCA on Primary 20 is shown in the table below
  It is not easy to understand in its current format
  It does not capture some cases: a STA in a X1 MHz operating mode needs to be able to detect the start of PPDUs with X2 MHz bandwidth, where X2 > X1
11ac CCA had same issue and was recently resolved in REVmd by passing a new motion with the following simplified text
  Start of a PPDU for which its power measured within the primary 20 MHz channel is at or above –82 dBm.

## Slide 5: 11be CCA Rules (1)
11be CCA operations
  Same ED checking rules and level: -62dBm/20Mhz
  CCA check on primary 20MHz channel the start of a packet
    This is always needed, can follow the improved text in REVmd on CCA on primary 20MHz
      Start of a PPDU for which its power measured within the primary 20 MHz channel is at or above –82 dBm
    This covers 320MHz PPDU

## Slide 6: 11be CCA Rules (2)
Need to better detect and support puncturing transmission
11be CCA operations
  CCA check for signal not occupying primary 20MHz channel within a period aCCAMidTime
    Not very efficient in channel selection
    Not support puncturing transmission
    For simplicity, propose to remove this CCA operation in11be
  Per 20MHz CCA within a period aCCAMidTime
    Provides good spectral efficiency and flexibility in the operating channel selection
    Per 20MHz CCA as the only non-primary 20MHz checking
    Simple extension of 11ax per 20MHz CCA to detect up to 320MHz

## Slide 7: Discussion on CCA threshold for Per 20MHz check
11ax per 20 CCA uses BW dependent mid packet detection threshold for detecting any 20/40/80MHz WLAN signal occupying a 20MHz subband (-72/-72/-69dBm), which has the following issues
  Mid packet can not tell the BW explicitly without preamble
  Puncturing transmission makes it harder to estimate PPDU BW
  The existing 11ax mid packet detection has uneven threshold across BW
    -72dBm for 20MHz, -72dBm for 40MHz, -69dBm for 20MHz
To simplify the CCA operation, propose to check the WLAN signal level captured on each 20MHz with single threshold of -72dBm
  Single CCA threshold not depending on BW
  Aligned with ESTI approach

## Slide 8: SP 1
Do you support 11be defines start of packet CCA check (PD) for primary 20MHz channel up to 320MHz?
  Start of a PPDU for which its power measured within the primary 20 MHz channel is at or above –82 dBm
Y/N/ABS

## Slide 9: SP 2
Do you support 11be not define CCA on secondary channels and only define per 20MHz check up to 320MHz?
  CCA threshold TBD
Y/N/ABS

## Slide 10: SP 3
Do you support for per 20MHz check, single threshold of -72dB (regardless of BW) is used for the WLAN signal level captured on each 20MHz?
Y/N/ABS