## Slide 1: Setting context for submission 11-20/1376r0 ‘Technical report on the interworking between 3GPP 5G system and WLAN’
Date: 2020-09-14
Authors:

## Slide 2: Abstract
These slides are meant to provide some context around why we have made the submission 11-20/1376r0, which is a ‘Technical report on the interworking between 3GPP 5G system and WLAN’
These slides also provide at a high-level main issues with 11-20/0013r5 and how those are addressed in 11-20/1376r0

## Slide 3: Why we submitted 11-20/1376r0 report (1/2)
With our background and knowledge working on the Wi-Fi and 5G Convergence project for last 2 years within WBA, we noticed the AANI report 11-20/0013 a few months ago.
We did a thorough review of 11-20/0013 report and found severe inaccuracies, misinformation and missing details on the WLAN and 5G interworking as defined by 3GPP Release 15/16. We found the report to be misleading in terms of gap items and what functions need to be supported within WLAN to enable interworking with 5G.
We provided our detailed inline comments on 11-20/0013r3 to AANI on 2020-07-14 highlighting technical issues we found in the report.
Some updates were done to the report in 11-20/0013r5 to address few of the comments, however majority of technical issues raised still remained in the report.

## Slide 4: Why we submitted 11-20/1376r0 report (2/2)
We tried to integrate our comments in 11-20/0013 but found that the report would require significant updates and major rewrites to be technically accurate, complete and well-informed to be used as a reference by the stekeholders interested in WLAN and 5G interowrking.
Hence, we decided to write a separate comprehensive report on the interworking between 3GPP 5G system and WLAN, instead of trying to fix 11-20/0013 report which will require lot of cycles.
With our background in WLAN and 5G convergence, we wrote the 11-20/1376r0 report in 5 weeks time.
The 11-20/1376r0 is a comprehensive report on the interworking between WLAN and 5G system – it covers 3GPP defined solutions and identifies key technical gaps and challenges related to enabling the interworking and provides guidance and recommendations for addressing those gaps in IEEE 802.11 and/or 3GPP.

## Slide 5: Main Issues we see with 11-20/0013 Report (1/2)
Issues | Report 11-20/0013r5 | Report 11-20/1376r0
1 | Defines a tightly coupled interworking model which is not defined by 3GPP | 
2 | Does not define details of trusted WLAN integration with 5G network | Report 11-20/1376r0 captures detailes on trusted WLAN integration in section 5 and 6
3 | Does not define the key 5G functionalities including UE registration, authentication, PDU session management, ATSSS traffic steering, QoS model and user data transport over the WAN access integrated with 5G network. | Provides details of key 5G functionalities over WLAN access in section 6.
4 | Functionalities described in section 3, 4 and 5 do not accurately represent what is defined in 3GPP on interworking with WLAN. There is major lack of technical accuracy and clarity in those sections. Anybody who knows and understands what 3GPP has defined for interworking will find majority of the text very confusing, inaccurate and misinformed. | Provides comprehensive details on the interworking between WLAN and 5G system in section 5 and 6.

## Slide 6: Main Issues we see with 11-20/0013 Report (2/2)
Issues | Report 11-20/0013r5 | Report 11-20/1376r0
5 | Section 5 does not address interworking related gaps for dual radio devices supporting both 5G and Wi-Fi radio. | Covers challenges and gaps for both dual radio devices and Wi-Fi only devices in section 7.
6 | Gap analysis section 5 suggests that IKEv2, EAP-5G, IPsec, NAS, GRE, session control are required to be supported on the WLAN AP (ANC) for STA only UE, which is not correct. WLAN AP does not need to support these functionality as per 3GPP defined solution for untrusted WLAN. | Covers challenges and gaps for Wi-Fi only devices in section 5.3 and 7.3.
7 | The TSN architecture described in section 5 for ‘WLAN and 5G CN interworking’ and for WLAN only network is not correct. | Section 9.2 describes challenges/issues with TSN support for integrated 5G and WLAN system.
8 | Technical recommendations in section 5.2 do not accurately represent what needs to be done within WLAN to enable interworking with 5G. | Section 8 provides comprehensive set of recommendations on what needs to be considered within WLAN as well as enhancements to be considered in 3GPP to enable interworking.

## Slide 7: Our Intent with 11-20/1376r0 report
It is not our intent to undermine the AANI current process. Our intent is to ensure that AANI (and IEEE 802.11) generates a technically accurate, comprehensive and well-informed report with meaningful proposed next steps on WLAN and 5G interworking.
We tried to integrate our comments into 11-20/0013 report, but we found that the report would require significant rewrites and major updates given the number and severity of issues identified.
Our submitted report 11-20/1376r0 is a genuine and good faith attempt to be constructive to the current AANI activities and our intent is to help AANI and IEEE to publish an accurate and well-informed report.