## Slide 1: IEEE 802.11 Coexistence SC Sep 2020 (virtual) closing report
Date: 20200916
Authors:

## Slide 2: IEEE 802.11 Coexistence SC achieved its goals as a discussion forum for coexistence issues
802.11 Coex SC activities in Sep 2020 (11-20-1296-00)
  Heard an update on July’s LS response to ETSI ERM TG11 related to 2.4 GHz operation
  Noted that LAA deployments are increasing, meaning coexistence is no longer just theoretical!
    Early measurements in Chicago suggest Wi-Fi is adversely affected by LAA operations
  Heard that EN 303 687 (6 GHz in Europe) is generally progressing well
    There is a compromise (& HS text) on the use of ED-only at -72 dBm for LBT detection …
    … but future work will be required to enable new 802.11be features in 6 GHz (& 5 GHz)
    … and a number of other threats/opportunities related to coexistence are still being discussed
  Heard that EN 301 892 (5 GHz in Europe) is dealing with the same old issues … again!
    Some are challenging the 2 year old compromise for PD/ED+ED-only operation …
    … with a potential adverse impact on Wi-Fi’s equitable access to 5 GHz
    … in a complex political & technical debate
  Documented recent 3GPP activities relevant to coexistence

## Slide 3: The IEEE 802.11 Coexistence SC discussed a possible extension of its charter to encompass 802.11be coexistence
Charter extension discussion
  The current charter of the Coex SC focuses on 802.11ax coexistence
  However, coexistence discussions will continue after 802.11ax is ratified
    In particular, as 802.11be is being developed
  The Coex SC discussed a possible new charter extension but did not vote on it
  Two refinements were suggested, which have been implemented
    Make it clear the Coex SC should work with 802.11 TGs
    Use “equitable access” rather than “fair access”
  Two concerns were expressed and briefly discussed
    Too often, the Chair prepares and delivers much of the material
    The issues are often the same old issues, repeated endlessly

## Slide 4: A couple of concerns were expressed in relation to continuing the Coex SC activity
Charter extension concerns & responses
  Concern: Too often, the Chair prepares and delivers much of the material
    It is true that the Chair often prepares and delivers much of the material
    Partially, this is because he happens to be enthusiastic & knowledgeable about the issues through his work in multiple forums dealing with coexistence
    In addition, no doubt others do not object to someone else volunteering to do the work
    The Chair will encourage a wider diversity of contributors in the future
  Concern: The issues are often the same old issues, repeated endlessly
    It is also true that the same old issues are arising, particularly in the 5 GHz context
    However, this is mainly because LAA/NR-U stakeholders keep re-raising them
    This suggests they are probably important because they certainly seem to be important to the proponents of LAA/NR-U technology

## Slide 5: A revised “scope” & “close down criteria” are proposed for a Coex SC charter extension
Revised “scope” for Coex SC charter extension
  The Coex SC shall promote, within the 802.11 WG and externally, an environment that enables IEEE 802.11 technologies to have equitable access to unlicensed spectrum globally
  The Coex SC should focus particularly on coexistence of 802.11ax & 802.11be with LAA & NR-U in the 5 GHz & 6 GHz bands globally
  The Coex SC may consider coexistence with other technologies and in other bands as directed by the Chair of the 802.11 WG
Revised scope “close down criteria” for Coex SC charter extension
  The Coex SC will close when it is determined by the 802.11 WG that the SC is unlikely to make further progress towards its goals

## Slide 6: IEEE 802.11 Coexistence SC will continue promoting good coexistence in Nov 2020
IEEE 802.11 Coexistence SC will meet virtually in Nov 2020
  Review results of ETSI BRAN #107 meeting in Sep/Oct 2020
    EN 301 893 (5 GHz)
    EN 303 687 (6 GHz)
  Review results of 3GPP RAN meeting in Sep 2020
    Plans for 6 GHz licensed operation for NR & unlicensed operation for NR-U
  Consider extending charter, if not approved in Sept 2020
  …

## Slide 7: The WG is requested to consider a revised charter for the Coex SC
Motion: Approve a revised charter for the Coex SC as follows:
  Scope
    The Coex SC shall promote, within the 802.11 WG and externally, an environment that enables IEEE 802.11 technologies to have equitable access to unlicensed spectrum globally
    The Coex SC should focus particularly on coexistence of 802.11ax & 802.11be with LAA & NR-U in the 5 GHz & 6 GHz bands globally
    The Coex SC may consider coexistence with other technologies and in other bands as directed by the Chair of the 802.11 WG
  Close down criteria
    The Coex SC will close when it is determined by the 802.11 WG that the SC is unlikely to make further progress towards its goals
  Moved: Andrew Myles
  Seconded:
  Result: