## Slide 1: Signaling for various transmission modes of MU-PPDU
Date: 2020-09-29
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sept. 2020

## Slide 2: Introduction
Two types of PPDU are defined in 11be SFD.
  MU-PPDU and TB-PPDU
And, since we agreed that the one unified PPDU format for SU transmission and MU transmission is used in 11be, the MU-PPDU can be used to support the various transmission modes as follows.
  Compressed mode ( i.e., non-OFDMA MU-MIMO)
  Non-compressed mode (i.e., OFDMA)
  SU transmission.
  NDP transmission.
  SU-DUP transmission.
Thus, in this contribution, we consider how to indicate the different transmission modes when MU-PPDU is used.

## Slide 3: Transmission modes ( 1/3)
Compressed mode and Non-compressed mode
  According to passed motion[Motion 122, #SP140], two modes are supported in MU-PPDU and each mode has the following characteristics.
    Compressed mode
      No RU Allocation subfield in the Common field of the EHT-SIG.
    Non compressed mode
      RU Allocation subfield in the Common field of the EHT-SIG.
  And, as the following motion, by a subfield in the U-SIG, we can easily indicate whether the MU-PPDU is used for compressed mode or not.
    “A subfield for an indication of compressed mode is included in U-SIG as version dependent field”

## Slide 4: Transmission modes ( 2/3)
SU and SU-DUP mode
  In these transmission modes as in the compressed mode, the EHT-SIG does not need to include the RU allocation subfield in the common field.
  In addition, the subfield of the number of non-OFDMA users is set as a value for 1 user to indicate the single-user transmission. And the User field for a non-MU-MIMO allocation is used.
  Unlike the OFDMA and non-OFDMA MU-MIMO transmission, the one EHT-SIG content channel can be present in EHT-SIG as [1, 2, 3,5]. So, for the indication of different configuration of EHT-SIG CC in SU transmission, we can consider using a subfield contained in U-SIG.
  And, since all fields present before the data field in the MU-PPDU are constructed same for both two transmission modes, the DUP mode can be differentiated by using the specific MCS index indicating the MCS0+DCM+Nss =1. [4]

## Slide 5: Variant transmission modes ( 3/3)
NDP mode
  Basically, the NDP is formed on the basis of SU PPDU at 11ac and 11ax.
  So, NDP can be configured as follows for the consistency with SU transmission mode
    No RU Allocation subfield in the Common field of the EHT-SIG
    In NDP transmission, we can consider the following EHT-SIG field by considering the passed motion
      “There is STA-ID related information in the EHT PPDU preamble sent to a single user and multiple users. TB PPDU is TBD. [Motion 111, #SP0611-19]”
    Thus, the one user field is present in EHT-SIG, and then, STA-ID in the user field can be set to as a specific value. (i.e., STA-ID = 2046)
      As similar with SU/SU-DUP mode, the User field for a non-MU-MIMO allocation is used.
  Therefore, since the pre-EHT field for NDP is consistent with SU cases, we can consider the application of similar signaling for this transmission.
    It does not need to allocate the specific entity of a subfield for indication of NDP.

## Slide 6: Indication of transmission modes
By considering the two types of PPDU and various transmission modes by using the MU-PPDU, we can consider using the PPDU type field which is already defined in the U-SIG field.
  Propose that the PPDU type field is consist of 2bits and the content of this field can be composed of as follows.
  We prefer no coupling with DL/UL field in the Version independent field which is designed to use as being independent per generation
    For the indication of the newly defined PPDU types or transmission modes in R2, we can put a reserved 1bit after this field in the U-SIG.
PPDU Type (2 bits) | PPDU type and Transmission mode | Note
00 | TB-PPDU | No EHT-SIG
01 | OFDMA | EHT-SIG, No SIG compression, RU Allocation, CC= [1 2 1 2]
10 | non-OFDMA MU-MIMO | EHT-SIG, SIG compression, No RU Allocation, CC= [1 2 1 2]
11 | SU/SU-DUP/NDP | EHT-SIG, SIG compression, No RU Allocation: CC= [1 1 1 1]

## Slide 7: Summary
We investigated the characteristics of various transmission mode by using the MU-PPDU.
For signaling of each transmission mode, we propose to use the PPDU type field with 2bits.
  The composition of the PPDU type field is as follows.
PPDU Type (2 bits) | PPDU type and Transmission mode | Note
00 | TB-PPDU | No EHT-SIG
01 | OFDMA | EHT-SIG, No SIG compression, RU Allocation, CC= [1 2 1 2]
10 | Non-OFDMA MU-MIMO | EHT-SIG, SIG compression, No RU Allocation, CC= [1 2 1 2]
11 | SU/SU-DUP/NDP | EHT-SIG, SIG compression, No RU Allocation: CC= [1 1 1 1]

## Slide 8: Straw Poll #1
Do you agree to add the following text in the TGbe SFD:
  In the SU transmission and SU-DUP transmission,
    The compressed mode is used.
    The number of non-OFDMA users subfield is set to 0 to indicate the one user
    The User field for a non-MU-MIMO allocation is used
  Y/N/A

## Slide 9: Straw Poll #2
Do you agree to add the following text in the TGbe SFD:
  In NDP transmission,
    The compressed mode is used.
    The number of non-OFDMA users subfield is set to 0
    One user field is present in EHT-SIG and the STA-ID is set to 2046 to indicate the zero user.
    The User field for a non-MU-MIMO allocation is used
  Y/N/A

## Slide 10: Straw Poll #3
Do you agree to add the following text in the TGbe SFD:
  SU-DUP is indicated by using the specific MCS index of 11be MCS table in SU transmission.
    Note : specific MCS means MCS0 + DCM + DUP
    Note: This specific MCS only apply to Nss = 1
  Y/N/A

## Slide 11: Straw Poll #4
Do you agree to add the following text in the TGbe SFD:
  SU, SU-DUP and NDP is indicated by using the one entity of the PPDU type and compressed mode field in U-SIG.
  Y/N/A

## Slide 12: Straw Poll #5
Do you agree to add the following text in the TGbe SFD:
  The PPDU type and compressed mode field in U-SIG is consists of 2bits.
    This field is used for indication of PPDU type and transmission modes.
  Y/N/A

## Slide 13: Straw Poll #6
Do you agree to add the composition of the PPDU type and compressed mode field as follows to indicate the various transmission modes in the TGbe SFD
  Note : for the indication of PPDU type/transmission mode defined in R2, a reserved bit after this field in U-SIG can be used.
  Y/N/A
PPDU Type and Compressed mode(2 bits) | PPDU type and Transmission mode | Note
00 | TB-PPDU | No EHT-SIG
01 | OFDMA | EHT-SIG, RU Allocation, CC= [1 2 1 2]
10 | Non-OFDMA MU-MIMO | EHT-SIG, No RU Allocation, CC= [1 2 1 2]
11 | SU/SU-DUP/NDP | EHT-SIG, No RU Allocation: CC= [1 1 1 1]

## Slide 14: Straw Poll#7
Do you agree to add the following text in the TGbe SFD:
  In NDP transmission,
    The compressed mode is used.
    The number of non-OFDMA users subfield is set to 0.
    One user field is present in EHT-SIG and the STA-ID is TBD.
    The User field for a non-MU-MIMO allocation is used.

## Slide 15: Reference
[1] 11-20-1238r2, Open Issues on Preamble Design
[2] 11-20/0524r2, Signaling of preamble puncturing in SU transmission
[3] 11-20/1317r0, SIG contents discussion for EHT sounding NDP
[4] 11-20/1377r0, On TBD MCSs
[5] 11-20/1474r0 , NDP Design for EHT