## Slide 1: TID-to-Link Mapping Negotiation
Date: 2020-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yiqing Li |  |  |  | 
Mengyao Ma |  |  |  | 
Notes: September 2012

## Slide 2: Introduction (1)
We already agreed that for TID-to-link mapping negotiation [1]
  The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
    Format TBD.
    NOTE – When the responding MLD cannot accept the update, it can reject the TID-to-link mapping update.
According to the above motion, both AP MLD and non-AP MLD can initiate the TID-to-link mapping negotiation

## Slide 3: Introduction (2)
For the non-AP MLD, it may initiate the TID-to-link mapping negotiation request for one or more of the following reason(s):
  Link unreachability
  Power save
  Bad QoS for some TID
For the AP MLD, it also can initiate the TID-to-link mapping negotiation request for one or more of the following reason(s):
  Admission control based on the type of STAs, STA capabilities and so on
  Load balance
  Separation of delay-sensitive traffic and delay-tolerant traffic
  Separation of downlink traffic and uplink traffic

## Slide 4: Problem Statement
If considering that the TID is directional, there are 16 TIDs and each TID may have the different link set
However, the responder may reject or accept with/without a minor change to the proposed mapping
So the question is how to reduce the number of TID-to-link mapping negotiations and quickly converge to the final TID-to-link mapping scheme
TID-to-link Mapping Response
TID-to-link Mapping Request
Non-AP MLD (AP MLD)
AP MLD (Non-AP MLD)
Time

## Slide 5: Proposed Solution (1)
Some auxiliary information can be provided by non-AP MLD to assist the AP MLD to decide whether to reject or accept with/without a minor change to the TID-to-link mapping, e.g.
  Info on link RSSI or disable link set if the TID-to-link mapping negotiation is initiated due to the link unreachability
  Info on max number of enable links or disable link set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS of TID(s) if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 6: Proposed Solution (2)
Since these auxiliary information is optional, there are three options to signal whether the corresponding info is present
  Option 1. Use a control bit to indicate whether the corresponding info field is present, as shown in the below figure (Prefer)
    It can support the case that the TID-to-link mapping negotiation is initiated due to several reasons
  Option 2. Define the corresponding info as optional elements
  Option 3. Use a Remapping Reason Code field with a different value to indicate whether the corresponding info field is present

## Slide 7: Summary
This contribution proposes that the non-AP MLD provides some auxiliary information to assist the AP MLD to decide whether to reject or accept with/without a minor change to the TID-to-link mapping
  Info on link RSSI or disable link set if the TID-to-link mapping negotiation is initiated due to the link unreachability
  Info on max number of enable links or disable link set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS of TID(s) if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 8: Reference
[1] 11-20-0566-69-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx

## Slide 9: SP
Do you support that the non-AP MLD provides some auxiliary information to assist the AP MLD to decide whether to reject or accept with/without a minor change to the TID-to-link mapping?
  Note. The detailed auxiliary information is TBD
  Yes
  No
  Abstain