## Slide 1: ML Reconfiguration
Date: 2020-10-14
Authors:
Name | Affiliations | Address | Phone | email
Payam Torab | Facebook Inc. | 1 Hacker way Menlo Park, CA |  | torab@ieee.org
Chunyu Hu |  |  |  | chunyuhu@fb.com
Pooya Monajemi | Cisco |  |  | pmonajem@cisco.com
Malcolm Smith |  |  |  | mmsmith@cisco.com

## Slide 2: Introduction
Multi-link operation (MLO) is an established feature of 11be
  STA* entities within Multi Link Devices (MLDs) forming connections referred to as links
  A link is a pairing of one AP STA* of an AP MLD and one non-AP STA* of an associated non-AP MLD
We refer to the mapping between AP and non-AP STA* entities of two associated MLDs as the “Multi-Link (ML) Configuration”
There are MLO scenarios that require changing the ML configuration established at association time – see [20/0810] for discussion
  Radio | processing core becoming available/unavailable (device centric)
  Reachability/range changes (environment, mobility) …
Furthermore, details of deciding the ML configuration at association time are not clear
* We prefer a different name for these entities in the the 802.11 architecture (e.g., “endpoints”), but have kept the term STA to stay consistent with contributions to this point.

## Slide 3: Introduction
We discuss the problem of ML Reconfiguration, defined as changing the mapping of STA entities of MLDs (ML configuration) post association
  Change in the mapping in general also includes change in the number of links
AP 1
AP 2
AP 3
AP 4
STA 1
STA 2
STA 3
AP 1
AP 2
AP 3
AP 4
STA 1
STA 2
STA 3
AP MLD
Associated
Non-AP MLD
AP MLD
Associated
Non-AP MLD
ML
Reconfiguration

## Slide 4: Why ML reconfiguration
Some MLO scenarios require changing the ML configuration
  Radio becoming available/unavailable post association (changes in device)
    Maintenance, hardware additions, hardware failure, upgrades ...
  New reachability/range with mobility (changes in environment)
  New traffic conditions (static/permanent increase/decrease in traffic)
  See [20/0810] for discussion
Changing ML configuration does not require disassociation
  As long as there are unaffected links through the process to carry out the signaling

## Slide 5: More on ML configuration (1) Deciding the ML configuration at association time
Beacon,
Probe Response
Elements: RNR, ML
AP STA capabilities
Probe Request,
Association Request
Elements: ML
Non-AP STA capabilities
AP
MLD
Non-AP
MLD-
ML configuration (= mapping between AP and non-AP STAs)
decided by non-AP MLD
References
[20/0389]
[20/0390]
[20/0741]
[20/1274]
[20/1592]
References
[20/0389]
[20/0390]
[20/0865]
2.4 GHz channel
AP1
AP2
AP3
AP4
STA1
STA2
STA3
Non-AP
MLD-
STA1
STA2
STA3
AP
MLD
AP1
AP2
AP3
AP4
6 GHz channel
ML element in Association Request declares a mapping by indicating the Link ID (better name is AP ID) corresponding to each non-AP STA [20/1274]
The choice (including number) of non-AP STAs to connect to AP STAs and the mapping to AP STAs belongs to non-AP MLD
That is, non-AP MLD decides the number and endpoints of the links, which is accepted or rejected by the AP MLD
Non-AP MLD decides the STAs and mapping to APs, based on many factors including capabilities (e.g., channels, number of spatial streams)

## Slide 6: More on ML configuration (2) Deciding the ML configuration at association time
Desired ML configuration (mapping between non-AP and AP STAs of MLDs) is specified through the ML IE in Association Request
AP MLD can reject a requested ML configuration for a variety of reasons
  Association Response must include proper error code and possibly a recommended ML reconfiguration in case of rejection
Non-AP MLD can (does not have to) include more per-STA profiles (including all) in ML IE than those present in the mapping
  Giving more information to AP to make recommendations at association time or later

## Slide 7: ML reconfiguration scenarios (1) Change in the AP endpoint of a link
AP performing ML reconfiguration to change the AP endpoint of a link
  Common scenarios
    Fewer non-AP STAs than AP STAs within associated MLDs (no 1:1 mapping), or
    AP STAs within the MLD tied to certain bands/channels (switching constraints, or radio in use)
AP
MLD
MLD1 (3 STAs) on 2.4, 5 and 6 GHz
MLD2 (2 STAs) on 2.4 and 5 GHz
MLD3 (2 STAs) using 2.4, 5 and 6 GHz
MLD1 (3 STAs) on 2.4, 5 and 6 GHz
MLD2 (2 STAs) on 2.4 and 6 GHz
MLD3 (2 STAs) using 2.4 and 6 GHz
AP1
AP2
AP3
Non-AP MLD with 2 STAs (connected to 2 APs of the AP MLD; this MLD needs ML reconfiguration)
Non-AP MLD with 3 STAs
(connected to 3 APs of the AP MLD; this MLD can simply disable the 5 GHz link)
2.4 GHz
6 GHz
5 GHz
Non-AP
MLD2-
Non-AP
MLD1-
Non-AP
MLD3-
STA1
STA2
STA3
STA1
STA2
STA3
STA1
STA2
Scenario: AP MLD associated with 3 MLDs, decides to move the 5 GHz operation of MLD2 and MLD3 to 6 GHz
5 GHz congestion or link loss,
or just traffic engineering
Move 5 GHz
endpoint …
... to 6 GHz
Non-AP MLD with 3 STAs
(no change in configuration)
Notes: AP2 will stay on 5 GHz for its connection to STA2 in MLD1. STA2 in MLD2 needs to switch to a new AP (AP3) for operation on 6 GHz.

## Slide 8: ML reconfiguration scenarios (2) Change in the non-AP endpoint of a link
AP performing ML reconfiguration to change the non-AP endpoint of a link
  Common scenarios
    Fewer AP STAs than non-AP STAs within associated MLDs (no 1:1 mapping)
    Non-AP STAs within an MLD tied to certain bands/channels (switching constraints)
  Non-AP MLDs should make the AP MLD aware of all their STAs and capabilities
MLD1 (2 STAs) on 2.4 and 5 GHz
MLD2 (3 STAs) on 2.4 and 5 GHz
MLD3 (2 STAs) on 2.4 and 5 GHz
MLD1 (2 STAs) on 2.4 and 6 GHz
MLD2 (3 STAs) on 2.4 and 6 GHz (through a new STA)
MLD3 (2 STAs) on 2.4 and 6 GHz
2.4
AP STA switching from 5 to 6 GHz; needs to connect to different non-AP STAs affiliated with non-AP MLDs
5
switching
to 6 GHz
STA2
STA3
STA1
Non-AP
MLD1-
Non-AP
MLD3-
STA1
STA2
STA1
STA2
AP
MLD
Non-AP
MLD2-
Non-AP MLD with 3 STAs
(STA2: Only 5 GHz capable,
STA3: Only 6 GHz capable,
new link on a new STA set up)
Non-AP MLD with 2 STAs
(one of the STAs performs a channel switch from 5 to 6GHz)
Non-AP MLD with 2 STAs
(one of the STAs performs a channel switch from 5 to 6GHz)
Channel switch from 5 to 6 GHz
Channel switch from 5 to 6 GHz
... to 6 GHz
Move 5 GHz
endpoint …
2.4 GHz
6 GHz
5 GHz congestion or link loss,
or just traffic engineering
Scenario: AP MLD associated with 3 MLDs, decides to move the 5 GHz operation of all MLDs to 6 GHz
Notes: STA2 in MLD1, and STA2 in MLD 3 are capable of both 5 and 6 GHz operation and will perform a channel switch. STA2 in MLD2 is capable of only 5 GHz, so moving the operation to 6 GHz requires using the new STA3.

## Slide 9: ML reconfiguration scenarios (3) Other scenarios (similar in nature)
Adding a link due to:
  Traffic load increases
  Current channel condition (range, reachability..) changes
  Or just new application starts to run, requiring new radio purposed for the type of application. E.g. activating a new 6GHz radio in response to VR application request.
Removing a link
  Operating on all available links may not always be the best option due to:
    Efficiency, power save
    Less management overhead
    Sticking with the dominant traffic component (e.g., keeping a TID with 5% of the traffic together with the only other TID carrying 95% of the traffic, in one link)
See [20/810] (Dynamic Link Set) for more discussion

## Slide 10: ML reconfiguration | Summary
ML reconfiguration: Changing the AP/non-AP STA mapping within the associated MLDs
Reconfiguration scenarios
  Changing one end of the link
    AP end
    Non-AP end
  Adding a link
  Removing a link
  Note: Changing one end of the link can be achieved through link removal and addition, but listed separately to emphasize possibly an efficient one-step solution
Mechanism for reconfiguration are not present in current framework
  Early discussion: [19/1943], [20/0741]
Reconfiguration signaling needed in R1
AP
MLD
Non-AP
MLD
Non-AP connecting to new AP
Fewer non-AP STAs than AP STAs within MLDs, or
AP STAs having band/channel switching constraints
AP
MLD
Non-AP
MLD
AP connecting to a new non-AP
Fewer affiliated AP STAs than affiliated non-AP STAs, or
affiliated non-AP STAs having band/channel switch constraints
AP
MLD
Non-AP
MLD
Adding | removing a link
New link was not set up at association time (adding a link),
or link removed permanently from protocol standpoint

## Slide 11: Operations that are not ML reconfiguration
TID switch
  Change of TID-to-link mapping
Channel switch
  Change of link-to-channel mapping
Changes to link power save state
None of these operations changes the mapping of AP/non-AP STAs decided at association time
AP
MLD
Non-AP
MLD
TID switch
Links remain the same, mapping between TIDs and links changes
TID 1
(split between
two links)
AP
MLD
Non-AP
MLD
Channel switch
No change from MLO perspective;
same link operating on a different channel
AP
MLD
Non-AP
MLD
Changes to link power save or TIDs
Links still set up at association time

## Slide 12: Discussion (1) Fit into the architecture
ML reconfiguration is a basic part of the architecture
  There are many use cases, but in general it is not even a question of why
  Framework should provide mechanisms to create, remove and possibly modify (in one step) links post association, without having to disassociate
The case of non-AP connecting to a different AP within the MLDs is remotely similar to BTM, but there is really no network wide transition
  For example, a BTM-like signaling can be used, but there is no re-association
  Assuming same PTK for all ML links, PTK can stay the same, and new GTK set up on new links

## Slide 13: Discussion (2) Symmetry, traffic hit
ML reconfiguration is generally a symmetric operation
  There is little difference between AP and non-AP STAs within two associated MLDs in terms of reasons to initiate a link switch
    Need to add/remove/replace a link can arise on any side – AP or non-AP
    Reconfiguration does not change the MLD-level network roles
Reconfiguration can be initiated by the AP MLD however
  Non-AP can trigger the operation, similar to sending a Query frame in BTM
Traffic loss during the reconfiguration must be minimized
  This is a common goal (with potentially common solutions) for all switching scenarios, TID-level or link-level
  Design elements from Fast Session Transfer (FST) can be borrowed
    Data plane ownership during reconfiguration, making sure MPDUs are received on new link(s) before declaring the operation successful

## Slide 14: Discussion (3) Disabled (“ghost”) links at association time
A non-AP MLD that does not match the AP MLD in terms of number of affiliated STAs can create “ghost” links at association time
  For example, non-AP MLD having a STA for each AP of the AP MLD
  Some links in an indefinite state of power save or “TID-free zone” after association
This is a scenario-dependent choice at association time, requiring
  Additional resources (unique MAC addresses, Link/AP IDs, information blocks …)
  Additional MAC features (e.g., power save)
Creating these links neither replaces nor is precluded by ML reconfiguration
  Not a substitute for general link addition (when new links are unavailable or not set up for any reason at association time), link removal (absent from all subsequent signaling), or modifying the link endpoints post association
  In some cases these do not even look similar, e.g., fewer AP STAs than non-AP STAs of different capabilities (see reconfiguration scenario #2)
  Matter of operation vs. configuration
Notes: Regarding ghost/disabled links: Association time ML configuration can be decided with or without extra links. ML reconfiguration is a fundamentally different problem – changing the configuration post association for any reason that was not present or clear at the time of association. With regards to implementation, and by way of example, if a non-AP MLD with two basebands associates with an AP MLD with 3

## Slide 15: Discussion (4) State preservation across ML reconfiguration
MLD-level states/parameters preserved across ML reconfiguration
  BlockAck operation, TIDs (TSs, TCs)
  Security (authentication, possibly PTK)
Link-level states/parameters initialized for new/modified links
  Power save states, TWT sessions
  Per-link security attributes (e.g., GTK)
ML reconfiguration is generally not a substitute for frequent switching between two or more links (as in enhanced multi-link single radio for example)
  Logic should be simple and straightforward; for example,
    TIDs mapped to links modified during ML reconfiguration (if those links have not been vacated) fall back to to TID-to-any link, until possibly mapped again
    Fresh new power save state

## Slide 16: Straw Poll 1 Link addition, removal
Do you agree to add to TGbe SFD in R1, a mechanism to
  Add a new link to an associated AP/non-AP MLD pair
  Remove a link from an associated AP/non-AP MLD pair
  Note: Mechanism to include advertising changes to available links
  Yes
  No
  Abstain

## Slide 17: Straw Poll 2 Changing the AP end of a link
Do you agree to add to TGbe SFD in R1, a mechanism to connect a non-AP STA of a non-AP MLD to a different AP of an associated AP MLD?
  Note: Non-AP MLD to be able to trigger the ML reconfiguration
  Yes
  No
  Abstain
AP
MLD
Non-AP
MLD

## Slide 18: Straw Poll 3 (Changing the non-AP end of a link)
Do you agree to add to TGbe SFD in R1, a mechanism to connect an AP STA of an AP MLD to a different non-AP STA of an associated non-AP MLD?
  Note: Non-AP MLD to be able to trigger the ML reconfiguration
  Yes
  No
  Abstain
AP
MLD
Non-AP
MLD

## Slide 19: References
[19/1943] 11-19-1943-09-00be-multi-link-management.pptx
[20/0389] 11-20-0389-03-00be-multi-link-discovery-part-1.pptx
[20/0390] 11-20-0390-03-00be-multi-link-discovery-part-2.pptx
[20/0412] 11-20-0412-01-00be-mlo-link-switching-method.pptx
[20/0669] 11-20-0669-00-00be-mld-transition.pptx
[20/0741] 11-20-0741-02-00be-indication-of-multi-link-information-follow-up.pptx [20/0751] 11-20-0751-01-00be-multi-link-setup-clarifications.pptx [20/0810] 11-20-0810-01-00be-dynamic-link-set.pptx [20/0908] 11-20-0908-00-00be-multilink-ts-operation.pptx
[20/1187] 11-20-1187-00-00be-multilink-setup-discussion.pptx
[20/1274] 11-20-1274-09-00be-mac-pdt-mlo-ml-ie-structure.docx
[20/1592] 11-20-1592-00-00be-ml-ie-in-authentication-frame.docx

## Slide 20: Backup slides

## Slide 21: Mechanisms with potential design reuse (1) BSS Transition Management (BTM)
AP recommending or requiring non-AP to transition to a new AP
Query, Request and Response frames
Neighbor Report element

## Slide 22: Mechanisms with potential design reuse (2) Fast Session Transfer (FST) overview
FST is designed to transfer a session (defined as one or more TSs) from one band/channel to another band/channel
  TCs should be able to use FST too; TS constraint is probably unnecessary
Equivalent of an MLO link is an independent association between the FST endpoints in each band/channel
  For example, the endpoints network roles (AP | non-AP relationship) can be different in the new band/channel
Operating parameters of each FST association are generally unavailable across BSSs in the FST framework, which means they need to be signaled at transition (through the Multi-band element)
  Architecturally, the two endpoints of an FST session do not manage their multiple MAC sublayers through a multiple MAC SME (MM-SME)
FST can switch one TID from one BSS to another BSS between two given multi-band devices
  Multi-band definitions are general enough to apply to two channels in the same band.

## Slide 23: Mechanisms with potential design reuse (3) FST session transfer protocol
Session transfer can be initiated by either end (initiator end, the other end called responder)
State machine with 4 states (Initial, Setup Completed, Transition Done, and Transition Confirmed), and the following state transition logic,
  “Initial” to “Setup Completed”: Successful exchange of FST Setup Request and FST Setup Response Action Ack frame; no timeout, retries left to initiator, MAC address-based arbitration between racing requests
  “Setup Completed” to “Transition Done”: After a STA-based or stream-based (TS-based) countdown to 0; counter initially loaded to LLT ×32 μs, where link loss timeout (LLT) is specified in the FST Setup Request frame; counter reset to initial value every time an individually addressed frame for the STA or for the specific TS in the STA is received from the peer STA
  “Transition Done” to “Transition Confirmed”: Successful exchange of FST Ack Request and FST Ack Response (both Action Ack frames) or other MPDUs in the new band/channel