## Slide 1: Multi-RU Indication in RU Allocation Subfield Follow up
Date: 2020-09-30
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
In [1], the following large MRU entries are proposed for MU PPDU, requiring a 9-bit RU Allocation subfield.
  Provide explicit indications for MRU position: receivers can identify the allocated MRU by just identifying one of the related RU Allocation subfields.
  However, more bits for indication are needed compared with the implicit methods (Opt B & Opt C) proposed in [2].
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  | 996 |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  | 996 |  |  |  |  |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  | 484 |  |  |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 484 |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
484 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  | 484 |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 484 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  | 484 |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 484 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  | 484 |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 484 |  |  |  | 8
Entries used in explicit 9-bit MRU indication [1] | 
11ax small RUs | 26 entries
Punctured RU242 and empty RU242/484/996 | 4 entries
11be small multi-RU | 24 entries
Large single RUs | 32 entries
Large multi-RUs | 208 entries
Unassigned RU242 (newly added) | 1 entry
9-bit table: Total 512 entries, entries used: 295, reserved: 217 | 

## Slide 3: Implicit MRU Indication
Here we summarize the implicit methods for MRU indication proposed in [2].
  Meaning
  The word implicit indicates that receivers need to identify all the RU Allocation subfields related to the MRU allocated to them.
  Benefits
  The explicit indication doesn’t need to check all the related subfields
  The implicit indication needs smaller entries for indication.
  Performance
  A receiver allocated a large MRU always needs to read the two content channels correctly to obtain the number of MU-MIMO users and the allocated MRU. Therefore, implicit indication doesn’t mean a higher error ratio compared with the explicit indication.
In this contribution we focus on reducing the RU Allocation subfield size from 9 bits to 8 bits by utilizing implicit indication for some high-overhead MRU combinations.

## Slide 4: RU Allocation Utilizing Implicit Indication
To reduce the entries in RU Allocation table, we suggest a mixed indication for large MRU by using implicit indication for 2*996+484 and 3*996+484. Then the large MRU table can be further simplified as the following two options
Large MRU entries needed in explicit indication | 
484+242 | 32 entries
996+484 | 32 entries
2*996+484 | 48 entries
3*996 | 32 entries
3*996+484 | 64 entries
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 / 3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
Opt. 1 (Opt. B in [2])
Opt. 2 (Opt. C in [2])
Note: Implicit M-RU signaling is limited to one per PPDU

## Slide 5: Motivation and Benefit
Motivation of mixed indication
  The needed numbers of entries 484+2*996 and 484+3*996 are large, leading to a 9-bit RU Allocation subfield.
  The entries 484+2*996 and 484+3*996 only occur in 320MHz. Lots of STAs operating in smaller bandwidth do not need to use these entries.
Benefit of mixed indication
  The mixed indication reduces the 295 used entries to 201 and 192 respectively, enabling an 8-bit RU Allocation subfield.
In the following we show the detailed designs of implicit methods.
  Opt. 1: 18 entries are needed.
  Opt. 2: 9 entries are needed.

## Slide 6: Multi-RU indication (Opt. 1)
Opt. 1 represents the Opt. B proposed in [2].
  Since all the RU Allocation subfields exist for non-compression mode for the baseline mode, the Rx can check which RU allocation subfields are indicated as an MRU entry. The MRU combination is indicated in each related RU Allocation subfield.
  Example
  to indicate the MRU 3*996+484, we can just use 9 entries to indicate the MRU with different number of user fields. The Rx can check all the RU Allocation subfields containing 3*996+484 to get its allocated MRU.
Proposed entries for 2*996+484 and 3*996+484
TBD | 996+996+484 | 9
TBD | 996+996+996+484 | 9
320MHz
996+996+996+484 for each related RU Allocation subfield

## Slide 7: Multi-RU indication (Opt. 2)
Opt. 2 represents the Opt. C proposed in [2].
  The Rx can check which RU allocation subfields are indicated as an MRU entry. The MRU types can be distinguished by the number of the implicit indication entries. In addition, 2*996+484 always comes with one punctured RU996, that also helps the differentiation.
  Example,
  to indicate the MRU 3*996+484, we can just use 9 entries to indicate the MRU with different user fields. The Rx can check all the RU Allocation subfields containing 2*996+484 / 3*996+484 to get its allocated MRU.
Proposed entries for 2*996+484 and 3*996+484
  3*996+484 and 2*996+484 will not occur at the same time. The MRU types can be distinguished by the number of related RU Allocation subfield.
TBD | 2*996+484 / 3*996+484 | 9
320MHz
Implicit indication for each related RU Allocation subfield

## Slide 8: Summary of Opt. 2 and Opt. 1
Common points
  Both options indicates two MRU combinations.
  Both options know the MRU position by checking all of the related RU Allocation subfields.
  2*996+484 always comes with one punctured RU996, helping the MRU differentiation for both options.
Different points
  Opt. 1 uses additional 9 entries to know the MRU combination (not MRU position) by the indication carried in the entries.
Since both options need to check all of the related RU Allocation subfields, Opt. 2 is preferred because of further reducing the entries. The MRU combination can also be easily distinguished by:
  Calculating the number of related RU Allocation subfields
  Identifying the punctured RU996
TBD | 996+996+484 | 9
TBD | 996+996+996+484 | 9
TBD | 2*996+484 / 3*996+484 | 9
Opt. 1 (Opt. B in [2])
Opt. 2 (Opt. C in [2])

## Slide 9
Discussed the explicit and implicit indications for large MRU.
Proposed to have a mixed indication for large MRU by using implicit indication for 2*996+484 and 3*996+484.
  The mixed indication reduces the 295 used entries to 201 and 192 respectively, enabling an 8-bit RU Allocation subfield.
Summary
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 / 3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
Opt. 1 (Opt. B in [2])
Opt. 2 (Opt. C in [2])

## Slide 10: Straw Poll #1
Do you agree to use an implicit MRU indication for the following MRU combinations in the RU Allocation subfield in MU PPDU?
  2*996+484
  3*996+484
  Y
  N
  A

## Slide 11: Straw Poll #2
Which option do you prefer for the implicit MRU indication?
  Opt. 1
  Opt. 2
  Y
  N
  A

## Slide 12: Straw Poll #3
Do you agree to add the following entries to the RU Allocation table in MU PPDU?
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9
3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9

## Slide 13: Straw Poll #4
Do you agree to add the following entries to the RU Allocation table in MU PPDU?
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 / 3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9

## Slide 14: Straw Poll #4
Do you agree to add the following entries to the RU Allocation table in MU PPDU?
 | 242 | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
242 |  | 484 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  | 242 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8
 |  | 484 |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
484 |  |  |  | 996 |  |  |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  |  |  | 484 |  |  |  |  |  |  |  |  |  | 8
996 |  |  |  | 484 |  |  |  |  |  |  |  |  |  |  |  | 8
 |  |  |  | 996 |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  |  |  |  |  | 996 |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  |  |  |  |  | 996 |  |  |  | 8
996 |  |  |  | 996 |  |  |  | 996 |  |  |  |  |  |  |  | 8
2*996+484 / 3*996+484 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9

## Slide 15: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
The RU Allocation subfield corresponding to 242-tone RU in the allowed combinations of 484+242 tone MRU is set to x (TBD) to indicate the zero users.
x is a value corresponding to the entry of ‘242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated’ in RU Allocation subfield table.
The RU Allocation subfield corresponding to 484-tone RU or 484-tone RU in the allowed combinations of 484+242 tone MRU and 996+484 tone MRU is set to y (TBD) to indicate the zero users.
y is a value corresponding to the entry of ‘484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated’ in RU Allocation subfield table.
The RU Allocation subfield corresponding to 996-tone RU or 996-tone RU in the allowed combinations of 996+484 tone MRU, 3×996 tone MRU, and 2×996-tone RU is set to z to indicate the zero users.
z is a value corresponding to the entry of ‘996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated’ in RU Allocation subfield table.

## Slide 16
IEEE 802.11-20/1138r4 Large M-RU Table and RU Table Ordering, Broadcom
IEEE 802.11-20/970r1 Multi-RU indication in RU allocation subfield, Huawei
IEEE 802.11-20/985r5 RU Allocation Subfield Design in EHT-SIG Follow up, Samsung
References