## Slide 1: 802.11be AP MLD Architecture Discussion
Date: 2020-08-10
Authors:

## Slide 2: Abstract
This presentation considers architecture concepts for TGbe AP MLDs. This follows ideas in some first presentations in the ARC SC sessions on Aug 6, Aug 24, and Sep 16.

## Slide 3: Need to sort out the functions within an AP MLD – which are “MLD” and which are “AP(s)”
Consider the MAC stack, as shown in 802.11 Figure 5-1:
Might be useful to ask, “Does this function have to be link-specific?” and/or “Is this function explicitly shared across the links?”
For now, ignore “legacy” AP, only affiliated AP(s) are considered

## Slide 4: “MLD-level”, or “per-AP/link-level”
All the figures/discussion presented in discussion so far have had some concept of some MAC functions that are per-link and “lower” in the stack, and some MAC functions that are shared across the links “at MLD level” and shown “higher” in the stack.
A proposed split/allocation of some MAC functions:
MLD (shared state across all links/can use any available link):
  Security Association/state; Encryption/Decryption; PN space [Motion 111]
  Sequence Number assignment; Receive reordering buffer [Motion 62]
  A-MSDU aggregation/de-aggregation [Must be done “above” encryption and reordering buffer]
  Retransmission [Motion 61, Motion 115]
Implementation choice (explicitly):
  Block-Ack scoreboarding [Motion 63. Motion 114. (Motion 112.) ]
Per-link:
  CCA, backoff, NAV, etc. [No change proposed – channel access is per-link (although there may be alignment done across the links, which puts restrictions on the EDCA access)]
  A-MPDU aggregation/de-aggregation [I’m just assuming, since this is such a low-level function]
  Address 1 matching [Allows per-link MAC address; allows per-link scoreboarding. Although, maybe this should be in the “Implementation choice” category?]

## Slide 5: “MLD-level”, or “per-AP/link-level”
Implications:
MLD:
  802.1X controlled/uncontrolled filtering
  RX/TX MSDU rate limiting
  A-MSDU aggregation/deaggregation
  (  bufferable MMPDUs generally inject into the stack here, so Action frames’ functions??)
  PS Defer Queuing
  Sequence Number assignment
  Packet Number assignment/Replay detection
  Block Ack Buffering and Reordering
  MPDU Encryption/Decryption
  Duplicate Detection
Per-link:
  Control frames (RTS/CTS, Acks, NDP, etc.)
  Management frames (non-bufferable):
    Beacon generation: has link-specific capabilities/attributes
    Probe Request/Response, Authentication/Association/Reassociation Request/Response

## Slide 6
So, something like: