## Slide 1: Discussion on Soft AP MLD Definition
Date: 2020-10-09
Authors:

## Slide 2: Abstract
In this contribution, we review the struggle the 11be TG faces to reach consensus on a definition of Soft AP MLD.

## Slide 3: The Origin
11be TG assumes that a regular AP MLD is capable of simultaneously transmitting and receiving (STR) frames on its radio chains, but NOT necessarily for a Non-AP MLD
Extensive effort in 11be TG has been devoted to the operation of a Non-STR Non-AP MLD
  If a Non-AP MLD has 3 links, typically there is no sufficient isolation between 5GHz and 6 GHz RF chains

## Slide 4: Soft AP configured from Non-STR Non-AP MLD
Quite some members have NO interest to define or enable Non-STR AP MLD
  From performance point of view, it is claimed there may not be sufficient gain, therefore it is preferred not to allow low-end AP MLD products on the market
  Non-STR AP operation is conceived as complicated, which could hurt the overall timeline of the 11be TG development
This leaves a blank area: If a Non-STR Non-AP MLD is configured as an AP MLD, it could not utilize both 5GHz and 6GHz links
  Soft AP is one of the most important use cases for a client device

## Slide 5: Then the Need of A Definition
Finally, 11be TG agrees to enable such use case in SFD
  “Move to define mechanisms to support the operation of a Non-STR AP MLD in R1? The mechanisms are limited to instantiate a Non-STR Non-AP MLD as a Soft AP that could utilize all its links under TBD conditions. The exact language to govern such scope is TBD.”
When it comes to write the specification text, we need a subject to be written for, that is a new term needing a name or definition

## Slide 6: Fact-checking
There is NO definition on the Soft AP in IEEE 802.11 Specification
However, it is a common understanding that Soft AP is the result of configuring Wi-Fi clients into an AP with limited functionality
It is not necessary to define Soft AP for pre-11be devices as the IEEE 802.11 society lives very well without it for past 3 decades
Based on current agreement in 11be, the AP MLD are all STR! How about Soft APs instantiated by the Non-STR Non-AP MLDs?
  We are not allowed to call them “Non-STR APs”
  Solution: define terms “Soft AP MLD” and “Non-STR Soft AP MLD”

## Slide 7: Version 1
An MLD, consists of more than one affiliated STAs of a Non-AP MLD , where these STAs are operated only as APs.
Limit the scope such that by only considering a Non-AP MLD
The Soft AP MLD operates the STAs insides a Non-AP MLD as APs, rather than these Non-AP STAs are APs

## Slide 8: Complaints
One member strongly argued against this definition because
  A Non-AP MLD only has Non-AP STAs
  How can a Non-AP STA be an AP? This is a contradiction by those definitions on AP and Non-AP STA in the specification
Our response
  When Soft AP MLD operates the original Non-AP STAs, the STAs inside Soft AP MLD has already been changed, it is NOT the original Non-AP STAs anymore
  We cannot convince the member not to interpret the way he is reading the text

## Slide 9: Version 2
Soft AP MLD: an AP MLD, whose affiliated STAs use the same antenna connectors as a set of Non-AP STAs that can be instantiated at different times
Motivation for this wording
  Emphasize the Soft AP MLD uses the same RF chains as some Non-AP STAs, so we avoid “the Non-AP STA is an AP” concern
  And the Non-AP STAs using the same RF chains are instantiated either earlier or later, not at the same time
  The Soft AP MLD inherits the constraints of the Non-AP STAs

## Slide 10: New Complaints
What happens with Soft AP MLD and Non-AP MLD, are they coexisting, time sharing the resources?
  A: we are only concerned with Soft AP MLD operation, anything else is out of the scope
Can you add ”battery powered” as a constraint to limited scope to mobile devices?
  A: high-end setup box, home appliance are not battery powered
  A: it is not clear what ”battery powered” means in the spec
What is the scope of Soft AP MLD, is it supporting “UL-OFDMA”? Without knowing the scope, it is problematic…
  A: it is an unfair question. In current spec, when AP and Non-AP are defined, we never claim its PHY/MAC capability. Additionally, how Soft AP MLD works will be explicitly discussed and defined in the corresponding section. It is too early to sort these details at this stage.

## Slide 11: Other Suggestions
Soft AP MLD: An AP MLD, whose capabilities are limited. (Similar style of Mobile AP definition in WFA)
Complaints:
  what does “capabilities are limited” really mean?
  It does not explicitly mention the origin of such device from “Non-AP MLD”!

## Slide 12: Multiple Shackles Were Put on the Soft AP MLD Definition
Must explicitly mention its origin “Non-AP MLD”
Different opinions whether battery should be added as power source
What is the clear scope of capabilities?
Some members felt uncomfortable with the rare term “antenna connectors”
Some members were concerned about other Non-AP STAs that are possibly co-existing with the Soft AP MLD, even the definition is about Soft AP MLD only

## Slide 13
Suggestions on How to Move Forward?

## Slide 14: Reference
[1] Non-STR AP Operation, 11-20-0755-01-00be-non-str-ap-operation.pptx
[2] IEEE 802.11-2016
[3] tgbe-spec-framework

## Slide 15: Appendix: AP, Non-AP STA, AP MLD and Non-AP MLD [2][3]
AP: An entity that contains one station (STA) and provides access to the distribution services, via the wireless medium (WM) for associated STAs. An AP comprises a STA and a distribution system access function (DSAF).
STA: A logical entity that is a singly addressable instance of MAC and PHY interface to the wireless medium (WM)
Non-AP STA: A STA that is not contained within an AP
AP MLD: An MLD, where each STA affiliated with the MLD is an AP
Non-AP MLD: An MLD, where each STA affiliated with the MLD is a non-AP STA