## Slide 1: TXOP rules to reduce worst-case latency
Date: 2020-10-23
Authors:
Name | Affiliations | Address | Phone | email
Thomas Handte | Sony Corporation |  |  | Thomas.Handte (at) sony.com
Dana Ciochina |  |  |  | Dana.Ciochina (at) sony.com
Daniel Verenzuela |  |  |  | Daniel.Verenzuela (at) sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud (at) sony.com
Liangxiao Xin |  |  |  | Liangxiao.Xin (at) sony.com

## Slide 2: Introduction (1/2)
Low latency service is an important application scenario for 11be
  Various submissions addressed
    Indication of low latency traffic [1-4]
    Protected period for low latency traffic [3,5,6]
    New EDCA queue [4,7]
    Scheduling provision information [8,9]
    QoS negotiation [1,3]
    TXOP resource agreements [10]
The goal of these proposals is to reduce average and/or worst-case latency
  Some target to limit retransmissions by e.g. protected period
  However, retransmissions may still occasionally happen e.g. due to collisions or rate sounding
Retransmissions have large impact to worst-case latency
  Goal of this submission is to provide improvements to existing technology in “missing response” case

## Slide 3: Introduction (2/2)
Current behavior in missing response case depends on the position of the failed PPDU within a TXOP [11]
  If the failed PPDU is the initial PPDU within a TXOP, a STA
    Invokes backoff procedure with incremented CW[AC]
  If the failed PPDU is a non-initial PPDU within a TXOP, a STA has the following options
    Perform PIFS recovery,
      Continue if CS mechanism indicates idle at TxPIFS boundary and remaining TXNAV is sufficient
    Invoke backoff procedure within same TXOP with incremented CW[AC], or
    Wait for TXNAV timer to expire and perform backoff with CW[AC] = CWmin[AC]
Suitability for low latency traffic
  Anything that causes a STA to increment CW[AC] is harmful as it potentially provides various TXOPs to other ACs or STAs
    This applies for option a), option c), or option b) if CS mechanism indicates non-idle
  Option d) may be suitable if missing response occurs towards the end of a TXOP
Focus of this submission are options a), b), or c), i.e. the cases when
  A missing response occurs to an initial PPDU within a TXOP
  A missing response occurs to a non-initial PPDU within a TXOP and the channel is detected as busy

## Slide 4: Goal of the submission
This submission provides new rules for TXOP configuration to mitigate worst case latency
  The rules are applicable for the “missing response” case under the conditions of previous slide
    i.e. if a STA increments its CW[AC].
Example for a “missing response”
  STA A transmits a PPDU to STA B that requires a response
  A response frame is not received by STA A
  STA A initiates backoff procedure and retransmits data
Definition of a new behavior of STA A in case of a “missing response”
  The new behavior is applicable for
    the AC in which the collision was caused, or
    all ACs except the AC in which the collision was caused
  Regular behavior applies once retransmission was successful or related MSDU lifetime is exceeded

## Slide 5: TXOP content restriction (1/2)
Issue
  Once a new TXOP is obtained by STA A, it may hold not only retransmitted data but also other data e.g. from same or other TID
    This behavior is favorable to maximize throughput, but causes latency
  Latency is caused to
    STA A’s own link, if latency is measured until BAck is received
    Other links if a collision was the reason for the backoff
Example

## Slide 6: TXOP content restriction (2/2)
Solution
  Restrict content of a TXOP after a missing response
  Two options for a TXOP to contain no more than
    retransmitted data
    retransmitted data and data of previously agreed TIDs (e.g. same TID) if available
Benefits
  Avoids delay until a response is received
  Allows other STA to access medium sooner in case of a collision
Example

## Slide 7: TXOP shortening (1/2)
Scenario
  A STA has low-latency traffic and best-effort traffic mapped to different ACs, e.g. AC_VO and AC_BE
Issue
  The TXOP of other ACs impedes retransmission in a missing response case
    Assume LL_AC to be any AC that contains data to be retransmitted, e.g. of a low latency TID
    If an AC other than LL_AC is first to transmit and has a full queue, its TXOP impedes retransmission
      Note that TXOP sharing is not applicable because primary AC has non-empty queue

## Slide 8: TXOP shortening (2/2)
Solution
  Reduce TXOP limit of ACs other than LL_AC in case LL_AC holds data to be retransmitted
  Extent of shortening is TBD
    Could be a function of retry counter, e.g. with
    i.e. TXOP limits is halved with every retransmission
Benefits
  Time in between CW count downs gets lower, hence time until retransmission lowers
  Allows the LL_AC to get channel access sooner

## Slide 9: Effect of the proposed rules (1/2)
The proposed rules allow to balance between throughput and latency
  TXOP utilization reduces; hence throughput lowers due to more fragmented channel access
  However, latency improves in the critical situation of a “missing response”
There are two sources of the latency gain
  Self-induced, i.e. a STA that applies the TXOP rules has a latency advantage
    E.g. BAck arrives earlier or can retransmit earlier
  Induced by other STAs, i.e. a particular STA can transmit earlier because another STA applies the TXOP rules
    E.g. earlier chance to retransmit after a collision

## Slide 10: Effect of the proposed rules (2/2)
Sometimes behavior of some STAs can not be influenced, e.g. legacy STA or OBSS STA
  The self-induced latency gain is still present, but what is the impact of STAs not following the proposed TXOP rules?
Analysis of two scenarios
  Scenario A
    STA-A and STA-B apply the proposed TXOP rules
    STA-A and STA-B are missing a response from their peer STAs due to a collision
    Performance of each STA is given in comparison to both STAs using current TXOP rules
  Scenario B
    As Scenario A, but STA-A uses existing TXOP rules (e.g. legacy STA), STA-B applies the proposed TXOP rules
 | Latency | TXOP utilization
STA-A | Advantage | Unchanged
STA-B | Unchanged | Reduced for traffic not related to retransmission
 | Latency | TXOP utilization
STA-A | Advantage | Reduced for traffic not related to retransmission
STA-B | Advantage | Reduced for traffic not related to retransmission
Scenario A
  In scenario B, the disadvantage of STA-B may be balanced by setting different TXOP limit for (legacy) STA-A
Scenario B

## Slide 11: Simulation (1/3)
Simulation Scenario
  2 STAs transmitting uplink traffic to an AP
    Both STAs have full buffer
  EDCA
    AIFSN=3, CWmin=15, CWmax=1023
    Initial max TXOP duration is 5.5ms
  Minstrel rate adaption
  Shortened max TXOP duration is 2.8ms
  STA-A follows the TXOP rules, whereas STA-B does not
  Analysis of the latency gain of STA-B induced by STA-A for a latency metric measured without (w/o) Ack response or with (w/) Ack response
AP
STA-A
STA-B

## Slide 12: Simulation (2/3)
Proposed rules reduce worst-case latency
  Difference plays out for CDF>0.9 as a missing response is a prerequisite for the TXOP rule to be applied
Reference [12]

## Slide 13: Simulation (3/3)
Gains are the order of 0.5 to 6ms for the considered scenario
  Corresponds to 2% to 16%
  Tendency is that TXOP content restriction achieves smaller gain than TXOP shortening
    The retransmission goes into two TXOPs, because rate adaption lowers MCS
      First TXOP has unchanged size but only the second is shortened. The likelihood that a TXOP of the considered STA with retrans- mitted data comes after the second TXOP is small.
      With TXOP shortening, all TXOPs are shortened, increasing the likelihood that a TXOP of the considered STA comes after at least one shortened TXOP.
Gain certainly depends on
  How many STAs are part of the collision domain
    For large collision domain triggered access or TWT is favorable
  How many STAs are following the new TXOP rules
  TXOP shortening parameters (here length is halved)
0.5-1ms
1-2ms
2.5-3ms
1-2ms
3.5-6ms
3-6ms
gain

## Slide 14: Applicability
The effectiveness of the proposed rules depends on traffic type, applied ACs, environment, and overall traffic load
  Applicability of the proposed TXOP rules should be adjustable to requirements and constraints
  Legacy STA can be controlled by setting a different (lower) TXOP limit
AP or STA may negotiate with its peer the applicability for its traffic streams among other parameters
  The negotiation may be part of low-latency or RTA session initiation
Negotiation/ signaling is TBD
  ADDTS request/response or scheduling session [8,9] could be reused
  A bitmap could be envisioned to indicate applicability of each rule
    Applicability should be made TID or AC specific (TBD)

## Slide 15: Conclusion
TXOP rules as defined today may hinder low latency service
  It is important to revisit how a TXOP is configured after a missing response
We propose two rules for TXOP that alleviate low latency service
  TXOP content restriction
    After a missing response, the TXOP that contains the retransmitted data shall contain no more than the data to be retransmitted, except data from agreed TIDs
  TXOP shortening
    After a missing response, the maximum TXOP duration of ACs other than the one that suffered a missing response, shall be shortened
Benefits
  Lower latency until successful response to retransmission
  Earlier chance to retransmit in collision case
  Both rules allow to balance throughput in favor of latency
Applicability
  AP and STA may negotiate appropriate settings according to requirements and constraints

## Slide 16: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
An AP may request a STA for a TID mapped to any AC0 to restrict the content of a TXOP of AC0 to contain only MPDUs with retry subfield set to 1 and any required acknowledgements, if
  no response frame was received for a transmitted PPDU that contained at least one MPDU soliciting an immediate response frame, and
  the missing response frame caused the transmitting STA to increment CW[AC0].
  The restriction is valid until no more MPDUs are pending for retransmission for the requested TID within AC0 or related MSDU lifetime is exceeded.

## Slide 17: Straw Poll #2
Do you agree to add the following to the TGbe SFD?
An AP may request a STA to shorten the maximum TXOP duration of one or more ACs, if
  - no response frame was received for a transmitted PPDU that contained at least one MPDU soliciting an immediate response frame, and
  the missing response frame caused the transmitting STA to increment CW[AC0].
  The shortened maximum TXOP duration is applicable for all agreed ACs except AC0.
  The shortened maximum TXOP duration is valid until no more MPDUs are pending for retransmission in AC0 or related MSDU lifetime is exceeded.
  Extent of the TXOP shortening is TBD
  If this rule is applicable for all TIDs mapped to AC0 is TBD

## Slide 18: References
[1] 11-20/418r4 Low latency service in 802.11be
[2] 11-20/463r3 Priority Access Support Options for NS/EP Serveices
[3] 11-20/163r1 Low Latency Enhancements for R1
[4] 11-19/1175r0 Channel Access Category
[5] 11-20/1350r0 Enhancements for QoS and low latency in 802.11be R1
[6] 11-20/1046r4 Protected TWT Enhancement for Latency Sensitive Traffic
[7] 11-20/1041r2 EDCA queue for RTA
[8] 11-20/1006r1 New Methods To Meet Low Latency Requirement
[9] 11-20/1076r0 Traffic indication of latency sensitive applications
[10] 11-20/1670r0 Low Latency resource agreements
[11] Draft P802.11REVmd_D4.0
[12] 11-19/1298r1 IEEE 802.1 TSN – An Introduction