## Slide 1: TXOP rules to reduce worst-case latency
Date: 2020-12-18
Authors:
Name | Affiliations | Address | Phone | email
Thomas Handte | Sony Corporation |  |  | Thomas.Handte (at) sony.com
Dana Ciochina |  |  |  | Dana.Ciochina (at) sony.com
Daniel Verenzuela |  |  |  | Daniel.Verenzuela (at) sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud (at) sony.com
Liangxiao Xin |  |  |  | Liangxiao.Xin (at) sony.com

## Slide 2: Introduction (1/2)
Low latency service is an important application scenario for 11be
  Various submissions addressed
    Indication of low latency traffic [1-4]
    Protected period for low latency traffic [3,5,6]
    New EDCA queue [4,7]
    Scheduling provision information [8,9]
    QoS negotiation [1,3]
    TXOP resource agreements [10]
The goal of these proposals is to reduce average and/or worst-case latency
  Some target to limit retransmissions by e.g. protected period
  However, retransmissions may still occasionally happen e.g. due to collisions
Retransmissions have large impact to worst-case latency
  Goal of this submission is to provide improvements to existing technology in “missing response” case

## Slide 3: Introduction (2/2)
Current behavior in missing response case depends on the position of the failed PPDU within a TXOP [11]
  If the failed PPDU is the initial PPDU within a TXOP, a STA
    Invokes backoff procedure with incremented CW[AC]
  If the failed PPDU is a non-initial PPDU within a TXOP, a STA has the following options
    Perform PIFS recovery,
      Continue if CS mechanism indicates idle at TxPIFS boundary and remaining TXNAV is sufficient
    Invoke backoff procedure within same TXOP with incremented CW[AC], or
    Wait for TXNAV timer to expire and perform backoff with CW[AC] = CWmin[AC]
Suitability for low latency traffic
  Any option that causes a STA to increment CW[AC] is harmful as it potentially provides various TXOPs to other ACs or STAs
    This applies for option a), option c), or option b) if CS mechanism indicates non-idle
  Option d) may be suitable if missing response occurs towards the end of a TXOP
Focus of this submission are options a), b), or c), i.e. the cases when
  A missing response occurs to an initial PPDU within a TXOP
  A missing response occurs to a non-initial PPDU within a TXOP and the channel is detected as busy

## Slide 4: Goal of the submission
This submission provides new rules for TXOP configuration to mitigate worst case latency
  The rules are applicable for the “missing response” case under the conditions of previous slide
    i.e. if a STA increments its CW[AC].
Example for a “missing response”
  STA A transmits a PPDU to STA B that requires a response
  A response frame is not received by STA A
  STA A initiates backoff procedure and retransmits data
Definition of a new behavior of STA A in case of a “missing response”
  Regular behavior applies once retransmission was successful or related MSDU lifetime is exceeded

## Slide 5: TXOP content restriction (1/3)
Scenario
  PPDUs of two STAs collide
Issue
  Once a new TXOP is obtained by a STA, it may hold not only retransmitted data but also other data e.g. from same or different TID to exploit TXOP
  TXOP exploitation is favorable to maximize throughput, but causes latency to collision opponent
    Duration of other data frame exchange adds to retry latency of collision opponent

## Slide 6: TXOP content restriction (2/3)
Solution
  Restrict content of a TXOP after a missing response
  After a missing response, a TXOP shall contain no more than
    retransmitted data and data of previously announced TIDs (e.g. same TID)
Benefits
  Allows collision opponent (STA C) to access medium sooner

## Slide 7: TXOP content restriction (3/3)
Applicability
  TXOP content restriction applies to the AC in which the collided data units reside
Advantages
  If colliding ACs are same
    Content restriction prioritizes frames of an AC which are pending for retransmission across a BSS
      Particularly important if multiple TIDs are mapped to same AC
  If colliding ACs are different
    Content restriction alleviates impact of a low priority AC transmitting before high priority AC
    Example
      AC_VI transmits before AC_VO with a probability of ~0.25 (assuming default EDCA parameter set [11])
      Without TXOP content restriction, AC_VI may exploit its TXOP limit by adding further data
        This causes latency to AC_VO traffic
      Note that by default low priority ACs have typ. longer TXOP limit than high priority ACs [11]

## Slide 8: TXOP shortening (1/3)
Scenario
  Each STA has low-latency traffic and other traffic mapped to different ACs
    Assume LL_AC to be any AC that contains low-latency traffic to be retransmitted
    Assume that the AC that contains other traffic has full queue
Issue
  The TXOP of the AC other than LL_AC impedes retransmission within LL_AC
  TXOP sharing is not applicable, because AC of other traffic has non-empty queue

## Slide 9: TXOP shortening (2/3)
Solution
  Reduce TXOP limit of ACs other than LL_AC after a missing response
  Extent of shortening is TBD
    Could be a function of retry counter, e.g. with
      i.e. TXOP limits are halved with every retransmission
Benefits
  Time in between CW count downs gets lower, hence time until retransmission lowers
  Thus, the LL_AC gets channel access sooner

## Slide 10: TXOP shortening (3/3)
Applicability
  TXOP shortening applies to all ACs except the AC in which the collision was caused
  The extent of the TXOP shortening is defined in advance (e.g. by signaling)
  Only STAs that detect a missing response apply TXOP shortening
Advantages
  TXOP shortening is most useful if TXOP sharing can’t be applied
    Traffic of low priority AC is of type full buffer, e.g. streaming data

## Slide 11: Usage of the proposed rules
The proposed rules allow to balance between throughput and latency
  TXOP utilization reduces; hence throughput lowers due to more fragmented channel access
  However, latency improves in the critical situation of a “missing response”
There are two sources of the latency gain
  Self-induced, i.e. a STA that applies the proposed TXOP rules has a latency advantage
    For example, a STA may transmit earlier because it applies TXOP shortening
  Induced by other STAs, i.e. a STA has a latency advantage because another STA applies the proposed TXOP rules
    For example, a STA may transmit earlier because another STA applied TXOP content restriction
Need for signaling
  AP signals the appropriate TXOP rules to ensure that the latency gain induced by other STAs is present
    Similar as TXOP limit of current spec [11]
  Detailed signaling TBD
    Could be part of EDCA parameter element, ADDTS request/response, or scheduling session [8,9]
Impact of legacy STAs
  AP may control legacy STAs via different TXOP limit
    Any throughput disadvantage compared to legacy STA may be balanced with lower TXOP limit

## Slide 12: Simulation (1/3)
Simulation Scenario
  2 STAs transmitting uplink traffic to an AP
    Both STAs have full buffer
  EDCA
    AIFSN=3, CWmin=15, CWmax=1023
    Initial max TXOP duration is 5.5ms
  Minstrel rate adaption
  Shortened max TXOP duration is 2.8ms
  STA-A follows the TXOP rules, whereas STA-B does not
  Analysis of the latency gain of STA-B induced by STA-A for a latency metric measured without (w/o) Ack response or with (w/) Ack response
AP
STA-A
STA-B

## Slide 13: Simulation (2/3)
Proposed rules reduce worst-case latency
  Difference plays out for CDF>0.9 as a missing response is a prerequisite for the TXOP rule to be applied
Reference [12]

## Slide 14: Simulation (3/3)
Gains are the order of 0.5 to 6ms for the considered scenario
  Corresponds to 2% to 16%
  Tendency is that TXOP content restriction achieves smaller gain than TXOP shortening
    The retransmission goes into two TXOPs, because rate adaption lowers MCS
      First TXOP has unchanged size but only the second is shortened. The likelihood that a TXOP of the considered STA with retrans- mitted data comes after the second TXOP is small.
      With TXOP shortening, all TXOPs are shortened, increasing the likelihood that a TXOP of the considered STA comes after at least one shortened TXOP.
Actual gain depends on
  How many STAs are part of the collision domain
    For large collision domain triggered access or TWT is favorable
  How many STAs are following the new TXOP rules
  TXOP shortening parameters (here length is halved)
0.5-1ms
1-2ms
2.5-3ms
1-2ms
3.5-6ms
3-6ms
gain

## Slide 15: Conclusion
TXOP rules as defined today may hinder low latency service
  It is important to revisit how a TXOP is configured after a missing response
Two rules for TXOP are proposed that alleviate low latency service
  TXOP content restriction
    After a missing response, the TXOP that contains the retransmitted data shall contain no more than the data to be retransmitted, except data from announced TIDs
  TXOP shortening
    After a missing response, the maximum TXOP duration of ACs other than the one that suffered a missing response, shall be shortened
Benefits
  Lower latency until successful response to retransmission
  Earlier chance to retransmit in collision case
  Both rules allow to balance throughput in favor of latency
Usage
  AP signals appropriate settings according to traffic requirements and constraints

## Slide 16: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
An AP may request a STA to restrict the content of a TXOP of AC0 to contain only MPDUs with retry subfield set to 1, MPDUs of indicated TIDs, and any required acknowledgements, if
  no response frame was received for a transmitted PPDU that contained at least one MPDU soliciting an immediate response frame, and
  the missing response frame caused the transmitting STA to increment CW[AC0].
  The restriction is valid until no more MPDUs in AC0 are pending for retransmission or related MSDU lifetime is exceeded.

## Slide 17: Straw Poll #2
Do you agree to add the following to the TGbe SFD?
An AP may request a STA to shorten the maximum TXOP duration of one or more AC0, if
  - no response frame was received for a transmitted PPDU that contained at least one MPDU soliciting an immediate response frame, and
  the missing response frame caused the transmitting STA to increment CW[AC0].
  The shortened maximum TXOP duration is applicable for all indicated ACs except AC0.
  The shortened maximum TXOP duration is valid until no more MSDUs are pending for retransmission in AC0 or related MSDU lifetimes are exceeded.
  Extent of the TXOP shortening is TBD

## Slide 18: References
[1] 11-20/418r4 Low latency service in 802.11be
[2] 11-20/463r3 Priority Access Support Options for NS/EP Serveices
[3] 11-20/163r1 Low Latency Enhancements for R1
[4] 11-19/1175r0 Channel Access Category
[5] 11-20/1350r0 Enhancements for QoS and low latency in 802.11be R1
[6] 11-20/1046r4 Protected TWT Enhancement for Latency Sensitive Traffic
[7] 11-20/1041r2 EDCA queue for RTA
[8] 11-20/1006r1 New Methods To Meet Low Latency Requirement
[9] 11-20/1076r0 Traffic indication of latency sensitive applications
[10] 11-20/1670r0 Low Latency resource agreements
[11] Draft P802.11REVmd_D4.0
[12] 11-19/1298r1 IEEE 802.1 TSN – An Introduction