## Slide 1: A TXOP rule to reduce worst-case latency
Date: 2021-02-02
Authors:
Name | Affiliations | Address | Phone | email
Thomas Handte | Sony Corporation |  |  | Thomas.Handte (at) sony.com
Dana Ciochina |  |  |  | Dana.Ciochina (at) sony.com
Daniel Verenzuela |  |  |  | Daniel.Verenzuela (at) sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud (at) sony.com
Liangxiao Xin |  |  |  | Liangxiao.Xin (at) sony.com

## Slide 2: Introduction (1/2)
Low latency service is an important application scenario for 11be
  Various submissions addressed
    Indication of low latency traffic [1-4]
    Protected period for low latency traffic [3,5,6]
    New EDCA queue [4,7]
    Scheduling provision information [8,9]
    QoS negotiation [1,3]
    TXOP resource agreements [10]
The goal of these proposals is to reduce average and/or worst-case latency
  Recent decision by TGbe to introduce R-TWT as protected period for low-latency traffic [6]
  However, retransmissions may still occasionally happen, e.g., due to collisions or rate sounding
Retransmissions have large impact to worst-case latency
  Goal of this submission is to provide improvements to existing technology in “missing response” case

## Slide 3: Introduction (2/2)
Current behavior in missing response case depends on the position of the failed PPDU within a TXOP [11]
  If the failed PPDU is the initial PPDU within a TXOP, a STA
    Invokes backoff procedure with incremented CW[AC]
  If the failed PPDU is a non-initial PPDU within a TXOP, a STA has the following options
    Perform PIFS recovery,
      Continue if CS mechanism indicates idle at TxPIFS boundary and remaining TXNAV is sufficient
    Invoke backoff procedure within same TXOP with incremented CW[AC], or
    Wait for TXNAV timer to expire and perform backoff with CW[AC] = CWmin[AC]
Suitability for low latency traffic
  Any option that causes a STA to increment CW[AC] is harmful as it potentially provides various TXOPs to other ACs or STAs
    This applies for option a), option c), or option b) if CS indicates non-idle
  Option d) may be suitable if missing response occurs towards the end of a TXOP
Focus of this submission are options a), b), or c), i.e., cases when
  A missing response occurs to an initial PPDU within a TXOP
  A missing response occurs to a non-initial PPDU within a TXOP and the channel is detected as busy

## Slide 4: Goal of the submission
This submission provides a new rule for TXOP configuration to mitigate worst case latency
  The rule is applicable for the “missing response” case under the conditions of previous slide
    i.e., if a STA increments its CW[AC].
Example for a “missing response”
  STA A transmits a PPDU to STA B that requires a response
  A response frame is not received by STA A
  STA A initiates backoff procedure and retransmits data
Definition of a new behavior of STA A in case of a “missing response”
  Regular behavior applies once retransmission was successful or related MSDU lifetime is exceeded

## Slide 5: Assumptions
We assume that
  At least one STA has low-latency traffic and other traffic mapped to a different AC
    The low-latency traffic is mapped to AC0 which may be any high priority AC (e.g. AC_VO)
    The other traffic is mapped to different AC than AC0 (e.g. AC_VI) and has full queue
      E.g., streaming data
  R-TWT is in place and shrinks the number of STAs accessing the medium at same time
    During TWT SP at least two STAs intend to access the channel
      This may be intentionally or because STAs don’t consent with R-TWT agreement
  EDCA is applied within R-TWT

## Slide 6: TXOP limit shortening (1/3)
Scenario
  After R-TWT SP starts STA A and STA B transmit at same time and PPDUs collide
  After Ack timeout and CW increase, STAs content again to retransmit
    However, AC ≠ AC0 has smaller backoff counter and transmits first
Issue
  The TXOP of the AC other than AC0 impedes retransmission of AC0
  TXOP sharing is not applicable, because AC of other traffic has full buffer

## Slide 7: TXOP limit shortening (2/3)
Solution
  Shorten TXOP limit of ACs other than AC0 after a missing response
  Extent of TXOP limit shortening is TBD
    Could be a function of retry counter, e.g., with
Benefits
  Time in between backoff count downs gets lower, hence time until retransmission lowers
  AC0 can access the channel sooner

## Slide 8: TXOP limit shortening (3/3)
Applicability
  TXOP limit shortening applies to all ACs except the AC in which the collision was caused (AC0)
  The extent of the TXOP limit shortening is defined in advance (e.g. by EDCA parameter element)
  STAs that detect a missing response apply TXOP limit shortening
    There is no signaling among STAs
A STA is supplied with different TXOP limits
  One limit applies for initial transmission, whereas another limit applies for retransmission
Advantages
  TXOP limit shortening is most useful if TXOP sharing can’t be applied
    Traffic of low priority AC is of type full buffer, e.g. streaming data

## Slide 9: Example
AP signals EDCA Parameter values to STAs
  incl. new TXOP limits for retransmissions
A STA that observes a missing response in AC0 (primary AC) applies the shortened TXOP limit for all ACs other than AC0
Example: Collision in AC_VO
  Shortened TXOP limits are: (AC_BK / AC_BE / AC_VI / AC_VO) = (1.264ms / 1.264ms / 2.048ms / 2.080ms)
AC | CWmin | CWmax | AIFSN | TXOP limit | 
 |  |  |  | if CW=CWmin | Otherwise
AC_BK | aCWmin | aCWmax | 7 | 2.528 ms | 1.264 ms
AC_BE | aCWmin | aCWmax | 3 | 2.528 ms | 1.264 ms
AC_VI | (aCWmin+1)/2-1 | aCWmax | 2 | 4.096 ms | 2.048 ms
AC_VO | (aCWmin+1)/4-1 | aCWmin+1/2-1 | 2 | 2.080 ms | 1.040 ms

## Slide 10: Simulation (1/3)
Simulation Scenario
  2 STAs transmitting uplink traffic to an AP
    Both STAs have full buffer
  EDCA
    AIFSN=3, CWmin=15, CWmax=1023
    Initial TXOP limit is 5.5ms
  Minstrel rate adaption
  Shortened TXOP limit is 2.8ms
  STA-A follows the TXOP limit shortening, whereas STA-B does not
  Analysis of the latency gain of STA-B induced by STA-A
    Latency is measured without (w/o) Ack response or with (w/) Ack response
AP
STA-A
STA-B

## Slide 11: Simulation (2/3)
The proposed rule reduces worst-case latency
  Difference plays out for CDF>0.9 as a missing response is a prerequisite for the TXOP rule to be applied
Reference [12]

## Slide 12: Simulation (3/3)
Gains are in the order of 0.5 to 6ms for the considered scenario
  Corresponds to 2% to 16%
Actual gain depends on
  How many STAs are part of the collision domain
    For large collision domain triggered access or R-TWT is required
  How many STAs are following the TXOP rule
  TXOP limit shortening parameters
    TXOP limit is divided by two in simulation
1ms
2ms
3ms
2ms
6ms
6ms
gain

## Slide 13: Conclusion
TXOP rules as defined today may hinder low latency service
  It is important to revisit how a TXOP is configured after a missing response
TXOP limit shortening is proposed to alleviate low latency service
  After a missing response, the TXOP limit of ACs other than the one that suffered a missing response, shall be shortened
Benefits
  Lower latency until successful response to retransmission
  Earlier chance to retransmit
  The proposed rule allows to balance throughput in favor of latency
Usage
  AP signals TXOP limit shortening parameters according to traffic requirements and constraints
  A STA that detects a missing response, applies the TXOP limit for shortened TXOP

## Slide 14: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
An AP may request STAs to shorten the TXOP limit of one or more AC0, if
  - no response frame was received for a transmitted PPDU that contained at least one MPDU soliciting an immediate response frame, and
  the missing response frame caused the transmitting STA to increment CW[AC0].
  The shortened TXOP limit is applicable for all indicated ACs except AC0.
  The shortened TXOP limit is valid until no more MSDUs are pending for retransmission in AC0 or related MSDU lifetimes expired.
  Signaling is TBD
  The extent of the TXOP limit shortening is TBD

## Slide 15: References
[1] 11-20/418r4 Low latency service in 802.11be
[2] 11-20/463r3 Priority Access Support Options for NS/EP Serveices
[3] 11-20/163r1 Low Latency Enhancements for R1
[4] 11-19/1175r0 Channel Access Category
[5] 11-20/1350r0 Enhancements for QoS and low latency in 802.11be R1
[6] 11-20/1046r12 Protected TWT Enhancement for Latency Sensitive Traffic
[7] 11-20/1041r2 EDCA queue for RTA
[8] 11-20/1006r1 New Methods To Meet Low Latency Requirement
[9] 11-20/1076r0 Traffic indication of latency sensitive applications
[10] 11-20/1670r0 Low Latency resource agreements
[11] Draft P802.11REVmd_D5.0
[12] 11-19/1298r1 IEEE 802.1 TSN – An Introduction