## Slide 1: TSPEC for Low Latency for R1
Date: 2020-10-6
Authors:
Name | Affiliation | Address | Phone | Email
Duncan Ho | Qualcomm Inc. | 5665 Morehouse Dr. San Diego, CA 92121 |  | dho@qti.qualcomm.com
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Abhishek Patil | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 

## Slide 2: Intro
For a STA of a non-AP MLD to request low latency service, the STA needs to convey its expected traffic pattern and QoS requirements to the AP
To provide this information we can leverage the existing TSPEC defined in 802.11

## Slide 3: What is a TSPEC Element?
The TSPEC element contains the set of parameters that define the characteristics and QoS expectations of a traffic flow, in the context of a particular STA, for use by the HC or PCP and STA(s) or a mesh STA and its peer mesh STAs in support of QoS traffic transfer using the procedures defined in 11.4 (TS operation) and 11.22.16.3 (GCR procedures).

## Slide 4: TSPEC Element
TSPEC has 28 fields - 57 or 59 octets
  There are a lot of fields. Do we need all of them for 11be?
  We highlighted 14 fields that we think are useful for 11be
 | B0 | B1 B4 | B5 B6 | B7 B8 | B9 | B10 | B11 B13 | B14 B15 | B16 | B17 B23
 | Traffic Type | TSID | Direction | Access Policy | Aggregation | APSD | User -Priority | TS Info Ack Policy | Schedule | Reserved
Bits: | 1 | 4 | 2 | 2 | 1 | 1 | 3 | 2 | 1 | 7
TS Info field format |  |  |  |  |  |  |  |  |  | 

## Slide 5: Proposals
Define a new IE* (e.g., TSPEC-lite) that has the following properties:
  Indicates expected traffic pattern and QoS requirement of a TID in a specific traffic direction
    The traffic can be periodic or aperiodic
  Contains a subset of fields of the TSPEC IE and some new fields (e.g., Age to discard)
  Can be included as an IE in other MGMT frames (e.g., TWT Request, TID-to-Link Mapping/ML setup, etc.)
    Not coupled with AddTS and the original TSPEC
  Extensible (note: original TSPEC element is not extensible for non-DMG STAs)
  Includes a TID bitmap to indicate which TID(s) the same parameters apply to (i.e., same parameters in the TSPEC-lite will be applied to all indicated TIDs)
    The AP can serve the TIDs independently according to the parameters
Note: We can still use TSPEC IE, and make it extensible, since it is sent to STAs supporting reception.

## Slide 6: TSPEC-lite Fields
Field Name | Definition (shortened) | Notes
Element ID (1 octet), Element ID Extension (1 octet) | Element ID, Element ID Extension set by <ANA> | Basics
Length (1 octet) | Length of the payload | Basics
TID Bitmap (1 octet) | The TID Bitmap specifies which TIDs the element applies to. If the bit position corresponding to the TID value is set to 1, this elements apply to that TID. One or more bits can be set to 1. | New field
Direction (2 bits) | The Direction subfield specifies the direction of data carried by the TS as defined in Table 9-160 indicating: UL, DL, Direct link, Symmetrical bi-directional link. | Inherited from TSPEC
Minimum Service Interval (4 octets) | The Minimum Service Interval field (#4696)contains an unsigned integer that specifies the minimum interval, in microseconds, between the start of two successive SPs. | Inherited from TSPEC
Maximum Service Interval (4 octets) | The Maximum Service Interval field (#4696)contains an unsigned integer that, when the TSPEC element is for the admitting of HCCA streams, specifies the maximum interval, in microseconds, between the start of two successive SPs. | Inherited from TSPEC
Inactivity Interval (4 octets) | The Inactivity Interval field contains an unsigned integer that specifies the minimum amount of time, in microseconds, that can elapse without arrival or transfer of an MPDU belonging to the TS before this TS is deleted by the MAC entity at the HC. | Inherited from TSPEC
Suspension Interval (4 octets) | The Suspension Interval field contains an unsigned integer that specifies the minimum amount of time, in microseconds, that can elapse without arrival or transfer of an MSDU belonging to the TS before the generation of successive QoS(+)CF-Poll is stopped for this TS. | Inherited from TSPEC
Service Start time (4 octets) | The Service Start Time field contains an unsigned integer that specifies the time, expressed in microseconds, when the first scheduled SP starts. The service start time indicates to the AP the time when a STA first expects to be ready to send frames and a power saving STA needs to be awake to receive frames. | Inherited from TSPEC

## Slide 7: The TSPEC-lite Fields
Field Name | Definition (shortened) | Notes
Minimum Data Rate (4 octets) | The lowest data rate specified at the MAC SAP, for transport of MSDUs or A-MSDUs belonging to this TS | Inherited from TSPEC
Mean Data Rate (4 octets) | The average data rate specified at the MAC SAP, for transport of MSDUs or A-MSDUs belonging to this TS | Inherited from TSPEC
Peak Data Rate (4 octets) | The Peak Data Rate field indicates the maximum allowable data rate specified at the MAC SAP for transport of MSDUs or A-MSDUs belonging to this TS within the bounds of this TSPEC element. | Inherited from TSPEC
Burst Size | The Burst Size field (#4696)contains an unsigned integer that specifies the maximum burst, in octets, of the MSDUs or A-MSDUs belonging to this TS that arrive at the MAC SAP at the peak data rate. | Inherited from TSPEC
Delay Bound (4 octets) | Unsigned integer that specifies the maximum amount of time, in microseconds, allowed to transport an MSDU or A-MSDU belonging to the TS in this TSPEC, measured between the time marking the arrival of the MSDU, or the first MSDU of the MSDUs constituting an A-MSDU, at the local MAC sublayer from the local MAC SAP and the time of completion of the successful transmission or retransmission of the MSDU or A-MSDU to the destination. The completion of the MSDU or A-MSDU transmission includes the relevant acknowledgment frame transmission time, if present. | Inherited from TSPEC
Discard Age (2 octets) | Unsigned integer that specifies the maximum age of an MSDU, in milliseconds, after which the transmitter shall discard the MSDU. | New field

## Slide 8: SP1
Do you agree to add to the TGbe SFD:
  Create a new IE to convey the expected QoS requirement of a traffic stream from a non-AP MLD to an AP-MLD
    Details of the IE is TBD but expect to reuse some fields of the TSPEC element if applicable

## Slide 9: SP2
Do you agree to add to the TGbe SFD:
  The new IE shall contain at least the following fields from the TSPEC element:
    Direction
    Minimum Service Interval
    Maximum Service Interval
    Inactivity Interval
    Suspension Interval
    Service Start time
    Minimum Data Rate
    Mean Data Rate
    Peak Data Rate
    Burst Size
    Delay Bound
  Notes:
    The traffic flow can be between two non-AP MLDs
    TBD if more fields are needed