## Slide 1: UL Sync Channel Access Procedure
Date: 2020-10-29
Authors:

## Slide 2: Straw Poll
Do you support an STA that is affiliated with an MLD shall follow the channel access procedure described below?
  The STA may initiate transmission on a link when the medium is idle and one of the following conditions are met:
    The backoff counter of the STA reaches zero on a slot boundary of that link.
    The backoff counter of the STA is already zero, and the backoff counter of another STA of the affiliated MLD reaches zero on a slot boundary of the link that the other STA operates.
  When the backoff counter of the STA reaches zero, it may choose to not transmit and keep its backoff counter at zero.
  If the backoff counter of the STA has already reached zero, it may perform a new backoff procedure. CW[AC] and QSRC[AC] is left unchanged.

## Slide 3: Backup
Highlight of MLO synchronous channel access procedure learned from current backoff procedure:
  The STA may initiate transmission on a link when the medium is idle and one of the following conditions are met:
    The backoff counter of the STA reaches zero on a slot boundary of that link.
    The backoff counter of the STA is already zero, and the backoff counter of another STA of the affiliated MLD reaches zero on a slot boundary of the link that the other STA operates.
  When the backoff counter of the STA reaches zero, it may choose to not transmit and keep its backoff counter at zero.
  If the backoff counter of the STA has already reached zero, it may perform a new backoff procedure. CW[AC] and QSRC[AC] is left unchanged.
Notes: `

## Slide 4: Backup
Highlight of MLO synchronous channel access procedure learned from current backoff procedure:
  For example,
    When the backoff counter of the STA1 reaches zero, the STA1 does not transmit and keep its backoff counter at zero based on the rule b.
    The STA1 initiates a TXOP based on the rule a-2.
    The STA2 initiates a TXOP based on the rule a-1.
9 | 8 | 7 | 6 | 5
4 | 3 | 2 | 1 | 0
TX A-MPDU
MLD
Rx BA
STA2
STA1
4 | 3 | 2 | 1 | 0
TX A-MPDU
Rx BA
Rule b
Rule a-1
Rule a-2

## Slide 5: Backup
Highlight of MLO synchronous channel access procedure learned from current backoff procedure:
  The STA may initiate transmission on a link when the medium is idle and one of the following conditions are met:
    The backoff counter of the STA reaches zero on a slot boundary of that link.
    The backoff counter of the STA is already zero, and the backoff counter of another STA of the affiliated MLD reaches zero on a slot boundary of the link that the other STA operates.
  When the backoff counter of the STA reaches zero, it may choose to not transmit and keep its backoff counter at zero.
  If the backoff counter of the STA has already reached zero, it may perform a new backoff procedure. CW[AC] and QSRC[AC] is left unchanged.

## Slide 6: Backup
Busy
Highlight of MLO synchronous channel access procedure learned from current backoff procedure:
1 | 0
Empty
Busy
6 | 5 | 4 | 3 | 2
3 | 2 | 1 | 0
TX A-MPDU
Busy
Empty
8 | 7 | 6 | 5 | 4
AIFS
1 | 0
TX A-MPDU
Rx BA
1 | 0
3 | 2
Rule c
Rule c
MLD
STA2
STA1
MLD
STA4
STA3

## Slide 7: References
[1] https://mentor.ieee.org/802.11/dcn/20/11-20-0993-02-00be-sync-ml-operations-of-non-str-device.pptx (D. Akhmet and L. Cariou)
[2] https://mentor.ieee.org/802.11/dcn/20/11-20-1053-01-00be-synchronous-multi-link-transmission-of-non-str-mld.pptx (Y. Seok and D. Ho)