## Slide 1: Feasibility Study of Human Pose and Occupancy Classification using mmWave WiFi Beam Attributes
Date: 2020-11-03
Authors:
Name | Affiliation | Address | Phone | Email
Pu (Perry) Wang | Mitsubishi Electric Research Laboratories (MERL) | 201 Broadway, Cambridge, MA 02139, USA |  | pwang@merl.com
Jianyuan Yu |  |  |  | jyu@merl.com
Toshiaki Koike-Akino |  |  |  | koike@merl.com
Ye Wang |  |  |  | ywang@merl.com
Philip V. Orlik |  |  |  | porlik@merl.com
Notes: September 2012

## Slide 2: Abstract
This contribution is a continuation of
  20/1074r1 WLAN Localization and Sensing With Mid-Grained Channel Measurements
  which adopts mid-grained channel measurement – mmWave beam attributes (e.g., beam SNRs) for indoor sensing and monitoring applications
This contribution reports feasibility study of indoor device-free sensing (e.g., human pose & seat occupancy) using beam SNRs from commercial 60-GHz WiFi routers.
https://www.merl.com/demos/mmBSF
Pose Classification
(Seat) Occupancy
Sensing

## Slide 3: Background
WLAN sensing mainly uses two kinds of WiFi channel measurements
  Coarse-grained RSSI (received signal strength indicator)
    In the unit of dBm, easy to access, coarse channel information
  Fine-grained CSI (channel state information)
    Complex amplitudes at freq.-domain OFDM subcarriers (802.11g/n/ac at sub-6 GHz)
    WiFi CSI can be accessible from commercial routers in earlier 2010s
    The CSI-based fingerprinting outperforms the RSSI-based fingerprinting
    (DeepFi’16, PhaseFi’17, BiLoc’18, CSI-Net’19, Person-in-WiFi’19)
CSI sequences for 2 Tx & 3 Rx
Picture sources: [7]
RSSI
  Mid-grained beam attributes (e.g., beam SNRs)
    Data collection and exchange (between AP and User) are already defined in 802.11ad standards during beam training (therefore, minimal additional overhead)
    Spatial-domain channel measurements at mmWave bands, weighted by beam patterns
    Can be accessed from commercial 60-GHz WiFi routers [10, 11]
Beam SNRs over 36 probing beams
Picture sources: https://www.netspotapp.com/ and [7]
Picture source: https://www.netspotapp.com
Picture copyright@MERL

## Slide 4: (mmWave) Beam SNRs
2-D illustration
Two Sweeping Beam Patterns
(Irregular beampatterns measured in a chamber – TU Darmstadt [9])
h20
h24=22.69 dB

## Slide 5: Feasibility Study (I): Pose Classification
One router as Tx and the other Rx using commercial-off-the-shelf 802.11ad routers [10,11]
One subject performing 8 poses
Beam SNRs were collected for different poses
5 independent data sessions for cross-session performance evaluation
  32-element array in one of its fingers
  30+ highly irregular probing beams for mmWave beam training
Picture source: [10, 11]
Picture source: TP-Link
Picture sources: MERL
Picture sources: MERL

## Slide 6: 60-GHz Beam SNR Measurements
Data Session A
Data Session D
  There is a magnitude variance (jump)
  The beam SNR patterns preserve the feature for each pose over different sessions
Picture sources: MERL
  Less impacted by environmental changes (people movements in nearby rooms)
  Less sensitive to minor motions (e.g., finger).

## Slide 7
16
5-GHz CSI Measurements
Data Session B
Data Session D
  Significantly larger amount of data: 16 streams x 234 subcarriers with a 100-Hz frame rate
  Easy recognizable patterns for different poses
Picture sources: MERL
  For Poses 4 & 7, CSI patterns are changed over different data sessions
  Potentially due to environmental changes, e.g., people movement in nearby room, which cannot be always labeled in the data.
  More sensitive to minor motions (e.g., finger)

## Slide 8
16
4-Layer MLP
beamSNR-MLP (88.8%)
Picture sources: MERL
CSI-MLP (79.74%)
  Performance can be further improved by other NN architectures (e.g., ResNet, Autoencoder-based classification). Will be introduced in future contributions.

## Slide 9
16
Impact of Subject Body Size
beamSNR-MLP (88.8%)
beamSNR-MLP (64.97%)
  The same subject in the training and test dataset
  Confusion matrix is averaged over cross-session validation
  One subject in the training data
  A different subject (smaller body size) in the test dataset
  Confusion matrix is averaged over cross-session validation
  Performance can be improved by including more subjects in the training dataset
  Pose classification that is robust to subject variation and environmental changes will be valuable
Picture sources: MERL

## Slide 10: Feasibility Study (II): Seat Occupancy
One router as Tx and the other Rx using commercial-off-the-shelf 802.11ad routers [10,11]
One subject occupied one of 4 chairs + 2 subjects occupied two of 4 chairs
Beam SNRs were collected for different seat occupancy patterns
5 independent data sessions for cross-session performance evaluation
Picture source: TP-Link
Picture sources: MERL

## Slide 11: 60-GHz Beam SNR Measurements

## Slide 12
16
beamSNR-MLP (91.2%)
Picture sources: MERL
CSI-MLP (80.93%)

## Slide 13: Conclusions
This contribution demonstrated the potential of a mid-grained channel measurements (beam attributes, e.g., SNRs) for device-free indoor sensing and monitoring (pose classification & seat occupancy sensing).
Subject and environmental invariance will be valuable for robust WLAN sensing.

## Slide 14: References
[1] CSI-based Wi-Fi Sensing: Results and Standardization Challenges, IEEE 802.11-19/1769r1
[2] 802.11 sensing: Applications, feasibility, standardization, IEEE 802.11-19/1626r1
[3] Wi-Fi sensing in 60GHz band, IEEE 802.11-19/1551r1
[4] Wi-Fi sensing, IEEE 802.11-19/1164
[5] Wi-Fi sensing: cooperation and standard support, IEEE 802.11-19/1416
[6] “Spotfi: Decimeter Level Localization using WiFi”, Manikanta Kotaru, Kiran Joshi, Dinesh Bharadia, Sachin Katti
[7] X. Wang, L. Gao, S. Mao and S. Pandey, "DeepFi: Deep learning for indoor fingerprinting using channel state information," WCNC, New Orleans, LA, 2015, pp. 1666-1671
[8] "Towards Context-assisted Indoor Navigation", Ayyalasomayajula Roshan, Aditya Arun, Chenfeng Wu, Sanatan Sharma, Deepak Vasisht, Abhishek Sethi, Dinesh Bharadia
[9] D. Steinmetzer, D. Wegemer, M. Schulz, J. Widmer, and M. Hollick, ‘‘Compressive millimeter-wave sector selection in off-the-shelf IEEE 802.11ad devices,’’ in Proc. 13th Int. Conf. Emerg. Netw. EXperiments Technol., Nov. 2017
[10] D. Steinmetzer D. Wegemer and M. Hollick Talon Tools: The Framework for Practical IEEE 802.11ad Research 2018 [online] Available: https://seemoo.de/talon-tools/
[11] M. Schulz D. Wegemer and M. Hollick Nexmon: The C-Based Firmware Patching Framework 2017
[12] Z. Wang, K. Jiang, Y. Hou, W. Dou, C. Zhang, Z. Huang, et al., "A survey on human behavior recognition using channel state information" IEEE Access vol. 7 pp. 155986-156024 2019. 32.
[13] M. Pajovic, P. Wang, T. Koike-Akino, H. Sun and P. V. Orlik "Fingerprinting-based indoor localization with commercial mmWave WiFi—Part I: RSS and beam indices" GLOBECOM 2019, pp. 1-6, Dec. 2019.
[14] P. Wang, M. Pajovic, T. Koike-Akino, H. Sun and P. V. Orlik "Fingerprinting-based indoor localization with commercial mmWave WiFi—Part II: Spatial beam SNRs" GLOBECOM 2019, pp. 1-6 Dec. 2019.
[15] T. Koike-Akino, P. Wang, M. Pajovic, H. Sun and P. V. Orlik "Fingerprinting-based indoor localization with commercial mmWave WiFi: A Deep Learning Approach”, IEEE Access, Vol. 8, pp. 84879-84892, 2020.
[16] J. Yu, P. Wang , T. Koike-Akino, Y. Wang, and P. V. Orlik " Human Pose and Seat Occupancy Classification with Commercial mmWave WiFi”, GLOBECOM Workshop on JSAC, December, 2020.
[17] W. Wu, N. Cheng, N. Zhang, P. Yang, W. Zhuang, and X. Shen "Fast mmWave beam alignment via correlated bandit learning" IEEE Trans. Wireless Comm., vol. 18 no. 12 pp. 5894-5908 Dec 2019.