## Slide 1: EHT NDPA Partial BW Info Design
Date: 2020-10-30
Authors:

## Slide 2: Introduction
It is agreed that EHT NDPA frame reuses the same structure as HE NDPA [1, 2, 3, 4].
  STA Info field has 4 bytes.
Partial BW Info.
  11be feedback resolution increases from RU26 to RU242 [5], to reduce complexity and modes.
  11be has much better support of channel puncturing.
  [RU start, RU end] design does not support puncturing cases well.

## Slide 3: NDPA Partial BW Info Design
Several table-based designs are proposed [1, 2, 4]
  7 bit table to include all allowed large RU/MRUs
    A new table needs to be designed.
  Reuse 9-bit TB RU table
    Only entries corresponds to RU/MRU>=242 are valid.
  The feedback index parsing is more complex than 11ax.
Bitmap is a natural way to signal punctured feedback request.

## Slide 4: Bitmap Design
Partial BW Info using bitmap: 9 bits
  1 bit indicates bitmap resolution: 20MHz or 40MHz
    Set to 0 for 20MHz for NDP BW<320MHz.
    Set to 1 for 40MHz for NDP BW=320MHz.
      Note: 320MHz NDP only allows puncturing granularity of 40MHz.
  8-bit bitmap to indicate the request for each resolution size
    B0=0: 8-bit bitmap signals feedback request for each 20MHz subchannel within 160MHz.
    B0=1: 8-bit bitmap signals feedback request for each 40MHz subchannel within 320MHz.
Resolution | Feedback Bitmap
B0 B1 B8

## Slide 5: Partial BW Info Bitmap: examples

## Slide 6: Discussions on Bitmap Proposal
Simple implementation for both beamformer and beamformee.
  8-bit bitmap, no table needed
  Beamformer: indicate which 20MHz/40MHz to feedback.
  Beamformee: directly map to feedback tone indices.
Good flexibility of feedback request
  Allowed modes for R1: any modes that are valid RU/MRU [1,2,4].
  Easier to accommodate R2 and future extension.

## Slide 7: SP
Do you agree to use 9-bit to signal NDPA partial BW info field as below?
  1 bit indicates bitmap resolution: 20MHz or 40MHz
    Set to 0 for 20MHz for NDP BW<320MHz.
    Set to 1 for 40MHz for NDP BW=320MHz.
  8-bit bitmap to indicate the request for each resolution size
Resolution | Feedback Bitmap
B0 B1 B8

## Slide 8: References
[1] Eunsung Jeon and etc., “Partial Bandwidth Feedback for Multi-RU”, 11-20/950.
[2] Chenchen Liu and etc., “EHT NDPA Frame Design Discussion”, 11-20/1015.
[3] Cheng Chen and etc., “EHT NDPA frame design”, 11-20/1435.
[4] Sameer Vermani and etc., “NDPA and MIMO Control Field Design for EHT”, 11-20/1436.
[5] Bin Tian and etc., “EHT Punctured NDP and Partial Bandwidth feedback”, 11-20/1161

## Slide 9: Appendix
Valid RU/MRU Example :
  8-bit map: B1B2B3B4B5B6B7B8
  If (C0+C1==0 || D0==1 || D1==1), disallowed; // 0000, 1001, 0110, 1010, 0101.
  elseif (C0+C1=8); // No puncture
  elseif (C0+C1=7); // 20 punctured in 160MHz or 40 punctured in 320MHz
  elseif (C0+C1=6 && (C0==4 || C1==4)); // 40 punctured in 160MHz or 80 punctured in 320MHz
  elseif (C0+C1=5 && (B1B2=00 || B7B8==00)); // (996*2+484): special two-hole cases in 320MHz
  elseif (C0==0 || C1==0); // RU/MRU <=80MHz: 996, 484+242, 484, 242
  else  disallowed
  Note: ^ is XOR operation, & is AND operation
C0 = (B1+B2+B3+B4), C1= (B5+B6+B7+B8)
D0 = ((B1^B2)&(B3^B4)), D1= ((B5^B6)&(B7^B8))