## Slide 1: EHT NDPA Partial BW Info Design
Date: 2020-10-30
Authors:

## Slide 2: Introduction
It is agreed that EHT NDPA frame reuses the same structure as HE NDPA [1, 2, 3, 4].
  STA Info field has 4 bytes.
Partial BW Info field uses 7~9 bits.
  11be feedback resolution increases from RU26 to RU242 [5], to reduce complexity and modes.
  11be has much better support of channel puncturing.
  [RU start, RU end] design does not support puncturing cases well.

## Slide 3: NDPA Partial BW Info Design
Table-based designs: proposed [1, 2, 4, 6]
  ~7 bit table to include all allowed large RU/MRUs
    A new table needs to be designed.
  Reuse TB RU table (TBD 9-bit)
    Only entries corresponds to RU/MRU>=242 are valid.
  The feedback index parsing is more complex than 11ax.
    Table entry  RU/MRU  feedback tone indices
Bitmap is a natural way to signal punctured feedback request. [6]
  bitmap  feedback tone indices
  [6] provides a two-level bitmap design, a little sophisticated.

## Slide 4: Bitmap Design
Partial BW Info using bitmap: 9 bits
  1 bit indicates bitmap resolution: 20MHz or 40MHz
    Set to 0 for 20MHz for NDP BW<320MHz.
    Set to 1 for 40MHz for NDP BW=320MHz.
      Note: 320MHz NDP only allows puncturing granularity of 40MHz.
  8-bit bitmap to indicate the request for each resolution size
    B0=0: 8-bit bitmap signals feedback request for each 20MHz subchannel within 160MHz.
    B0=1: 8-bit bitmap signals feedback request for each 40MHz subchannel within 320MHz.
Resolution | Feedback Bitmap
B0 B1 B8

## Slide 5: Partial BW Info Bitmap: examples

## Slide 6: Discussions on Bitmap Proposal
Simple implementation for both beamformer and beamformee.
  8-bit bitmap, no table needed
  Beamformer: indicate which 20MHz/40MHz to feedback.
  Beamformee: directly map the bitmap to feedback tone indices.
Good flexibility of feedback request
  Partial BW feedback not necessarily one-to-one mapping with RU/MRU
    For R1: mainly for supporting OFDMA beamforming, can limit the allowed modes to valid RU/MRU [1,2,4].
    For other beamforming overhead reduction usage and R2 MRU extension, more flexibility can be needed.
  Bitmap based design be easily relaxed to support for the extension.
  Table based design is limited by the number of Reserved entries.

## Slide 7: Discussions on Bitmap Proposal (2)
20MHz resolution for 320MHz NDP. [2, 6]
  The goal is to support 20MHz STAs.
    No 20MHz-only STA in 6GHz
    20MHz-operating STA: may not be interested in partial BW feedback.
  320MHz NDP to sound 20MHz STA need to be defined. [7]
  320MHz NDP puncturing granularity is 40MHz.
  320MHz OFDMA based on 20MHz resolution is also challenging.
  The proposed bitmap design may be extended to support 20MHz.
    We don’t see the necessity for that.

## Slide 8: SP
Do you agree to use 9-bit to signal NDPA partial BW info field as below?
  1 bit indicates bitmap resolution: 20MHz or 40MHz
    Set to 0 for 20MHz for NDP BW<320MHz.
    Set to 1 for 40MHz for NDP BW=320MHz.
  8-bit bitmap to indicate the request for each resolution size
Resolution | Feedback Bitmap
B0 B1 B8

## Slide 9: References
[1] Eunsung Jeon and etc., “Partial Bandwidth Feedback for Multi-RU”, 11-20/950.
[2] Chenchen Liu and etc., “EHT NDPA Frame Design Discussion”, 11-20/1015.
[3] Cheng Chen and etc., “EHT NDPA frame design”, 11-20/1435.
[4] Sameer Vermani and etc., “NDPA and MIMO Control Field Design for EHT”, 11-20/1436.
[5] Bin Tian and etc., “EHT Punctured NDP and Partial Bandwidth feedback”, 11-20/1161
[6] Eunsung Park and etc. “Partial BW Info Field Design in NDPA”, 11-20/1814.
[7] Rui Cao and etc. “EHT beamformee NDP and partial BW feedback support”, 11-20/1807r0

## Slide 10: Appendix
Valid RU/MRU Example :
  8-bit map: B1B2B3B4B5B6B7B8
  If (C0+C1==0 || D0==1 || D1==1), disallowed; // 0000, 1001, 0110, 1010, 0101.
  elseif (C0+C1=8); // No puncture
  elseif (C0+C1=7); // 20 punctured in 160MHz or 40 punctured in 320MHz
  elseif (C0+C1=6 && (C0==4 || C1==4)); // 40 punctured in 160MHz or 80 punctured in 320MHz
  elseif (C0+C1=5 && (B1B2=00 || B7B8==00)); // (996*2+484): special two-hole cases in 320MHz
  elseif (C0==0 || C1==0); // RU/MRU <=80MHz: 996, 484+242, 484, 242
  else  disallowed
  Note: ^ is XOR operation, & is AND operation
C0 = (B1+B2+B3+B4), C1= (B5+B6+B7+B8)
D0 = ((B1^B2)&(B3^B4)), D1= ((B5^B6)&(B7^B8))