## Slide 1: Support of high-resolution imaging sensors
Date: 2020-11-02
Authors:
Name | Affiliation | Address | Phone | Email
Naftali Chayat | Vayyar Imaging Ltd. | Shabazi 26, Yehud, Israel |  | Naftali.Chayat@Vayyar.com
Mark Popov |  |  |  | 
Damian Hoffman |  |  |  | 
Tsachi Rosenhouse |  |  |  | 
Zivi Nadiri |  |  |  | 
Ian Podkamien |  |  |  | 
Notes: Link level simulation

## Slide 2: Outline
Overview of 802.11 baseline and existing sensor technologies
Need for high-resolution sensing technologies
Provisions required for high resolution sensing technologies

## Slide 3: Resolution vs. #antennas
The most commonplace technology today is MIMO radar approach, with M transmit antennas by N receive antennas
Provides M*N measurements, and accordingly M*N spatial patterns “beams” that can be discriminated
  May discriminate azimuth or azimuth-elevation
Some additional info is available from Doppler or micro-Doppler variations
Some additional accuracy available through “superresolution” techniques
Still – raw resolution matters
  Dense scenarios, elevation resolution

## Slide 4: Commonplace sensors today
Typical sensors today use 1-3 transmit antennas and 3-4 receive antennas
  Cost and complexity of RF
  Size of antenna arrays and cost of special substrates
  Antenna arrays in a limited space on chip packages
One exception – sensors based on 24 transmit * 24 receive channel ASIC
802.11ay is advocated as a “technology toolbox” for TGbf
  8 antennas?

## Slide 5: Need for high resolution
Multiple applications require high resolution:
  Counting multiple people in spaces
  Discriminating people by body size and posture
  Per-person identification of vital signs
  Improved palm-based and hand-based gesture recognition
Superresolution techniques are good for few point-targets, give little in complex target cases
  Multiple scatter points in a single voxel
Doppler discrimination is of help, yet in increases detection time and depends on motion patterns.
Raw resolution counts.

## Slide 6: Monostatic vs. Bi-static cases
Bistatic sensing is being discussed and promoted in 802.11bf
Yet, we believe that monostatic sensing will be the dominant use case
  Allows higher complexity sensor device
  Does not incur STA complexity
  Does no demand 802.11bf-supporting station
  Does not depend on presence of STA
  Does not incur communication overhead for reporting measurements

## Slide 7: Monostatic sensor – minimal provisions
Monostatic sensor basically requires airtime allocation for sensing waveforms
Arbitrary complexity can be implemented on the sensing AP/STA side
Can use standard or non-standard waveforms – the station receives itself, no need to interoperate.
Provides room for innovation and added performance
We recommend providing mechanisms for allocating “sensing airtime” without further restriction on the content

## Slide 8: Provisions for supporting hi-res imaging
The 802.11bf has to address high resolution imaging systems
Need to support configurable sensing waveforms for large #antennas
  20 and more
Supporting airtime allocation for monostatic sensing using arbitrary waveforms