## Slide 1: Phase Shift Feedback Response – Supporting Slides
Date: Nov 3, 2020
Authors:

## Slide 2: Issue with current Phase Shift Feedback Protocol
When one side, the ISTA or the RSTA, feeds back the PS-TOA, it does not get feedback from the other side that it can use with its PSTOA to compute RTT.
The PSTOA reporting side is forced to also measure the TOA, if it wants to compute RTT.
  (Even though measuring TOA is required to be supported it is not required to be done all the time.)
Also, it has been shown that if the other side measures a more accurate TOA, then the first side can benefit from feeding back PSTOA and use the other sides TOA to calculate RTT.

## Slide 3: ISTA reporting PSTOA
Assume the ISTA wants to calculate RTT using only its measured PSTOA tp4.
Since, assuming the channel between the ISTA and the RSTA is reciprocal, we have:
t4 = tp4 – (tp2-t2),
and can thus write
RTT = t4 – t1 – (t3 – t2) = tp4 – (tp2-t2) – t1 – (t3 – t2) =
tp4 – t1 – ( t3 – (t2 – (tp2 – t2)) ) = tp4 – t1 – (t3 – t2_adj),
where
t2_adj = t2 – (tp2 – t2)
Thus, in order to enable the ISTA to be able to report RTT using only its PSTOA tp4, we propose that the RSTA instead of feeding back its measured TOA, feed back t2_adj.
Now, if the ISTA wants to calculate RTT using its measured TOA, it can still do this as we have, due to the channel reciprocity:
t2 = t2_adj + (tp2 – t2) = t2_adj + (tp4 – t4)
Since the ISTA in this case would have both tp4 and t4, it can adjust t2_adj back to t2 with the above calculation.
Case where the ISTA measures and reports PSTOA tp4:
RSTA
ISTA
t2
t1
tp4
t3
R2I NDP
I2R NDP
t2 or t2_adj, t3
R2I LMR
I2R LMR
t1, tp4

## Slide 4: RSTA is reporting PSTOA
Assume I2R LMR has been negotiated and assume the RSTA wants to calculate RTT using only its measured PSTOA tp2.
Since, assuming the channel between the ISTA and the RSTA is reciprocal, we have:
t2 = tp2 – (tp4-t4),
and can thus write
RTT = t4 – t1 – (t3 – t2) = t4 – t1 – (t3 – (tp2 – (tp4 – t4))) =
t4 - (tp4-t4) – t1 – ( t3 – tp2 ) = t4_adj – t1 – (t3 – t2),
where
t4_adj = t4 – (tp4 – t4)
Thus, in order to enable the RSTA to be able to report RTT using only its PSTOA tp4, we propose that the ISTA instead of feeding back its measured TOA, feed back t4_adj.
Now, if the RSTA wants to calculate RTT using its measured TOA, it can still do this as we have, due to the channel reciprocity:
t4 = t4_adj + (tp4 – t4) = t4_adj + (tp2 – t2)
Since the RSTA in this case would have both tp2 and t2, it can adjust t4_adj back to t4 with the above calculation.
Case where the RSTA measures and reports PSTOA tp2:
RSTA
ISTA
tp2
t1
t4
t3
R2I NDP
I2R NDP
tp2, t3
R2I LMR
I2R LMR
t1, t4 or t4_adj

## Slide 5
Thank You!