## Slide 1: Summary of ARC SC discussion on 11-20/1166r4
Date: 2020-11-05
Authors:

## Slide 2: Abstract
This submission provides a summary of the discussion held in the ARC SC Teleconference, 2020-11-4 @ 11:15-13:15 h ET, on 11-20/1166r4 “NGV 11bd Architecture Discussion”.

## Slide 3: Summary
11-20/1166r4 “NGV 11bd Architecture Discussion” was presented at the ARC SC Teleconference by Joseph Levy
11-20/1166r4 states: There are no planned changes to OCB concepts or behavior
  There was general agreement that this implies no architecture changes to 802.11 are needed.
  No further work need be done regarding the overall architecture.
The “clean up” of the MAC service to better support ITS an IEEE 1609 and other higher layer specifications did generate discussion and questions.
  The use of MA-UNITDATA for transferring the Radio Environment information was questioned
  Restrictions on the use of this facility to ITS or OCB only should be considered, note OCB is use is not restricted to ITS.
  The expiry time and number of repetitions elements were discussed
  Questions and comments for TGbd were generated (see next slide)

## Slide 4: Questions and Comments from the ARC SC to TGbd
Why is Radio Environment done via MA-UNITDATA, and not a management interface? Is it intended to be “affiliated” with a particular MSDU, per MSDU?
Is the MA-UNITDATA.indication meant to be on the peer device, providing the channel/radio information for a received MSDU? Or is this a ‘local’ response to the request to set the channel/radio information on the transmitter?
How is the reception of frames expected to work, between the transmissions controlled by MA-UNITDATA.requests?
It should be made clear that this new Radio Environment control is only for OCB operation.
We probably need the channel control items (frequency band, primary channel, and maybe channel width) to be a separate interface.

## Slide 5: References