## Slide 1: Partial BW Info Field Design in NDPA
Date: 2020-11-09
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Following figure shows an example of the agreed STA Info field in NDPA [1]
242 RU and 996 RU based partial BW feedback has been agreed [2]
In this contribution, we compare several options for Partial BW Info field design
  Option 1: Bitmap based design [3]
  Option 2: New bitmap based design
  Option 3: Table based design

## Slide 3: Option 1 – Bitmap based Design [3]
In [3], bitmap based design using 9 bits was proposed
  B0 indicates bitmap resolution (20/40MHz)
  B1~B8 indicate feedback request for each 20/40MHz channel
   It seems simple and intuitive
  In 320MHz transmission, the bitmap resolution needs to be set to 40MHz
  It may be impossible to request for feedback on the channels corresponding to 242 RU or (484+242) MRU in 320MHz (Use case: 242 RU for 20MHz operating STA, (484+242) MRU for 80MHz operating STA and 3x996 RU for 320MHz operating STA in 320MHz DL OFDMA)
  Also, it may preclude some of the MRU designs, e.g., 3x996+(484+242) or 2x996+(484+242) MRU (one 20MHz hole in 320/240MHz)
B0 B1 B8

## Slide 4: Option 2 – New Bitmap based Design (1/7)
New bitmap based design using 9 bits is proposed here
  B0: Select one 80MHz channel
    Different channel is selected according to the number of “0s” in B1 ~ B4
  B1~B4: Feedback request for each 80MHz
    Basically, “1” and “0” mean whole feedback and no feedback request in each 80MHz, respectively
    Feedback type for 80MHz selected by B0 is determined by B5~B8
  B5~B8: Feedback request for each 20MHz in a certain 80MHz selected by B0
    1: feedback request
    0: no feedback

## Slide 5: Option 2 – New Bitmap based Design (2/7)
If the number of “0s” in B1~B4 = 0, i.e., [B1 B2 B3 B4] = [1 1 1 1]
  B0, B5~B8: reserved
  B1~B4: [1 1 1 1]
    1: whole 80MHz feedback request, i.e., feedback request for whole 320MHz bandwidth
If the number of “0s” in B1~B4 = 1, e.g., [B1 B2 B3 B4] = [1 1 0 1]
  B0: reserved
  B1~B4
    1: whole 80MHz feedback request
    0: partial 80MHz feedback request determined by B5~B8
  B5~B8: Feedback request for each 20MHz in 80MHz with “0”
  E.g., 0 1101 1100
  Cover 4x996, 3x996+484, 3x996 MRUs and 3x996+(484+242), 3x996+242 MRUs as well

## Slide 6: Option 2 – New Bitmap based Design (3/7)
If the number of “0s” in B1~B4 = 2, e.g., [B1 B2 B3 B4] = [1 0 0 1]
  B0
    1: select higher 80MHz between two 80MHz channels with “0”
    0: select lower 80MHz between two 80MHz channels with “0”
  B1~B4
    1: whole 80MHz feedback request
    0: no 80MHz feedback request for 80MHz not selected by B0
    0: partial 80MHz feedback request determined by B5~B8 for 80MHz selected by B0
  B5~B8: Feedback request for each 20MHz channel for 80MHz selected by B0
  E.g., 1 1001 0011
  Cover 3x996, 2x996+484, 2x996 MRUs and 2x996+(484+242), 2x996+242 MRUs as well

## Slide 7: Option 2 – New Bitmap based Design (4/7)
If the number of “0s” in B1~B4 = 3, e.g., [B1 B2 B3 B4] = [0 0 0 1]
  B0
    1: select 80MHz with “1”
    0: select the other 80MHz in 160MHz which includes 80MHz with “1”
  B1~B4
    If B0 = 1
      1: partial 80MHz feedback request determined by B5~B8
      0: no 80MHz feedback request
      Cover 996, (484+242), 484, 242 RUs/MRUs
    If B0 = 0
      1: whole 80MHz feedback request
      0: no 80MHz feedback request for 80MHz not selected by B0
      0: partial 80MHz feedback request determined by B5~B8 for 80MHz selected by B0
      Cover 2x996, 996+(484+242), 996+484, 996 RUs/MRUs and 996+242 MRU as well
  B5~B8: Feedback request for each 20MHz channel for 80MHz selected by B0
  E.g., 1 0001 0111
  E.g., 0 0001 0111

## Slide 8: Option 2 – New Bitmap based Design (5/7)
It is possible to request feedback for all kinds of partial channels corresponding to RUs/MRUs (≥ 242 RU) defined in 11be
It may be helpful if we further consider MRUs such as 3x996+(484+242) / 2x996+(484+242) in R2
  Use case 1: 242 RU for 20MHz operating STA and 3x996+(484+242) for 320MHz operating STA in 320MHz DL OFDMA
  Use case 2: 242 RU for 20MHz operating STA, 996RU for 80MHz operating STA and 2x996+(484+242) for 320MHz operating STA in 320MHz DL OFDMA
However, it may be impossible to request feedback which consists of multiple 242 RU holes across 80MHz channels, e.g., 484+484 / (484+242) + (484+242) / 2x996+484+484 / 2x996+(484+242)+(484+242)
  If we limit the MRU design with 242 RU holes within only one 80MHz channel in R2, option 2 may be worth considering

## Slide 9: Option 2 – New Bitmap based Design (6/7)
In order to enable some multiple holes across 80MHz channels, we redefine the case with the number of “0s” in B1~B4 = 2 as follows
  B0
    1: select 80MHz with “1”
    0: select 80MHz with “0”
  B1~B4
    If B0 = 1
      1: partial 80MHz feedback request determined by B5~B8
      0: no 80MHz feedback request
      Cover 2x996, 996+484, 996, 484 RUs/MRUs and 484+484 MRU as well
    If B0 = 0
      1: whole 80MHz feedback request
      0: partial 80MHz feedback request determined by B5~B8
      Cover 4x996, 3x996+484, 3x996, 2x996+484, 2x996 RUs/MRUs and 2x996+484+484 MRU
  B5~B8: Feedback request for each 40MHz channel for two 80MHz channels selected by B0
  E.g., 0 1010 1000
  E.g., 1 1100 1001

## Slide 10: Option 2 – New Bitmap based Design (7/7)
It is possible to request feedback for all kinds of partial channels corresponding to RUs/MRUs (≥ 242 RU) defined in 11be
It may be helpful if we further consider MRUs such as 3x996+(484+242) / multiple 484 RU holes across two 80MHz channels in R2
It may be still impossible to request feedback which consists of multiple 242 RU holes across 80MHz channels, e.g., (484+242)+(484+242) / 2x996+(484+242)+(484+242) MRU
  We can simply use 484+484 and 2x996+484+484 instead
There are many overlapped RUs/MRUs when the number of “0s” in B1~B4 = 2, and thus, we may consider specially designing this case similar to the table based design for the future extension

## Slide 11: Option 3 – Table based Design
We can just reuse an RU allocation table that will be defined in the trigger frame
  9 bits may be used and entries for RUs/MRUs < 242 can be reserved
We can define a new table
  Using 7 bits may be enough to cover RUs/MRUs ≥ 242 defined in R1 with more than 30 entries reserved as shown in [4]
  For extension in R2, one more bit can be added (about 160 entries reserved)
It may require a smaller number of bits than other options and may cover any kinds of MRUs
It may need memory and a bit complicated decoding

## Slide 12: Summary
Comparison
  Option 1 seems not applicable even in R1
  Option 2 may be desirable if we limit the MRU design in R2
  Option 3 seems not to preclude any possibilities on MRU design in R2 if more bits are added for extension
  We slightly prefer option 2 or option 3 to option 1
 | Option 1 Bitmap | Option 2 New Bitmap | Option 3 Table
Pros | Simple and intuitive | Possible for all RUs/MRUs in R1 Possible for 242 RU based feedback | No restriction in R2 Fewer bits
Cons | Impossible for some of the MRUs in R1 Some restrictions in R2 | A bit complex due to a coupled property Some restrictions in R2 | Need memory Complicated decoding

## Slide 13: Straw poll #1
Do you agree to add the following text for the TGbe SFD?
  In the Partial BW Info field of NDPA, 11be shall be able to request feedback of the channel corresponding to each RU/MRU larger than or equal to 242 RU defined in the TGbe spec

## Slide 14: Straw poll #2
Do you agree to add the following text for the TGbe SFD?
  Option 2 shown in slide 4~7 is used for the design of the partial BW info field in NDPA

## Slide 15: Straw poll #3
Do you agree to add the following text for the TGbe SFD?
  Option 2 shown in slide 4, 5, 7 and 9 is used for the design of the partial BW info field in NDPA

## Slide 16: Straw poll #4
Do you agree to add the following text for the TGbe SFD?
  Table based design using 7~9 bits is used for the design of the partial BW info field in NDPA
    Specific design is TBD

## Slide 17: Straw poll #5
Do you agree to add the following text for the TGbe SFD?
  Table based design using 8 bits is used for the design of the partial BW info field in NDPA
    Specific design is TBD

## Slide 18: References
[1] 802-11-20/1436r6 NDPA and MIMO Control Field Design for EHT
[2] 802-11-20/1161r1 EHT Punctured NDP and Partial BW Feedback Tones
[3] 802-11-20/1747r0 EHT NDPA Partial BW Info Design
[4] 802-11-20/828r6 RU Allocation Subfield Design for EHT Trigger Frame