## Slide 1: Reserved Bit Behaviour for EHT
Date: 2020-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In these slides, we propose receiver behavior for R1 devices
  Reserved bits in the preamble
  Reserved states of certain fields
Impact of R2 has been kept in mind while designing the above
We also propose a way to support OFDMA transmissions to R2 devices using new RUs/M-RUs that may get defined in R2 while also serving R1 devices in the same transmission

## Slide 3: Reserved bits in U-SIG/EHT-SIG
8 Reserved bits in U-SIG
  1 below punctured channel indication
  1 below ‘PPDU type and compression mode’
  6 more; May instead be used for additional TxOP/BSS Color bits
4 reserved bits in U-SIG overflow part of EHT-SIG-common
Total of 12 reserved bits
  Assuming, no additional bits for BSS Color/TxOP
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 4
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17

## Slide 4: Background: Reserved bits
In general, 2 kinds of Rx behavior for R1 devices are possible when confronted with a reserved bit/state
  Don’t care or Ignore
  Check the value of the bit, and if not set to specified reserved state as prescribed in the R1 spec, Terminate reception
    Still respect the L-SIG and U-SIG’s version independent contents if U-SIG CRC passes
In the subsequent slides, we classify the different reserved bits/states into the two categories

## Slide 5: Thoughts about Reserved condition in EHT-SIG user-field
Since the information is targeted to the intended recipient only in the user field, after an AID match, any reserved condition (the reserved bit being set differently, or a reserved state of a field) should be met with an Terminate response at the recipient
  Should not happen often as AP should not send something to a STA that it does not understand or does not support
Conclusion: Incorrectly set reserved bits or states in user-field should be categorized as a Terminate Rx event, if AID matches
  If AID does not match, all the reserved bits or states in the user-field should be categorized “don’t care”

## Slide 6: Proposed behavior for different Reserved Bits in U-SIG and EHT-SIG
Reserved bit tied to | Proposed behavior when set incorrectly
Punctured channel indication | Since it implies a puncturing mode which is not supported by R1 device, Terminate
PPDU type and compression mode | This bit will also imply a PPDU type not supported by R1 devices, Terminate
6 reserved bits at the boundary of version independent and version dependent fields (or less if some end up being used for BSS Color/TxOP) | Most of the bits (5) as Don’t care: Maybe be used to convey something to R2 devices while keeping R1 devices in the same transmission 1 bit as Terminate: Future features that R1 devices will not understand can use this bit
4 reserved bits in EHT-SIG common | Make bits as Don’t care: Maybe be used to convey something to R2 devices while keeping R1 devices in the same transmission
1 reserved bit in the user field | If the AID matches, and bit set incorrectly, Terminate. If AID doesn’t match, all reserved bit in that user field are Don’t care

## Slide 7: Un-used states of certain fields in R1
Need to classify Rx behavior when the value of a field is set to a state which is un-used in R1, into two categories just like reserved bits
Recommend the following for the fields which have un-used entries for R1
  Terminate
    PPDU BW
    Punctured Channel Indication
    PPDU Type and Compression Mode
    Number of EHT-LTF symbols
    Spatial Configuration
    Nsts
  Don’t care
    Spatial re-use
    RU allocation
If the AID matches, and reserved state is present, Terminate
but don’t care if AID doesn’t match
More on this later, as R1 device will need to parse this and extract some information

## Slide 8: RU Allocation Sub-field
An R1 device cannot make sense of a bit field value of this sub-field that is not defined in R1
We want to be able to transmit a new M-RU/RU to an R2 device while keeping a R1 device in the same transmission
  Next few slides goes over an approach to achieve this

## Slide 9: Issue with new RU/M-RU entries
Recall that information about the number of users is embedded in the RU allocation field value
When we send a new RU allocation field value (defined in R2) in EHT-SIG that an R1 device does not understand
  R1 device can’t figure out the number of EHT-SIG user fields that are tied to it
Need a way to convey to the R1 STAs, at-least the number of users tied to an RU allocation field (even for values defined in R2)
  Enables R1 devices to skip that many user fields corresponding to the new RU allocation field value

## Slide 10: Details of the approach to solve RU allocation field issue
New entries in the M-RU for R2 will be defined such that “Field value modulo some number” tells the number of users
  E.g., “Field value modulo 8 +1” tells the number of users
    Value 400 means Num users =1, Value 401 means Num users =2... and so on up-to 8 users.
    This is equivalent to looking at the LSB bits of the 9-bit RU allocation field, where 000-111 indicate 1-8 users, respectively
  Just by looking at the RU allocation field value, the R1 devices understand the number of users for new entries introduced in R2 as well
Could accommodate up to floor((512-294)/8)=27 new large M-RUs that supports MU-MIMO

## Slide 11: Proposed Nomenclature and Allocation
Validate
  Reserved bits with Terminate as Rx behavior
Disregard
  Reserved bits with Don’t Care or Ignore as Rx behavior
Validate bit below Punctured channel indication
  Add “Maybe be used for an expanded set of puncturing patterns in R2” to description
Validate bit below PPDU type and compression mode
  Add “Maybe used for an expanded set of PPDU types or compressed modes in R2” to description
In addition to bits shown here, the reserved bit in user field is Validate
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Disregard | 5
 |  | Validate | 1
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Validate | 1
 |  | PPDU type & Compression Mode | 2
 |  | Validate | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Disregard | 4
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17

## Slide 12: Summary
Proposed Rx behavior for R1 devices when confronted with a reserved state in EHT preamble
Classified the reserved bits and states into two categories
  Reserved bits/states with Don’t Care or Ignore as Rx behavior
  Reserved bits/states with Teriminate as Rx behavior
Proposed a method to transmit new RUs/M-RUs (defined in R2) to R2 devices while keeping R1 devices in the same transmission
Proposed terminology for the reserved bits in the preamble and some descriptions for the same
  Disregard bits
  Validate bits

## Slide 13: SP1
Do you agree that we need two different kinds of reserved bits in the EHT preamble?
  Validate
    Reserved bits with Terminate as Rx behavior for an R1 device
  Disregard
    Reserved bits with Don’t Care or Ignore as Rx behavior for an R1 device

## Slide 14: SP2
Do you agree to have the following 3 validate bits in the U-SIG
  1 below Punctured channel indication field
  1 below the PPDU type and compression mode field
  1 more to tell R1 devices to terminate processing in certain R2 transmissions (which still use an R1 PPDU type and R1 puncturing pattern)

## Slide 15: SP3
Do you agree that we need to support OFDMA transmissions that send new M-RUs/RUs (that use reserved entries in R1 RU allocation table) to R2 devices while serving R1 devices in the same transmission?

## Slide 16: SP4
Do you agree to have the following rule about any new potential entries of RU allocation table in R2
  Values greater than 303
    For any states of the RU allocation sub-field that are defined as reserved in R1, R1 device can assume that “Field value modulo 8 +1” tells the number of R2 users
  When reserved values < 303 are used, R1 devices will terminate reception

## Slide 17: SP4a
Do you agree to have a rule in the R1 spec which allows an R1 device to extract the number of users associated with any R1 reserved state of the RU allocation sub-field?