## Slide 1: Duplication in time domain for LPI
Date: 2020-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin | Huawei Technologies |  |  | yan.xin@huawei.com
Junghoon Suh |  |  |  | junghoon.suh@huawei.com
 |  |  |  | osama.aboulmagd@huawei.com
Osama Aboul-Magd |  |  |  | 
 |  |  |  | shimi.shilo@huawei.com
Shimi Shilo |  |  |  | 

## Slide 2: Introduction
FCC [1] ruling allows low-power indoor (LPI) unlicensed devices to use the entire 6 GHz band by lowering the PSD of the transmit power and limiting indoor applications. Link budget, spectrum usage efficiency and implementation should be considered for LPI.
To compensate the loss in link budget for range extension in LPI operations, DUP mode is proposed [2], in which data coded/modulated by MCS0+DCM is duplicated in frequency domain. This DUP mode is proposed to support BWs of 80, 160 and 320 MHz without preamble puncturing.
This contribution proposes to duplicate an OFDM symbol in time domain (DUP mode in time domain) for LPI operations to meet requirements on link budget improvement and simple implementation for support of BWs of 20, 40, 80, 160 and 320 MHz and preamble puncturing as defined in 11be SFD [3].

## Slide 3: Revisit - DUP mode in frequency domain (DUP-F)
To extend the transmission range, a DUP mode [2], [4] is proposed for data payload transmission in LPI, in which DCM modulated signals are duplicated with consideration of PAPR reduction [3], [5] in frequency domain by employing an increased bandwidth.
Note
si: pre-DCM modulated freq.-domain signal
in OFDM symbol i in DUP in freq. domain;
si_DCM: signal obtained by applying DCM on si
Note
si: pre-DCM modulated freq.-domain signal
in OFDM symbol i; si = [siL, siU];
- siL and siU are lower and upper half of si respectively;
siL_DCM: signal obtained by applying DCM on siL;
siU_DCM: signal obtained by applying DCM on siU.

## Slide 4: Proposal - DUP mode in time domain (DUP-T)
A DUP mode in time domain: duplication of an OFDM symbol
Note
s: pre-DCM modulated freq.-domain signal in an OFDM symbol; given a BW, s = [s1 s2] where signals s1 and s2 are as specified in general for DUP mode in freq. domain (except for the case of BW=80 MHz)
s_DCM: signal obtained by applying DCM to s as in 11ax
Linear phase rotations applied to the time-domain samples, which result in cyclic shifts of subcarriers, may provide further diversity in frequency domain

## Slide 5: Data rates of frequency- and time-domain DUP modes
BW (MHz) | Data rates of DUP in time domain (Mbps) | Data rates of DUP in freq. domain (Mbps) | MCS0+DCM in 11ax (Mbps) 0.8uS GI, NSS=1 | N_SD in 11ax (NSS=1)
20 | 2.15 | - | 4.3 | 117
40 | 4.3 | (4.3) | 8.6 | 234
80 | 9.0 | 8.6 | 18.0 | 490
160 | 18.0 | 18.0 | 36.0 | 980
320 | 36.0 | 36.0 |  | 

## Slide 6: Comparison of frequency- and time-domain DUP modes
 | DUP in time domain | DUP in freq. domain
Supported BWs (MHz) | 20, 40, 80, 160 and 320 | 80, 160 and 320
Support of preamble puncturing | Support preamble puncturing with DCM * | Do not support preamble puncturing
Duplication gains | Data tones and pilot tones in frequency/time domain | Data tones in freq. domain
Waveforms | Same time-domain DCM signals as in 11ax. | Duplicated DCM signals in freq. domain with further phase optimization for PAPR reduction
IFFT/FFT operation | Once per each pair of OFDM symbols | Once per each OFDM symbol
Data rates | 9 Mbps for DUP BW 80 MHz MCS0+DCM for all BWs Same as DUP-F for BW 160/320 MHz | 8.6 Mbps for DUP BW 80 MHz No applicable for transmission in BW 20 MHz without a new MCS
Implementation | Simple DCM modulation in freq. domain, the same as in 11ax - Unified format in freq. domain for BWs 20, 40 , 80, 160 and 320 MHz | Require to further apply phase shifting to DCM modulated signals for PAPR reduction in freq. domain Different formats in freq. domain for BW 80/160 MHz and 320 MHz
* Simple duplication. No linear phase rotation applied to time-domain samples of the even OFDM symbol.

## Slide 7: Frequency/time-domain diversity of DUP-T
Assume that data tones in frequency domain s=[s1 s2] in DUP-T
Assume that no linear phase rotations are applied to the time-domain samples in even OFDM symbol
The following example shows data tone allocation in DUP-T for BW 160 MHz
DUP-T
DUP-F

## Slide 8: Summary
We propose DUP mode in time domain that supports all defined BWs 20, 40 , 80, 160 and 320 MHz and preamble puncturing in SFD
DUP-T benefits implementation with one single unified format for all BWs, few IFFT/FFT operations, 11ax-compliance DCM signals (no further segmentation and phase optimization needed for PAPR reduction)
DUP-T provides a higher data rate compared to DUP-F for BW 80 MHz

## Slide 9: Reference
[1] FCC 20-51, REPORT AND ORDER AND FURTHER NOTICE OF PROPOSED RULEMAKING, April 24, 2020.
[2] Ron Porat, IEEE 802.11-20/965r4, 6 GHz LPI Range Extension.
[3] IEEE 802.11-19/1262r18, Specification framework for TGbe.
[4] Jianhan Liu, et al, IEEE 802.11-20/986r1, DCM for range extension in 6GHz LPI.
[5] Ron Porat, et al, IEEE 802.11-20/1191r1, DUP mode PAPR reduction.

## Slide 10: SP
Do you agree to add the DUP mode in time domain as described in slide 4 of 11-20/1842r0 with MCS0+DCM and Nss=1 to the 11be SFD?
This is for an R1 feature.