## Slide 1: Discussion on low latency traffic
Date: 2020-11-2
Authors:
Name | Affiliations | Address | Email
Boyce Bo Yang | Huawei | Nanjing, China | yangbo59@huawei.com
Chenhe Ji |  | Nanjing, China | jichenhe@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Wayne Wei Qiu |  | Nanjing, China | wayne.qiuwei@huawei.com
Notes: September 2012

## Slide 2: Introduction
The group has agreed to define a mechanism that differentiates low latency traffic from regular traffic and prioritizes transmission of low latency traffic in R1 [Motion 135, #SP225]
Many contributions are trying to provided prioritized transmission by allocating restricted access periods where low latency traffic has higher priority to transmit [1][2][3].
There are some concerns that prioritized transmission of low latency traffic may largely degrade the performance of regular traffics

## Slide 3: Tradeoff between QoS and efficiency
Good of performance of low latency traffics would improve experience of WLAN users. On the other hand, bad performance of regular traffics would degrade experience.
  Mandatory: Regular traffic should stop contending channels when AP announces prioritized transmission for low latency traffic.
  Optional: Regular traffic may stop contending channels when AP announces prioritized transmission for low latency traffic
 | Mandatory | Optional
Low latency traffic | Good performance, almost no interference | Unpredictable performance, More interference
Regular traffic | Very low efficiency if low latency traffic has huge amount of data. | Efficiency would not be degraded greatly
Observation: we need to find a balance between regular traffic and low latency traffics to provide the best overall experience.

## Slide 4: Factors affecting efficiency of regular traffic
Duration of quiet time
  Effect: Regular STAs are not allowed to contend channel during protected access period
  Goal: Shorter duration
Boundary effect
  Effect: Transmission of regular traffics would be interrupted by start boundary of protected access period.
  Goal: Reduce number of boundaries

## Slide 5: Discussion on low latency traffic
Recall the low latency traffics defined in RTA report[4], 7 use cases with different traffic models are discussed.
These low latency traffics can be further classified into two types:
  Type 1: traffic with low data rate(e.g. <1Mbps)
    Typical use case: online game, AGV control, Human safety
    Discussion: transmission of type 1 traffic only consumes very small fraction of resources, and the effect on other traffics is small. Congestion is usually caused by regular traffics.
  Type 2: traffic with high data rate(e.g. >100Mbps)
    Typical use case: VR
    Discussion: transmission of type 2 traffic may need large fraction of resources, and may have big effect on other traffics. Congestion may caused by low latency traffic.
It would be a good trade-off between latency and efficiency if 11be defines different strategies for different types of low latency traffic

## Slide 6: Reducing number of boundaries
To obtain overall requirements of low latency traffics, an EHT AP may need to negotiate with each STA and set up reserved resources for each low latency STA. However, the number of boundaries would increase accordingly.
If AP set up one reserved resource for one traffic type, all STAs with the traffic share reserved resources and the number of boundaries would be irrelevant to the number of non-AP STAs
Further restrictions can be put on intervals between two consecutive reserved resources. For example, no less than 10ms

## Slide 7: Summary
We give a discussion on low latency traffics in 11be.
  We classify low latency traffics into 2 types based on data rate.
  For a good trade-off between low latency traffic and regular traffic, we suggest defining different rules for different types of low latency traffics

## Slide 8: Straw Poll 1
Do you agree that 11be classifies low latency traffic into more than one types and defines different rules for different types low latency traffic.
Note:
  This SP does not intend to put anything into 11be Draft
Y/N/A

## Slide 9: Straw Poll 2
Do you agree that 11be classifies low latency traffic into the following two types.
  Type 1: low latency traffic with low data rate
  Type 2: low latency traffic with high data rate
Note:
  The exact definitions of low data rate and high data rate are TBD
Y/N/A

## Slide 10: Straw Poll 3
Do you agree that 11be mandatory support prioritized transmission of low latency traffic type 1.
Y/N/A

## Slide 11: References
[1] 11-20-1355-05-00be-access-mechanisms-to-meet-the-requirements-of-low-latency-traffics
[2] 11-20-1046-08-00be-prioritized-edca-channel-access-slot-management
[3] 11-20-1350-00-00be-enhancements-for-qos-and-low-latency-in-802-11be-r1
[4] 11-18-2009-06-0rta-rta-report-draft

## Slide 12: Backup

## Slide 13: Multiple quiet intervals can be scheduled

## Slide 14: Defining different rules for different Traffic identifiers
A example design of resource reservation element is given in doc 1335/r5 as shown below. Different rules can be defined for different traffic identifiers.
Value | Description | Rules
0 | DFS Channel sensing | EHT non-AP STAs shall stop contending channel on reserved resources
1 | Low latency traffic type 1 (game and control) | EHT non-AP STAs should stop contending channel on reserved resources except for those with type 1 low latency traffic
2 | Low latency traffic type 2 (VR) | EHT non-AP STAs may stop contending channel on reserved resources except for those with type 2 low latency traffic
3~255 | To be defined | 
RR
Offset
RR
Interval
RR
Duration
RR
Period
RR Mode
(Traffic identifier)
RR
Count
TBD
Field(s)