## Slide 1: Discussion on low latency traffic
Date: 2020-11-2
Authors:
Name | Affiliations | Address | Email
Boyce Bo Yang | Huawei | Nanjing, China | yangbo59@huawei.com
Chenhe Ji |  | Nanjing, China | jichenhe@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Wayne Wei Qiu |  | Nanjing, China | wayne.qiuwei@huawei.com
Notes: September 2012

## Slide 2: Introduction
The group has agreed to define a mechanism that differentiates low latency traffic from regular traffic and prioritizes transmission of low latency traffic in R1 [Motion 135, #SP225]
Many contributions are trying to provided prioritized transmission by allocating restricted access periods where low latency traffic has higher priority to transmit [1][2][3].
There are some concerns that prioritized transmission of low latency traffic may largely degrade the performance of regular traffics

## Slide 3: Tradeoff between QoS and efficiency
Good of performance of low latency traffics would improve experience of WLAN users. On the other hand, bad performance of regular traffics would degrade experience.
  Option 1: Regular traffic should stop contending channels during reserved periods announce by AP for prioritized transmission of low latency traffic.
  Option 2: Regular traffic may stop contending channels during reserved periods announce by AP for prioritized transmission of low latency traffic
 | Option 1 | Option 2
Low latency traffic | Good performance, almost no interference from regular traffics | Unpredictable performance, More interference
Regular traffic | Very low efficiency if low latency traffic has huge amount of data. | Efficiency would not be degraded greatly
Observation: we need to find a balance between regular traffic and low latency traffics to provide the best overall experience.
Notes: That is to provide QoS to low latency traffics while minimizing the influence on regular traffics

## Slide 4: Factors affecting efficiency of regular traffic
Duration of quiet time
  Effect: Regular STAs are not allowed to contend channel during protected access period
  Goal: Shorter duration
Boundary effect
  Effect: Transmission of regular traffics would be interrupted by start boundary of protected access period.
  Goal: Reduce number of boundaries

## Slide 5: Discussion on low latency traffic
Recall the low latency traffics defined in RTA report[4], 7 use cases with different traffic models are discussed. These low latency traffics can be further classified into two types:
  Type 1: traffic with low data rate(e.g. <1Mbps, similar to voice)
    Typical use case: online game, AGV control, Human safety
    Discussion:
      Transmission of type 1 traffic only consumes very small fraction of resources, and the effect on other traffics is small.
      Congestion is usually caused by regular traffics, so delay performance would not be improved if regular traffic doesn’t give way to type 1 traffic.
  Type 2: traffic with high data rate(e.g. >100Mbps)
    Typical use case: VR
    Discussion:
      Transmission of type 2 traffic may need large fraction of resources, and may have big effect on other traffics.
      Congestion is very likely caused by type 2 traffic itself, so delay performance would be improved when collisions among STAs with type 2 traffic are well managed.
Notes: Game is widely supported by most of WLAN devices(phones, pads, laptops), user experience would be improved greatly if game performance is improved
the data rate is very low. So congestion must be caused by other traffics.
VR has huge amount of data, so congestion may be caused by VR traffic itself. If VR traffics can be well managed, link congestion would be alleviated.
VR is not as popular as game, which needs a specific device(VR helmet)

## Slide 6: Discussion on low latency traffic(2)
It would be a good trade-off between latency and efficiency if 11be defines different strategies for different types of low latency traffic.
Four possible strategies are discussed here:
  Strategy 1: EHT STAs mandatorily support low latency feature without further classification
  Strategy 2: EHT STAs mandatorily support low latency feature for Type 1 traffic and optionally for Type 2 traffic
  Strategy 3: EHT STAs optionally support low latency feature for both Type 1 and Type 2. The support for Type 1 traffic and Type 2 traffic are announced separately (e.g. using different capability fields)
  Strategy 4: EHT STAs optionally support low latency feature without further classification
    Note that: For Strategy 2 and 3, EHT AP should indicate explicitly that a reserved period is for Type 1 or Type 2 traffic when setting it up.
    STAs supporting this feature shall stop contending channel during reserved periods.
    STAs not supporting this feature may or may not stop contending channel during reserved periods.

## Slide 7: Reducing number of boundaries
To obtain overall requirements of low latency traffics, an EHT AP may need to negotiate with each STA and set up reserved resources for each low latency STA. However, the number of boundaries would increase accordingly.
If AP set up one reserved resource for one traffic type, all STAs with the traffic share reserved resources and the number of boundaries would be irrelevant to the number of non-AP STAs
Further restrictions can be put on intervals between two consecutive reserved resources. For example, no less than 10ms
Notes: If we define type 1 traffic to be mandatory, there would be only one boundary.
Regarding collisions on shared resources
The number of Low latency STAs would not be so much if we think about game signaling, which is the most popular low latency traffic.
Further scheduling algorithm can be adopted on reserved resource without introducing extra boundaries to regular traffic.
Intervals should be set to a value no less than 10ms

## Slide 8: Summary
We give a discussion on low latency traffics in 11be.
  We classify low latency traffics into 2 types based on data rate.
  For a good trade-off between low latency traffic and regular traffic, we suggest 11be defining different rules for different types of low latency traffics and give four possible strategies.

## Slide 9: Straw Poll 1
Do you agree that 11be classifies low latency traffic into more than one types and defines different rules for different types low latency traffic.
Note:
  This SP does not intend to put anything into 11be Draft
Y/N/A

## Slide 10: Straw Poll 2
Do you agree that 11be classifies low latency traffic into the following two types.
  Type 1: low latency traffic with low data rate
  Type 2: low latency traffic with high data rate
Note:
  The exact definitions of low data rate and high data rate are TBD
Y/N/A

## Slide 11: Straw Poll 3
Which option do you support in 11be:
  Option 1: EHT STAs mandatorily support low latency feature without further classification
  Option 2: EHT STAs mandatorily support low latency feature for Type 1 traffic and optionally for Type 2 traffic
  Option 3: EHT STAs optionally support low latency feature for both Type 1 and Type 2. The support for Type 1 traffic and Type 2 traffic are announced separately (e.g. using different capability fields)
  Option 4: EHT STAs optionally support low latency feature without further classification
  Option 5: None of above

## Slide 12: Straw Poll 4
Do you agree that 11be introduce a reserved period as follows:
  For STAs supporting this mechanism, specified traffics have higher priority to transmit on reserved resources
Y/N/A

## Slide 13: References
[1] 11-20-1355-05-00be-access-mechanisms-to-meet-the-requirements-of-low-latency-traffics
[2] 11-20-1046-08-00be-prioritized-edca-channel-access-slot-management
[3] 11-20-1350-00-00be-enhancements-for-qos-and-low-latency-in-802-11be-r1
[4] 11-18-2009-06-0rta-rta-report-draft