## Slide 1: Update on EHT Partial BW Feedback Tone Indices Table
Date: 2020-11-13
Authors:
Name | Affiliations | Address | Phone | Email
Alice Chen | Qualcomm |  |  | alicel@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Cheng-Ming Chen |  |  |  | chec@qti.qualcomm.com
Chi-Lin Su |  |  |  | clsu@qti.qualcomm.com
Notes: September 2012

## Slide 2: Abstract
In our 1161r1, we discuss the following and passed 4 related SPs
  Punctured NDP for sounding
  CSI feedback request granularity
  Feedback tone set
  Partial BW CSI feedback tone indices table
In this presentation, we would like to propose a change to the partial CSI feedback tone indices table of RU242 granularity
  Fix an error in the set of feedback tones of RU242-1 for 20MHz and make it consistent to the feedback tone set of 20MHz

## Slide 3: Recap: Feedback Tone Set of 20MHz in 1161r1 SP#2
20MHz: Reuse 11ax feedback tone sets for 11be
According to 11ax spec, the feedback tones for 20MHz are as following
  There is a conflict between the feedback tone set of 20MHz in SP#2 and the feedback tones of RU242-1 of 20MHz in SP#4

## Slide 4: Recap: Partial BW CSI Feedback with RU242 Granularity in 1161r1 SP#4
The following is the feedback tone indices table
  If the requested feedback range doesn’t cover entire 80MHz segment, use the following table
RU242 Index | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
1 | [-122:Ng:-4, 4:Ng:122] | [-244:Ng:-4] | [-500:Ng:-260] | [-1012:Ng:-772] | [-2036:Ng:-1796]
2 |  | [4:Ng:244] | [-252:Ng:-12] | [-764:Ng:-524] | [-1788:Ng:-1548]
3 |  |  | [12:Ng:252] | [-500:Ng:-260] | [-1524:Ng:-1284]
4 |  |  | [260:Ng:500] | [-252:Ng:-12] | [-1276:Ng:-1036]
5 |  |  |  | [12:Ng:252] | [-1012:Ng:-772]
6 |  |  |  | [260:Ng:500] | [-764:Ng:-524]
7 |  |  |  | [524:Ng:764] | [-500:Ng:-260]
8 |  |  |  | [772:Ng:1012] | [-252:Ng:-12]
9 |  |  |  |  | [12:Ng:252]
10 |  |  |  |  | [260:Ng:500]
11 |  |  |  |  | [524:Ng:764]
12 |  |  |  |  | [772:Ng:1012]
13 |  |  |  |  | [1036:Ng:1276]
14 |  |  |  |  | [1284:Ng:1524]
15 |  |  |  |  | [1548:Ng:1788]
16 |  |  |  |  | [1796:Ng:2036]

## Slide 5: Proposed Fix
Propose the following fix in the table
RU242 Index | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
1 | Ng=4: [-122, -120:4:-4, -2, 2, 4:4:120, 122]; Ng=16: [-122, -116:16:-4, -2, 2, 4:16:116, 122] | [-244:Ng:-4] | [-500:Ng:-260] | [-1012:Ng:-772] | [-2036:Ng:-1796]
2 |  | [4:Ng:244] | [-252:Ng:-12] | [-764:Ng:-524] | [-1788:Ng:-1548]
3 |  |  | [12:Ng:252] | [-500:Ng:-260] | [-1524:Ng:-1284]
4 |  |  | [260:Ng:500] | [-252:Ng:-12] | [-1276:Ng:-1036]
5 |  |  |  | [12:Ng:252] | [-1012:Ng:-772]
6 |  |  |  | [260:Ng:500] | [-764:Ng:-524]
7 |  |  |  | [524:Ng:764] | [-500:Ng:-260]
8 |  |  |  | [772:Ng:1012] | [-252:Ng:-12]
9 |  |  |  |  | [12:Ng:252]
10 |  |  |  |  | [260:Ng:500]
11 |  |  |  |  | [524:Ng:764]
12 |  |  |  |  | [772:Ng:1012]
13 |  |  |  |  | [1036:Ng:1276]
14 |  |  |  |  | [1284:Ng:1524]
15 |  |  |  |  | [1548:Ng:1788]
16 |  |  |  |  | [1796:Ng:2036]

## Slide 6: SP 1
Do you support the to fix the following in the feedback tone indices table with RU242 granularity for 11be?
Y/N/A
RU242 Index | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
1 | Ng=4: [-122, -120:4:-4, -2, 2, 4:4:120, 122]; Ng=16: [-122, -116:16:-4, -2, 2, 4:16:116, 122] | [-244:Ng:-4] | [-500:Ng:-260] | [-1012:Ng:-772] | [-2036:Ng:-1796]
2 |  | [4:Ng:244] | [-252:Ng:-12] | [-764:Ng:-524] | [-1788:Ng:-1548]
3 |  |  | [12:Ng:252] | [-500:Ng:-260] | [-1524:Ng:-1284]
4 |  |  | [260:Ng:500] | [-252:Ng:-12] | [-1276:Ng:-1036]
5 |  |  |  | [12:Ng:252] | [-1012:Ng:-772]
6 |  |  |  | [260:Ng:500] | [-764:Ng:-524]
7 |  |  |  | [524:Ng:764] | [-500:Ng:-260]
8 |  |  |  | [772:Ng:1012] | [-252:Ng:-12]
9 |  |  |  |  | [12:Ng:252]
10 |  |  |  |  | [260:Ng:500]
11 |  |  |  |  | [524:Ng:764]
12 |  |  |  |  | [772:Ng:1012]
13 |  |  |  |  | [1036:Ng:1276]
14 |  |  |  |  | [1284:Ng:1524]
15 |  |  |  |  | [1548:Ng:1788]
16 |  |  |  |  | [1796:Ng:2036]